## Slide 1
WF on spectrum utilization of single numerology case
ZTE, []
3GPP TSG-RAN WG4 NR AH#3 Meeting
Nagoya, Japan, 18 - 21 September, 2017
Agenda: 3.2.3.2
R4-1709989

## Slide 2: Background: Previous agreement for below 6GHz
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
Above RB values are agreed based on the assumption of symmetric guard band.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW . The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for sub 6GHz:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706971),EVM requirements (R4-1706969)
,SEM requirements (R4-1706973);
UE requirements: Power Class (PC3 and PC2), ALCR/ACS requirements (R4-1706525),EVM requirements (R4-1706612),SEM requirements; (R4-1706692)
Companies can further check above RB values based on further agreements for above requirements and agreements for channel raster.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform

## Slide 3: Background: Previous agreement for mmWave
Note 1: Above RB values are agreed based on the assumption of symmetric guard band. If asymmetric guard-band agreed, potential 1 RB reduced may be considered.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW. The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for mm Wave:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706954),SEM requirements (R4-1706964);
UE requirements: Power Class definition (R4-1706945), ALCR/ACS requirements (R4-1706063), SEM requirements (R4-1706073);
Companies can further check and bring analysis for above RB values based on further agreements for above requirements and agreements for channel raster, BS EVM and UE EVM requirements.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform
SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz
 | NRB | NRB | NRB | NRB
60 | 66 | 132 | 264 | N.A
120 | 32 | 66 | 132 | 264

## Slide 4: Background: the agreed minimum guard band (kHz) at each end of channel BW achievable for below 6GHz
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB | Min. GB
15 | 250 | 320 | 390 | 460 | 530 | 560 | 700 | N.A | N.A | N.A
30 | 520 | 680 | 660 | 820 | 800 | 920 | 1060 | 840 | 940 | 860
60 | N.A | 1040 | 1020 | 1360 | 1340 | 1640 | 1600 | 1560 | 1480 | 1400

## Slide 5: Background: the agreed minimum guard band (kHz) at each end of channel BW achievable for mmWave
SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz
 | Min. GB | Min. GB | Min. GB | Min. GB
60 | 1240 | 2480 | 4960 | N.A
120 | 1960 | 2480 | 4960 | 9920

## Slide 6: Background: Identified open issues
Which SCS in a channel BW will be the reference SCS for subcarrier and RB alignment to finalize the RB values?
  This is a RAN4 issue and do not need to ask RAN1.
  Option 1: determined minimum SCS in a channel BW.
    i.e. for sub6 GHz, CHBW <=50MHz, 15kHz, CHBW>50MHz, as 30kHz; mmWave as 60kHz
  Option 2: lowest SCS supported by the network
RAN1 agreements on subcarrier alignment and RB grid alignment among different SCSs in a channel BW is not clear. Here are the possible options understood by RAN4:
  Option 1: start from left channel edge
    Option 1A: Align PRB #0 across different SCSs.
    Option 1B: Do not put constraints on aligning PRB #0 across different SCSs.
  Option 2: start from channel center
    FFS if it implies any constraints on the number of RBs (e.g. even number only).

## Slide 7: Background: Identified open issues
3. The total number of RBs for the reference SCS per CBW for RB grid structure definition
  Option 1: The total number of RBs in a CBW is defined derived on agreed maximum spectrum utilization
  Option 2: The total number of RBs is equal to the mathematical maximum number of RBs for the given CBW.
  Option 3: Total number of RBs is selected as a multiple of 4 or 2 to ensure nested resource allocation for different numerologies.
  Other options are not precluded

## Slide 8: WF on spectrum utilization of single numerology case
Send an LS to RAN1 to inform RAN4 identified RB alignment options due to the confusion caused by the RAN1 agreement on subcarrier and RB alignment among different SCSs in a channel BW for single carrier single numerology case, and ask RAN1 to check whether any of the RAN4 identified RB alignment options violate RAN1 agreements.
Companies are encouraged to bring contributions to next RAN4 meeting with different RB alignment options to check which SCS and channel BW combinations’ RB values should be reduced and how much.