## Slide 1: 3GPP TSG-RAN WG4 Meeting NR-AH#3
Ericsson, Huawei, ZTE
WF on EMC radiated emission and RF spurious emission requirements for NR BS
R4-1710019

## Slide 2: Background
EMC radiated emission requirements for base stations and ancillary equipment were discussed in RAN4-#84. During the meeting some unclarities with respect to the regulatory requirements were identified.
[1] proposes a way forward on EMC radiated emission and RF spurious emission for NR base stations 1-C / 1-H and 1-O.
[2] proposes to not define EMC radiated emissions for Range 1-O and Range-2 NR BS in EMC specification TS 38.113.OTA spurious emissions will be captured in TS38.104 and TS 38.141. Ericsson in [1] coincides with ZTE proposal but covering NR 1-O.
In [1], Ericsson proposes that the EMC radiated emission for NR 1-C and NR 1-H shall be renamed Radiated spurious emission and be moved to TS 38.104 with a conformance test specified in TS 38.145-2. See table 3 in [1].
[3] shows that the linear sum of the EMC radiated emission limit and the RF spurious emission limits does not significantly impact the total OTA spurious emission limit. Therefore, Ericsson proposes to apply solely the RF spurious emission OTA TRP limits as the total OTA spurious emission limits for NR BS 1-O, i.e. do not specify the limit as a sum of RF spurious + EMC radiated emission as previously agreed in AAS TR.
[1-2] propose that the radiated emission core requirement should be removed and instead considered as included in the OTA RF spurious emission requirement.

## Slide 3: WF Agreement Plan
The arguments in favor of applying sole the RF spurious emission emission OTA TRP limits as the total OTA spurious emission limits for NR BS 1-O should be further analyzed.
The proposal on removing the EMC radiated emission from the core requirement to include it in the OTA RF spurious emission requirement in TS 38.104 should be further analysed.
Once agreed,the results of the discussion should be reflected in the TS before the deadline set for the definition of the EMC core requirements.

## Slide 4: WF Agreement
For NR BS 1-O and 2-O RF radiated spurious emission includes the EMC radiated emissions. In this case RF radiated spurious emissions and EMC radiated emissions cannot be distinguished in the OTA measurement setup.
Alternatives on how to handle this issue from the RAN4 specification perspective:
  Option 1: Remove the corresponding EMC radiated emission requirements from TS 38.113.
    Consider EMC radiated emission requirements as included in the OTA RF spurious emission requirements in TS 38.104.
    The requirements specification for OTA spurious emission need further study.
    Reflect this change in the new conformance requirement for OTA RF spurious emission to be specified in TS 38.141-2.
  Option 2: Other solutions not precluded.
requirements. shall be removed from TS 38.113 and instead considered as included in the OTA RF spurious emission requirements in TS 38.104 and reflected in the new conformance requirement for OTA RF spurious emission to be specified in TS 38.145-2.
tFor NR BS 1-O and 2, apply solely RSE OTA TRP limit as the total OTA TRP limit and removing EMC RE to OTA RSE in TS 38.104. How to define t
Apply solely the RF spurious emission OTA TRP limits as the total OTA spurious emission limits for NR BS 1-O and 2, i.e. do not specify the limit as a sum of RF spurious + EMC radiated emission as previously agreed in AAS TR.
For NR BS 1-C and 1-H, the EMC radiated emission shall be renamed Radiated spurious emission and be removed to TS 38.104 and the conformance test specified in TS 38.145-2.

## Slide 5: References
[1] R4-1709545- Discussion on EMC radiated emission and RF spurious emission requirements for NR BS. Ericsson
[2] R4-1709596 - Further consideration on EMC RE requirement for OTA BS in TS 38.113. ZTE
[3] R4-1709544 - Discussion on combined limit for EMC radiated emission and RF spurious emission for NR BS 1-R. Ericsson