## Slide 1: WF on BS ACLR for NR
NTT DOCOMO, INC.
R4-1710025
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3 Nagoya, Japan, 18 - 21 Sep, 2017
Agenda Item: 3.4.3.3

## Slide 2: Background
ACLR for FR1 and FR2 is discussed in [1-5].
This contribution summarizes way forward/agreement on this topic.
[1] R4-1709457 BS ACLR for NR NTT DOCOMO
[2] R4-1709738 BS ACLR requirements for sub-6GHz NEC
[3] R4-1709705 Proposals on below 6GHz NR BS ACLR Nokia
[4] R4-1709845 BS ACLR measurement BW for sub6GHz Ericsson
[5] R4-1709655 Further consideration on sub-6GHz NR BS ACLR requirement ZTE

## Slide 3: Agreements for FR2
ACLR definition, the same CBW with wanted signal can be assumed as a adjacent CBW. (already agreed in chairman)
Transmission BW configuration of wanted channel (it would differ depend on SCS and/or CBW) should be used as a measurement BW for wanted signal power measurement. (already agreed in chairman)
No ACLR2 requirement is needed since emission level at ACLR2 range will be close to noise floor. (already agreed in chairman)

## Slide 4: WF on MBW of adjacent channel
Example) 50MHz CBW for sub6GHz (the value of NRB is a just example)
SCS | NRB | X = BWconfig / BWchannel [%] | Transmission BW config.
15kHz | 270 | 97.2 | 48.6 MHz
30kHz | 133 | 95.8 | 47.88 MHz
60kHz | 65 | 93.6 | 46.8 MHz
 | Measurement BW
Option 1 | 48.6MHz
Option 2 | 48.6 or 47.88 or 46.8 MHz (depend on the SCS of wanted signal)
Open issue
  For ACLR vs. NR, following options can be considered as a measurement BW for adjacent channel power measurement.
  Option 1: max transmission BW configuration of the CBW (between SCS)
  Option 2: transmission BW configuration of wanted signal (with the same SCS)