## Slide 1: WF on RRM baseline setup
Rohde & Schwarz, Intel
3GPP TSG-RAN WG4 NR AH#3 R4-1710028
Nagoya, Japan, 18 – 21 September, 2017
Agenda: 3.6.4.1

## Slide 2: Status as per TR 38.810 v0.0.4 (Sep17) Cl.6.2.1.1
The baseline measurement setup of RRM characteristics for f > 6 GHz is capable of establishing an OTA link between the DUT and a number of emulated gNB sources and is shown in Figure 6.2.1.1-1 below.
The RRM baseline measurement setup shares all aspects in common with the UE RF setup defined in 5.2.1 and includes the following aspects in addition:
- N sets of cross-polarised antennas transmitting the signals from the emulated gNB sources to the DUT
- Up to 2 NR transmission reception points TRxPs are emulated
- N ≥ NMAX_AoAs, where NMAX_AoAs is the maximum number of total simultaneously emulated angles of arrival considering the modeled propagation conditions. Here “angle of arrival” refers to the arrival direction of the signals physically emulated in the chamber as result of the method used for channel emulation (and not directly to the same terminology used for clusters and sub-pathes specified in CDL model of TR 38.901).
- For non-standalone (NSA) NR devices, the test setup shall emulate in addition 1 LTE cell
- The emulated LTE cell provides a stable LTE signal without precise propagation modelling or path loss control between it and the DUT
- A positioning system such that at least 1 antenna provides for an angular relationship with the DUT with two axes of freedom that is independently controllable (or the setup should provide equivalent functionality)
- It is FFS whether more than 1 antenna needs to provide independently controllable angular relationships with the DUT.
- The N emulated signal sources will transmit into the test zone in such a way that signal polarization does not prevent the DUT receiving a consistent, predictable power level. The method for achieving this is FFS, pending further definition of the standard.
- It is likely that the measurement uncertainty budget for the RRM setup may contain additional measurement uncertainty elements relative to the setup defined in 5.2.1
- It is FFS how to model propagation conditions between the DUT and the emulated gNB sources

## Slide 3: Still to be finalized
The baseline setup definition for RRM still contains FFS as well as open items as follows:
  (1) Number of cross polarized antennas set
  N ≥ NMAX_AoAs, where NMAX_AoAs is the maximum number of total simultaneously emulated angles of arrival considering the modeled propagation conditions. Here “angle of arrival” refers to the arrival direction of the signals physically emulated in the chamber as result of the method used for channel emulation (and not directly to the same terminology used for clusters and sub-pathes specified in CDL model of TR 38.901).
  (2) Number of movable antennas
  It is FFS whether more than 1 antenna needs to provide independently controllable angular relationships with the DUT.
  (3) Polarization of antennas
  The N emulated signal sources will transmit into the test zone in such a way that signal polarization does not prevent the DUT receiving a consistent, predictable power level. The method for achieving this is FFS, pending further definition of the standard.
  (4) DL propagation condition
  It is FFS how to model propagation conditions between the DUT and the emulated gNB sources

## Slide 4: Progress in R4 NR AH#3 (1)
Based on R4-1708996 [1], RRM Testing Complexity Scenarios were identified in R4-1709837 [3]:
  Scenario 1: 1 NR TRxP + AWGN + Static AoA
  Scenario 2: 1 NR TRxP + AWGN + Dynamic AoA
  Scenario 3: 1 NR TRxP + Fading + Static AoA
  Scenario 4: 1 NR TRxP + Fading + Dynamic AoA
  Scenario 5: 2 NR TRxPs + AWGN + Static AoA
  Scenario 6: 2 NR TRxPs + AWGN + Dynamic AoA
  Scenario 7: 2 NR TRxPs + Fading + Static AoA
  Scenario 8: 2 NR TRxPs + Fading + Dynamic AoA

## Slide 5: Progress in R4 NR AH#3 (2)
R4-1709410 [2] addressed open questions captured in R4-1708996 [1] related to RRM testing:
Static channel geometry (no change of AoAs during the test) for RRM testing
    confirmed in the meeting that dynamic channel geometry is so far out of the scope of RRM testing
    dynamic channel geometry can be considered at a later stage based on further RRM agreements
The total number of distinct emulated AoAs bounded by the total number of beams emulated by the test equipment in any given RRM testing scenario.
 direct implication is a simplified channel with one AoA per Beam
   further discussed in the meeting
MIMO 2x2 Scenarios not the scope of RRM requirements (rather Demod).
     confirmed as not required in terms of data layers
    2 Tx transmission might be necessary for certain requirements (e.g. due to max BLER of control channel )
UE active beam steering.
    assumed for beam monitoring with measurement gap in static scenarios

## Slide 6: WF (1): Conclusions
1) Only RRM static geometry scenarios to be prioritized so far, i.e. in terms of RRM testing complexity scenarios as per [3]:
  Scenario 1: 1 NR TRxP + AWGN + Static AoA
  Scenario 3: 1 NR TRxP + Fading + Static AoA
  Scenario 5: 2 NR TRxPs + AWGN + Static AoA
  Scenario 7: 2 NR TRxPs + Fading + Static AoA
2) „Fading“ i.e. emulation of the propagation channel for RRM is under discussion in another WF. Its appliance to 1 or 2 TRxPs affects directly the baseline setup.

## Slide 7: WF (2): Further considerations / questions (to RRM requirement experts)
3) Test case definitions / requirements to be bounded by the RRM testing complexity scenarios in bullet 1) (such test coverage to be considered in the core requirement definitions)
4) In general recommended to avoid testing requirements with unnecessary high / combined complexity. This means: 4.1) Reduce complexity, to the lowest required. Example: if Fading required, consider to limit it only to the necessary TRxPs i.e. in cases with 2 TRxPs, consider the feasibility of requirement with only 1 TRxP faded.
    4.2) „Split“ complexity if requirement testing coverage is ensured by separate testing. Example: in stead of Beam steering with Fading, consider splitting the testing into Beam steering + AWGN and No beam steering + Fading.
5) In case of RRM testing with (DL) 2 Tx diversity, can polarization diversity be confirmed as the assumed scheme?

## Slide 8: References
[1] R4-1708996: WF on RRM/Demod baseline test system, R&S
[2] R4-1709410: On defining the testable channel model for RRM, Intel
[3] R4-1709837: Test scenarios and test system complexity for NR RRM OTA testing, R&S