## Slide 1: WF on UE RF requirements for Band n77, n78 and n79
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR#3 Meeting
Nagoya, Japan, 18 - 21 Sep, 2017
R4-1710031

## Slide 2: Background
UE RF requirements for below bands are being discussed to complete them by December 2017
  Band n77: 3.3-4.2 GHz
  Band n78: 3.3-3.8 GHz
  Band n79: 4.4-5.0 GHz

## Slide 3: Summary of proposals
 | Intel | Huawei | LGE | Dish | Skyworks | Docomo | Vodafone | Nokia
R4-170xxxx | 9304 | 9543 | 9581 | 9686 | 9384 | 7507, 9387 | 9746 | 9487
NF | 11dB for n77/n78/n79 | 10dB as B42 for n77/n78 1 or 2dB larger for n79 compared to n77/n78 | 10dB for n77/n79 9dB for n78 | 7.5dB for < 3GHz whose filter IL is max 2dB in ETC 8dB for 3-4.2GHz whose filter IL is max 2dB in ETC 9dB for > 4.2GHz whose filter IL is max 2dB in ETC | 9dB for TDD < 3-5GHz, low dup gap b/w 1.4-2.7GHz 8dB for FDD with reasonable duplex gap, and SDL/TDD bands b/w 1.4-2.7GHz FFS for FDD with challenging dup gap | Same for n77, n78 and n79 | 0.6dB better (filter only) for n78 compared to n77 | Same filter data as Vendor C (not LTCC) of Vodafone paper
IM | 2.5dB for n77/n78/n79 |  | 2.5dB for n77/n78/n79 | 2.5dB for FDD 2dB for TDD | < 1dB for TDD <1.5dB for FDD |  |  | 
Drib |  | if NF 10.5dB is allowed, delta RIB can be 0dB. |  | 0dB for all NR bands that are supported in any CA configuration |  |  |  | 
SNR | -1dB for n77/n78/n79 | -1.67 to -1.51 | -3dB |  |  |  |  | 

## Slide 4: WF on Band n77 and n78
REFSENS
  NF to be discussed based on more filter data
  Filter data satisfying the following conditions will be considered for insertion loss and REFSENS
    Attenuation is at least typ. 35 dB for ≤ 2.69 GHz and ≥ 5.15 GHz (35 dB is required for both B46 and 5 GHz WiFi as a consensus in RAN4)
    FFS how to treat cases that these NR bands and B46 are not supported simultaneously
  It will be confirmed that IM of TDD bands is 0.5 dB better than that of FDD ones
  SNR is being discussed in other documents
Out-of-band blocking
  To be discussed taking filter aspects above into account
DTib and DRib (for CA/DC)
  To discuss if values of LTE CA including B42 can be improved

## Slide 5: WF on Band n79
MOP and REFSENS
  To confirm if Band n79 UEs need to protect 5.15-5.925 GHz
    If 5 GHz is to be protected, filter data in R4-1709487 (Nokia) can be referred (max IL = 2.3 dB) but the IL could be improved considering relaxed attenuation to typ. 35 dB
    If 5 GHz is not to be protected, filter data in R4-1709387 (Docomo) can be referred (max IL = 1.1 dB)
Out-of-band blocking
  To be discussed taking above filter aspects into account
DTib and DRib (for CA/DC combo including Band n79)
  To confirm if separate antenna architecture can be assumed