## Slide 1: 3GPP TSG-RAN WG4 Meeting NR#3 Nagoya, Japan, 18-21 September 2017
Ericsson
WF on mmWave NR BS inband blocking
R4-1710041

## Slide 2: Background
Three questions are discussed in RAN4#NR AH3:
  What is the delta between wanted signal level and blocker level?
  What could the “conducted” blocking level be?
  How to define OTA level from the above defined “conducted” level?

## Slide 3: Delta between wanted signal level and blocker level
“Conducted” wanted signal level
  -174+log(200MHz)+10(NF)+6 = -75dBm/200MHz when CBW = 200MHz.
Note that, ACS level is defined as 24dB, thus “conducted” ACS interferer level will be -51dBm/200MHz
  Consider the fact that -51dBm has zero probability of occurrence according to blocking simulations
Delta is FFS.
  Companies are encouraged to provide insight into this issue in the coming meetings.
FFS how to derive absolute blocker levels and wanted levels based on the above mentioned delta.

## Slide 4: “Conducted” blocker level
The “conducted” blocker level can be within the following range:
  [-70, -65] dBm for digital beamforming architecture
  [-66, -63] dBm for analog beamforming architecture
This is valid for all mmWave bands

## Slide 5: How to convert OTA level from “conducted” level
Gains for analog and digital beamforming is different
  E.g. 30dBi vs 5dBi
Simulations show that blocker levels in conducted case is similar for both architectures
Options
  Option-1: Define one OTA level
    Pros: Simple solution
    Cons: Might be incorrect for one or both of the architectures
  Option-2: Attempt to reuse eAAS framework
    Cons: RoAoA declaration does not work properly
  Option-3: Declare “two” different OTA levels based on BS architectures (i.e. analog or digital BF)
    Cons: BS needs to declare “architecture”