## Slide 1: WF on support of sub-carrier spacing
Huawei
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3 R4-1710047
Nagoya, Japan, 18 - 21 Sep, 2017

## Slide 2: Background
RAN4 needs to discuss and decide on the support of sub-carrier spacing in the aspects that [1]
BS supporting sub-carrier spacing simultaneously and not simultaneously
UE supporting sub-carrier spacing simultaneously and not simultaneously

## Slide 3: Way forward for BS
BS shall support the sub-carrier spacing of synchronization signal for both data and synchronization signal
  In case more than one SS SCS can be configured for a band, the BS shall support at least one SS SCS
BS declares the support of other sub-carrier spacing(s) including:
  the sub-carrier spacing(s) that can be supported in TDM manner
  the sub-carrier spacing combinations that can be supported in FDM manner
    Detail is FFS

## Slide 4: Way forward for UE
UE shall support sub-carrier spacing(s) for data in TDM manner as below in Rel-15:
  For sub-1GHz
    Mandatory: 15k, 30k
  For 1GHz-6GHz
    Mandatory: 15k, 30k
    Optional: 60k
  For mmWave
    Mandatory: 60k, 120k

## Slide 5: Reference
[1] R4-1709548, On support of sub-carrier spacing, Huawei, HiSilicon