## Slide 1: WF on beam switching time requirement
NTT DOCOMO, INC.
R4-1710073
3GPP TSG-RAN WG4 NR Meeting #3
Nagoya, Japan, 18-21 September 2017
Agenda Item: 3.4.2.1

## Slide 2: Background
Base on the agreed WF in the last meeting [R4-1709079], Beam switching speed as NR BS new requirements are discussed in [1-7].
This contribution summarizes way forward/agreement on this topic.
[1] R4-1709431 Discussion on beam switching transient period for NR CATT
[2] R4-1709456 Proposal on NR BS beam switching speed requirements NTT DOCOMO, INC.
[3] R4-1709652 Discussion on beam switching speed for range2 NR BS ZTE Corporation
[4] R4-1709694 Beam switching requirement core requirement considerations Ericsson
[5] R4-1709695 Impact of beam switching time on DL performance Ericsson
[6] R4-1709729 Challenges of beam switching time requirement Huawei
[7] R4-1709827 Beam Switching Speed Simulation Results Nokia, Nokia Shanghai Bell

## Slide 3: WF on simulation
Encouraged companies provide the simulation results of the relation between beam switching time (0 ~ CP length) and performance degradation (100% is assumed for no delay) based on below simulation assumption in RAN4#84bis in Dubrovnik [and RAN4#85 in Reno]. Based on the results, RAN4 will further clarify the required beam switching time smaller than CP length.
Parameters | Values
Evaluated channel | PSS/PBCH/PDCCH/PDSCH
Carrier frequency | 28GHz
BS CBW | 400MHz
SS block SCS | 240kHz
Data CH SCS | 120kHz
Beam Switching Time | 0% , 20, 40, 60, 80, 100%, of CP
Channel Type | TDL_C
Delay spread | 300ns(, 100ns), 1000ns

## Slide 4: WF on core spec description
Attached draft text can be used for baseline for TS text for potential requirement.
  Encouraged companies provide suggested change for next RAN4#84 meeting, based on that.
[Information] Following is already agreed in R4-1706158
  RAN4 agrees to work to create a description of a RF Beam switching speed requirement for potential introduction in Rel-15 NR core spec is derived based on a NR BS with analog BF.
    If requirement description becomes agreed, RAN4 introduces the requirement in core spec.

## Slide 5: WF on TP for BS TR
Encouraged companies provide TP for BS TR capturing following contents on this topic.
  Background
  Discussion in RAN4
    Typical estimated delay
  Simulation results
  Conclusion (whether introduced this potential requirement in core spec or not)
  Note: Final one (conclusion) will be drafted once RAN4 reaches consensus.