## Slide 1
WF on BCS and CA bandwidth class for LTE-NR DC
Nokia, Nokia Shanghai Bell
R4-1710083

## Slide 2
BCS Background information (1/2)
Wheather to introduce BCS , simplified BCS or no BCS for NR was discussed in RAN4#NRAH3.
REFERENCES:
[1] R4-1709340 Discussion on Issues Related to NR CA and LTE-NR DC, Samsung
[2] R4-1709474 NR bandwidth combinations sets and CA bandwidth classes, Nokia
[3] R4-1709471 Considerations on NR Bandwidth combination set, ZTE
[4] R4-1709493 On NR CA bandwidth class, ZTE
[5] R4-1709579 Further clarification for Wideband operation of NR UE LG Electronics France

## Slide 3
Company proposals
BCS Background information (2/2)
Samsung [1]
Proposal 2: For LTE band combination within LTE-NR DC, BCS concept shall be reused, and the agreement for LTE fallback BC should be followed.
Proposal 3: For NR band combination within LTE-NR DC, no BCS concept will be introduced.
Nokia [2]
Proposal 1: Concept of bandwidth combinations sets is not introduced into NR
Proposal 2: When operating in LTE – NR DC UE shall indicate support for all specified LTE bandwidth combinations sets that belong to the LTE CA configuration part of LTE – NR DC.
Proposal 3: When operating in DC band combinations of LTE 1DL/1UL + one NR band UE will support all LTE channel bandwidths that are specified to the LTE band
ZTE [3]
Proposal 1: In order to compromise between the complexity of specification and UE implementation, a simplified concept of BCS is suggested to be used in NR CA configuration.
Proposal 2: It is suggested to categorize the channel bandwidth into several range sets according to different frequency ranges and SCSs, e.g., Low_ range, Mid_ range and High_ range.
Proposal 3: Similar to BCS concept in E-UTRA CA configuration, the simplified BCS concept can be applied to intra-band contiguous CA, inter-band CA and non-contiguous intra-band in NR.

## Slide 4
WF for NR BCS
Condering NR bands in LTE-NR DC:
Bandwidth combinations sets are not specified for NR bands part of LTE-NR DC configuration
UE supports same NR channel bandwidths when operationg in LTE-NR DC configuration as it supports for the that NR band in standalone operation
Where IMD is an issue only for a subset of channel bandwidths within a band/band combination, the bandwidths for which MSD is applicable shall be specified in receiver charateristics section.
Considering LTE bands LTE-NR DC:
The need for BCS for LTE band in LTE-NR DC is discussed separately from NR BCS
LTE-NR DC UE shall signal BCS information to eNodeB (to reduce changes to LTE UE and eNodeB desing)
LTE-NR DC UE shall signal support for all specified LTE bandwidth combinations sets that belong to the LTE CA configuration part of LTE – NR DC (to reduce UE fragmentation and make RAN4 specification effort smaller as no LTE BCS information is needed in NR specs)
When operating in DC band combinations of LTE 1DL/1UL + NR band(s) UE will support all LTE channel bandwidths that are specified to the LTE band (otherwise LTE bandwidth capablility is unknow as single CC operation does not have BCS)

## Slide 5
NR CA BW class Background information
Company proposals
Samsung [1]
Proposal 1: CA bandwidth class is not enough for intra-band contiguous CA, which should be replaced by number of CC. For UE capability indication on intra-band contiguous CA more specific bandwidth combination may be needed.
Nokia [2]
Separate CA BW Class tables for range 1 and range 2
ZTE [3] Separate CA BW Class tables for LTE refarming bands, range 1 and range 2
Proposal 1: It is suggested to classify CA bandwidth class by using the channel bandwidth for each carrier and the total aggregated channel bandwidth directly instead of calculating the RB numbers in NR.
Proposal 2: It is suggested to classify CA bandwidth class in NR by different maximum channel bandwidth for each frequency range, respectively.
Proposal 3: NR CA CC channel bandwidths can follow single carrier’s channel bandwidths but it is suggested to provide possibility to further reduction by allowing only a sub-set of single carrier NR BW’s.
Proposal 4: It is suggested that CA bandwidth class in NR be categorized according to the number of CCs supported in carrier aggregation.

## Slide 6
WF for NR CA bandwidth class
CA bandwidth class concept is introduced into NR specifications to distinquish UE capabilities when operating in LTE-NR DC and NR CA configurations
NR CA bandwidth class applicability to NR wideband operation is FFS
Separate NR CA bandwidth class tables are defined for NR range 1 and range 2.
NR CA bandwidth class includes atleast information on aggregated channel bandwidth and number of contiguous CC.