## Slide 1: NB-IoT RF-RRM status before RAN5#71 CMCC 2016.05.12

## Slide 2: Introduction
  RAN5 NB-IoT WI starts from RAN#71 and is planned to be complete in November.
  This slides will give a general information about NB-IoT progress in 3GPP RAN4 which mainly relate to RF and RRM core and performance requirements.
  The items marked blue means this requirements have been completed in RAN4.
  The items marked red means this requirements are still ongoing in RAN4.
  The items marked dark means this requirements are partially complete in RAN4.

## Slide 3: NB-IoT general information
  Duplex Mode
  HD-FDD
  Three operation modes
  Stand-alone operation
    making use of scattered spectrum and e.g. re-farming of GSM spectrum.
  In-band operation
    making use of resources that are within the system bandwidth of the MBB LTE cell.
  Guard-band operation
    making use of the currently unused resource blocks at the edges of the MBB LTE cell.
  UL Multiple Access
  Single tone: 3.75kHz carrier or 15kHz carrier
  Multi-tone: multiple 15kHz carriers, with SC-FDM
  DL Multiple Access
  15kHz carriers, with OFDM

## Slide 4: Overall progress after April adhoc meeting
Overall Core part: 95%
  RAN1 100%
  RAN2 92%
  RAN3 80%
  RAN4 85%
  Completion date: June 2016 RAN #72
RAN4 Performance part:
  Completion status: 0%
  Completion date: September 2016 RAN #73
  RAN5 Core part:
  Completion date: December 2016 RAN #74
  RAN5 Performance part:
  Completion date: March 2017 RAN #75

## Slide 5: RF progress in RAN4
  Use TS 36.101 for NB-IOT UE RF requirements
  Frequency bands and channel arrangement
  Operating bands
    Re-use existing E-UTRA band definition for NB-IOT.
  Channel bandwidth (R4-78AH-0177)
    for standalone: UL and DL channel BW is 200 kHz for both single tone and multitone
    for Guard band and In band: UL channel BW is 200 kHz, DL use LTE channel BW
  Channel raster
    for in, guard and standalone is 100 kHz
  EARFCN
    Channel numbering is defined

## Slide 6: RF TX progress in RAN4
  Maximum output power
  power classes 3 (23 dBm) and class 5(20dBm)
  MPR:
  single tone transmissions are not allowed to have MPR
  Tentatively agree MPR values for power class 3; Simulate power class 5 MPR for Nanjing; (R4-78AH-0237)
  AMPR: Not needed(R4-78AH-0060)
  Minimum power: -40 dBm
  OFF power: -50 dBm
  ON/OFF time mask: reuse E-UTRA General ON/OFF time mask
  Power control tolerance
  Absolute power tolerance reuse E-UTRA requirement
  Relative power tolerance, Aggregate power control tolerance requirement FFS
  Frequency error: same as LTE for all coverage modes(R4-78AH-0122)

## Slide 7: RF TX progress in RAN4
  EVM: single tone rotated pi/2 BPSK, pi/4 QPSK, multitone QPSK EVM requirement is 17.5 %, measurement method (R4-78AH-0040)
  In-band emissions:
  within a PRB, In-band emission including general emission, IQ Image and carrier leakage.
  General in-band emission:
    for NB-IoT with in a PRB is to be specified based scaling of the current LTE requirement .(R4-78AH-0199)
  carrier leakage: FFS
  Occupied bandwidth: defined as the bandwidth containing 99 % of the total integrated mean power of the transmitted spectrum (R4-78AH-0124)
  SEM: defined in R4-78AH-0064
  ACLR: defined GSMACLR requirement for protection of GSM system. defined UTRAACLR requirement for protection of UTRA and E-UTRA systems.(R4-78AH-0064)
  Transmitter Spurious emissions: reuse 6.6.3 in 36.101, with an exception that boundary shall be FOOB = 1.7 MHz (R4-78AH-0064)
  Spurious emission band UE co-existence: refers back to E-UTRA requirement

## Slide 8: RF TX progress in RAN4
  Additional spurious emissions: Not needed(R4-78AH-0060)
  Transmit intermodulation: defined in R4-78AH- 0234
  Inter system co-existence study
  study on standalone is complete, NB-IoT can coexist with GSM, UMTS and LTE.
  NB-IoT can coexist with LTE in-band and guard band with the observations as follows,
    NB-IoT perform some interference on 1st adjacent LTE PRB, while the interference on other PRBs is insignificant or acceptable.
    Some impact on NB-IoT at high SNR.
    Guard band operation perform slightly better coexistence compared to in-band operation.

## Slide 9: RF RX progress in RAN4
  Reference sensitivity:
  REFSENS without repetitions is defined as a baseline. This REFSENS will be used as reference for other NB-IoT Rx requirements. Sensitivity with repetitions will also be defined in section 7.3.1F. This REFSENS is specified only for normal conditions. No channel model is used in the test. (R4-78AH-0231)
  Maximum input level: -25dBm.
  ACS: defined in R4-78AH-0201
  In-band Blocking: defined in R4-78AH-0066
  Out-of-band blocking:
  FFS, shall not be more stringent than OBB for LTE
  Spurious response: Apply the legacy E-UTRA requirements(R4-78AH-0233)
  Narrow band blocking: Not needed because it can be verified by ACS. (R4-78AH-0071)
  Wide band Inter-modulation: parameters defined in R4-78AH-0238, requirements still under discussion
  Receiver spurious emissions
  reuse the existing EUTRA requirements. (R4-78AH-0073)

## Slide 10: RF Performance progress in RAN4
  Demodulation of NPDSCH
  Not yet discussed
  Demodulation of NPDCCH
  Not yet discussed
  Demodulation of NPBCH
  Not needed

## Slide 11: RF CSI report progress in RAN4
  CQI / PMI/ RI Reporting under AWGN conditions
  Not needed

## Slide 12: RRM progress in RAN4
  Cell selection requirement
  Requirement for initial cell selection shall not be specified.
  Cell reselection: (R4-78AH-0223)
  Measurement and evaluation of serving cell for NB-IOT in normal coverage and extended coverage
  Measurements of intra-frequency NB cells for NB-IoT in normal coverage and extended coverage
  Measurements of inter-frequency NB cells for NB-IoT in normal coverage and extended coverage
  Maximum interruption in paging reception: Tpaging= TSI-NB-IoT + 100 ms; (R4-78AH-0140)
  UE measurement capability
  RRC Re-establishment:
  The RRC re-establishment requirements in R4-78AH-0235.
  There is no need to introduce the corresponding requirements for RRC connection Resume procedure. (R4-78AH-0087)
  RRC re-establishment requirements should be defined for normal and enhanced coverage with different cell search delays. Companies is encouraged to investigate whether only the cell search delay is different for normal and enhanced coverage levels. (R4-78AH-0213)
  Random access:
  Will use LTE random access procedures. (R4-162865)
  Only contention based random access requirements will be defined.(R4-78AH-0213; R4-78AH-0086)

## Slide 13: RRM progress in RAN4
  UE transmit timing (R4-78AH-0191, R4-78AH-0192)
  NB-IoT UE initial transmission timing error limit Te for 240KHz downlink bandwidth is to be relaxed to 80*TS – k*Ts where ‘k’ is TBD
  RAN4 agrees that onset of a new UL repetition period shall be considered to be an initial transmission
  The NB-IoT UE shall adjust the timing of its uplink transmission at the end of contiguous UL repetitions, i.e. either at the end of a UL gap for frequency error correction or at the end of all UL repetitions, for a timing advance command received in sub-frame n.
  The NB-IoT UE shall adjust the timing of its transmissions with a relative accuracy better than or equal to ±13.33* TS seconds to the signalled timing advance value compared to the timing of preceding uplink transmission.
  The maximum autonomous time adjustment step Tq for NB-IoT UE shall be 58.33* TS seconds.
  The minimum aggregate adjustment rate shall be kept at 7*TS per second.

## Slide 14: RRM progress in RAN4
  UE Timing Advance
  Timing Advance adjustment delay and accuracy requirement defined in R4-78AH-0192
  Radio link monitoring
  The existing framework of RLM requirement for Cat-M1 UE can be reused for NB-IoT RLM(R4-162872)
  Assuming hypothetical NPDCCH BLER thresholds of 2% and 10%
  Whether the same or different transmission parameters are needed for RLM when NB-UE is configured on anchor carrier or non-anchor carrier is FFS.
  Define the NB-IoT RLM requirements based only on NB-RS in Rel-13.(R4-78AH-0164)
  RAN4 is to specify minimum RLM requirements for different ranges of Rmax. (R4-78AH-0220)
  Whether RAN4 is to specify different RLM requirements for the different deployment modes based on the simulations outcome is FFS.
  Whether there is any impact of power-boosting of NB-IoT NPDCCH/NRS RE compared to LTE CRS RE in in-band/guard band is FFS.

## Slide 15: RRM progress in RAN4
  Measurement (R4-78AH-0216)
  RAN4 will not define measurement reporting requirements for mobility.
  RAN4 is to define NRSRP/NRSRQ measurement requirements based on NB-RS measurement for Rel-13 NB-IoT
  Joint use of NB-RS and NB-SSS for measurement are not considered
  NB-SSS can be used alone for RRM measurement
  RAN4 is to define different measurement requirements for extreme and normal coverage modes.
  RAN4 is not to specify minimum number of inter-frequency carriers to monitor per deployment mode(in-band/standalone/guard-band).
  RAN4 is to specify NB-IoT measurement requirement for RRC_CONNECTED state.
  The SNR level of normal coverage is [-6dB], extreme coverage is [-12.5dB].
  When the measurement period is 800ms and SNR is -6dB, the absolute NRSRP accuracy is [+/-8dB], including +/-3dB RF margin, the absolute NRSRQ accuracy is [+/-6.5dB]
  When the measurement period is 800ms and SNR is -12.5dB, the absolute NRSRP accuracy is [+/-10dB], including +/-3dB RF margin, the absolute NRSRQ accuracy is [+/-8dB]
  RAN4 is not to define requirement for intra-frequency or inter-frequency relative RSRP measurement

## Slide 16: Discussion
  The overall completion of RAN4 RF and RRM core requirements now is 85%, it is anticipated RAN4 will complete all core requirements on time. Besides RAN4 is considering adding adhoc meetings for performance requirements after June to complete it in September.
  For RAN5, the work plan need to be discussed and optimized during RAN5#71. Test case definition work could be carried out afterwards.