## Slide 1: 3GPP RAN5 #76 Berlin, Germany 21-25 August 2017 R5-173920 Test Tolerance Review Training

## Slide 2: Overview
Contents
  Why we need an analysis
  Section-by-section review of the analysis.xls for simplest case 4.2.1
  High level summary of the analysis.doc contents
The analysis.xls and the analysis.doc are included in the zip file
This training focusses on the analysis.xls

## Slide 3: Why we need Test Tolerance analyses
Motivation
  Test Tolerances are applied, where necessary, so that a good UE does not fail a test case because of Test System uncertainties.
  For basic Core requirements, for example those tested in TS 36.521-1 sections 5 and 6, Test Tolerances are easy – just relax the core requirement by the amount of the Test System uncertainty.
  For most RRM Test cases in TS 36.521-3 there are side conditions as well as core requirements. Both must be met to avoid failing a good UE.
  The Test Tolerance analysis is to make sure both side conditions and core requirements are met, including effects of Test System uncertainties.
Scope
  This training covers an example RRM Test case in 36.521-3, with the analysis stored in TS 36.903.
  Some demodulation Test cases in 36.521-1, have analyses stored in TS 36.904.

## Slide 4: Section a) Original specified key parameters
Only a few of the parameters are required to define the test:
These are the ones that go into section a) of the analysis.xls

## Slide 5: Section b) Derived parameters, 1 of 3
Other parameters can be derived, and the spreadsheet derives them:
..so you can check that RAN4 got them right:
We also derive some extra parameters for use by the analysis

## Slide 6: Section b) Derived parameters, 2 of 3
Two examples of derivation: “Absolute power, linear” and Es/Iot

## Slide 7: Section b) Derived parameters, 3 of 3
Why do we derive parameters?
  Some derived parameters have to stay within a side condition
  Absolute power in linear units is used to calculate E/Iot, and also used to calcuate sensitivity factors in the spreadsheet section d)
  Some core requirements apply to parameters not given in the test case. For example we derive “RSRP difference” between Cell 1 and Cell 2, because there is a “better ranked” requirement in 36.133:

## Slide 8: Section c) Uncertainties
Test system uncertainties apply to the Original specified key parameters
..and match exactly with the values in TS 36.521-3:
The uncertainties have to be orthogonal to each other, and..
..be a minimum set. Derived parameters don’t need uncertainties in c).

## Slide 9: Section d) Controlled parameters critical to verdict, 1 of 4
Step 1: Decide which they are:
..by identifying the core requirements in TS 36.133 that apply to this test case

## Slide 10: Section d) Controlled parameters critical to verdict, 2 of 4
The sensitivity of Cell 1 Es/Iot to Noc (AWGN) is 0
The sensitivity of Cell 1 Es/Iot to Cell 1 Es/Noc is 1.000
The sensitivity of Cell 1 Es/Iot to Cell 2 Es/Noc is 0.975, = (interference from Cell 2/Total interference) = 6.310/(6.310+0.158)
Pie charts can be useful for calculating sensitivity factors
The sensitivity factors are per-controlled-parameter, per-uncertainty, and per-time-period
Step 2: Calculate how sensitive each parameter is to each uncertainty:

## Slide 11: Section d) Controlled parameters critical to verdict, 3 of 4
Step 3: For each controlled parameter, in each time period, multiply each uncertainty by its sensitivity factor
Here we are working out how much effect the uncertainty will have on the controlled parameter, for example Cell 1 Es/Iot during T2:
Cell 1 Es/Iot has a sensitivity factor of 0 to AWGN Noc uncertainty. So (+/-1dB x 0) = 0dB
Cell 1 Es/Iot has a sensitivity factor of 1 to Cell 1 Es/Noc uncertainty. So (+/-0.3dB x 1) = 0.3dB
Cell 1 Es/Iot has a sensitivity factor of 0.975 to Cell 2 Es/Noc uncertainty. So (+/-0.3dB x 0.975) = 0.293dB

## Slide 12: Section d) Controlled parameters critical to verdict, 4 of 4
Step 4: Add up the effects of all the uncertainties
Here we are working out how much effect the uncertainty will have on the controlled parameter, for example Cell 1 Es/Iot during T2:
Uncertainties are normally added root-sum-square, as they are statistical 90% confidence values
The overall uncertainties are per-controlled-parameter and per-time-period

## Slide 13: Section e) Determine parameters to offset
It’s usually best to leave this to the end!
We use section f) to try out offset values, and watch section g) to determine whether we meet all the requirements

## Slide 14: Section f) Parameters modified by Test Tolerances, 1 of 2
Step 1: List again the Original specified key parameters
Step 2: Make provision to apply an offset, and calculate the new value

## Slide 15: Section f) Parameters modified by Test Tolerances, 2 of 2
Step 3: Re-calcuate the derived parameters based on new values:
The selection of derived parameters is the same as in section b)
..and the calculation method is the same
..but the values now include the effect of any applied offsets

## Slide 16: Section g) Check controlled parameters Min/Max, 1 of 4
Step 1: List again the Controlled parameters critical to verdict, this time using the uncertainties from d) to calculate the Min and Max values:
Uncertainty values are per-controlled-parameter, and per-time-period. They are copied directly from section d)

## Slide 17: Section g) Check controlled parameters Min/Max, 2 of 4
Step 2: Find out the Core requirement relating to each parameter

## Slide 18: Section g) Check controlled parameters Min/Max, 3 of 4
Step 3: Adjust/check the offsets to make sure all core requirements met
  For example, if we set all the offsets to 0dB in this test case:
  The minimum RSRP difference between Cell 1 and Cell 2 is not big enough to meet the “3dB better ranked” requirement, and a good UE could fail the Test Case

## Slide 19: Section g) Check controlled parameters Min/Max, 4 of 4
Sometimes the amount of offset can be calcuated from the uncertainty
  For example, the offset is made equal to the (Cell 2 RSRP – Cell 1 RSRP) uncertainty:
  **

## Slide 20: Return to section e) Determine parameters to offset
Now we have found a solution, can summarise it:
Section e) is an encouragement to think about which offsets to apply
Sometimes the solution can only be found by trial and error
We aim to use the smallest offsets needed to meet all the requirements

## Slide 21: The analysis.doc
Contents
  Includes an extract of the TS 36.133 Annex A Test case
  Includes explanation of the uncertainty values
  Includes relevant Core requirement and side condition extracts from TS 36.133
  Often includes additional diagrams to explain the reasoning
  Often includes information about differences/similarities across the test cases covered by the analysis