## Slide 1: Summary of pending issues [1/3]
Pending issues during R4#88 <-> R5#80 are summarized as below. (Detailed contents are specified in attached spreadsheet.)
Specs | Pending issues | Impact on RAN5 | Pending items in RAN4 specs
TS 38.101-1 TS 38.521-1 | Requirements are not finalized. (TBD, square bracket) | Test req. (criteria) can not be defined and Test cases can not be completed. | ACS, Time mask, MPR (PC1, 4) EVM equalizer… (shaped pi/2-BPSK) Relative power tolerance, ACLR (PC1,4) etc.
 | Remaining “TBD”, “square brackets” | Corresponding TBDs also in RAN5 spec. | - Measurement period in Tx TCs (time mask, min output power etc.) - UE power for 256QAM is TBD (EVM) - References (RMC, OCNG in Rx TCs) etc.
 | Annex F.5.3/4/5 not defined. | Frequency Error test case ,transmit modulation quality test cases (EVM, Carrier Leakage) cannot be completed | - Window length (Annex F.5.3/4/5)
TS 38.101-2 TS 38.521-2 | Requirements are not finalized. (TBD, square bracket) | Test req. (criteria) can not be defined and Test cases can not be completed. | MPR (PC3), Configured transmitted power Abs/Rel/Agg power tolerance
 | Test cases are not defined. | Corresponding TCs can not be defined in test spec. | MPR (PC2,4), PUCCH time mask, OOBB, Spurious response, Receiver image
 | Ref. parameters for MPR = 0 dB is TBD. - “The waveform defined by TBD is the reference waveform with 0dB MPR and is used for the power class definition.”, - “UE requirements for the waveform defined by TBD shall be set to 0dB MPR.” | MOP test case (test configuration) cannot be defined. | 6.2.2 MPR (Missing this information MOP test case cannot be defined.)
 | DL RMC for Max input level is FFS. | Test spec for Max input level cannot be defined. | DL RMC for Max input level (Annex A)

## Slide 2: Summary of pending issues [2/3]
Pending issues during R4#88 <-> R5#80 are summarized as below.
Specs | Pending issues | Impact on RAN5 | Pending items in RAN4 specs
TS 38.101-1/2 TS 38.521-1/2 | “Confirm measurement period for MOP, transmit off power and frequency error: - On one hand minimum time unit that can be scheduled in NR is one slot - If 1ms is the measurement period for these requirements, there will be discontinuous measurements in time to collect 1ms according to current UL RMC definition for certain SCS.” | Discontinuous measurements for mean power and frequency error increase testing time. | MOP, Transmit off power, Frequency error
TS 38.101-1/2/3 TS 38.521-1/2/3 | “Occupied bandwidth“ Conformant UE in terms of SEM would not pass the Occupied BW tests. | Impact on test procedure. | Core requirement requires further clarification. (related to R4-1810866)
TS 38.101-1/2 TS 38.521-1/2 | UL-DL configuration for UL RMC is not defined. | Test procedure cannot be completed. | Annex A.2.3 Reference measurement channels for TDD
TS 38.101-3 TS 38.521-3 | Section title of several Rx test cases is not defined in core spec. (Please see TCs marked [Not defined] in slide#4.) | RAN5 38.521-3 spec cannot plan to define corresponding TCs. | Missing - Rx Blocking characteristics (Section 7.6) - Rx Spurious response (Section 7.7) , - Rx Intermod characteristics (Section 7.8) - Rx Spurious emissions (Section 7.9) etc.

## Slide 3: Summary of pending issues [3/3]
Specs | Pending issues | Impact on RAN5 | Pending items in RAN4 specs
TS 38.101-3 TS 38.521-3 | Several TRx test cases (across intra C, intra NC, inter FR1/2, FR1+FR2) have no content added. (Please see TCs marked [No contents] in slide#4.) | Based on previous Joint Session guidance from RAN4, current RAN5 assumption is that SA requirements apply. RAN5 asks RAN4 to add some verbiage for clarity in such sections indicating whether a) “SA requirements would apply” or b) “Additional requirements are still FFS” to avoid incorrect assumptions. | 6.2B.2 (MPR) 6.2B.4.1 (Configured Output Power Level) 6.5B.2.4 (OOBE) Below sections not present in 38.101-3 but guidance from joint session was SA reqs apply 7.4 – Max I/P Level 7.5 – ACS etc.
 | For EN-DC Inter-band within FR1, RAN4 provided guidance that LTE config can be based on 36.101. Request guidance for intra-band. | Test cases for EN-DC intra contiguous cannot be defined. | All EN-DC intra-band scenarios (6.XB, 7.XB)
 | Per RAN4 <-> RAN5 Joint session in Busan, RAN4 indicated that LTE Parametrics do not have to be measured as part of the EN-DC test for inter-band and can be leveraged from standalone 36.101 requirements based testing. Can RAN4 confirm this understanding? | Test cases for EN-DC inter contiguous cannot be defined. | All EN-DC inter-band scenarios (6.XB, 7.XB)
 | Power Sharing between LTE & NR not clarified | Completion of MOP tests | 6.2B.1 (MOP), 6.2B.4 (Configured Output power)
Pending issues during R4#88 <-> R5#80 are summarized as below.

## Slide 4: Status of TS 38.101-3 EN-DC TCs
Status (under discussion or Completed without additional requirement) of items “No contents”, “Not defined” should be clarified.
  Present : Section (Title) is defined and contents are present.
  No contents : Section (Title) is defined while contents are not defined.
  Not defined : Section (Title) is not defined.
TC | Title | Intra-band contiguous EN-DC | Intra-band non-contigusou EN-DC | Inter-band EN-DC within FR1 | Inter-band EN-DC including FR2 | Inter-band EN-DC including both FR1 and FR2
6.2B.1 | UE maximum output power for EN-DC | Present | Present | Present | Present | Present
6.2B.2 | UE maximum output power reduction and EN-DC | No contents | No contents | No contents | No contents | No contents
6.2B.3 | UE additional maximum output power reduction for EN-DC | Present | Present | No contents | No contents | No contents
6.2B.4 | Configured output power for EN-DC | No contents | No contents | No contents | No contents | No contents
6.2B.4.2 | ΔTIB,c for EN-DC | No contents | No contents | Present | Present | Present
6.3B | Output power dynamics for DC | Present | Present | Present | Present | Present
6.4B.2.X | Error Vector Magnitude | Present | Not defined | Not defined | Not defined | Not defined
6.4B.2.X | Carrier leakage | Present | Not defined | Not defined | Not defined | Not defined
6.4B.2.X | In-band emissions | Present | Not defined | Not defined | Not defined | Not defined
6.5B.1 | Occupied bandwidth for EN-DC | Present | Not defined | Not defined | Not defined | Not defined
6.5B.2.X | Spectrum emissions mask | Present | Present | Present | No contents | No contents
6.5B.2.X | Additional spectrum emissions mask | Present | Present | Present | No contents | No contents
6.5B.2.X | Adjacent channel leakage ratio | Present | Present | Present | No contents | No contents
6.5B.3.X | General spurious emissions | Present | No contents | Present | Present | Present
6.5B.3.X | Spurious emission band UE co-existence | Present | No contents | Present | Present | Present
6.5B.4 | Additional spurious emissions | Not defined | Not defined | Not defined | Not defined | Not defined
6.5B.[5] | Transmit intermodulation for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.3B.2 | Reference sensitivity for EN-DC | Present | Present | Present | Present | Present
7.3B.3 | ΔRIB,c, ΔRIBNC for EN-DC | No contents | Present | Present | Present | Present
7.4B | Maximum input level for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.5B | ACS for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.6B | Rx Blocking characteristics for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.7B | Rx Spurious response for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.8B | Rx Intermodulation characteristics for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined
7.9B | Rx Spurious emissions for EN-DC | Not defined | Not defined | Not defined | Not defined | Not defined