## Slide 1: Multi-band relaxation impacts on conformance test
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #82 R5-191148
Athens, Greece, 25th Feb 2019 - 1st Mar 2019
Agenda Item : 5.3.8.17
Document for : Discussion and Endorsement

## Slide 2: 1. Conclusion
Introduction
  Discussion on Multi-band relaxation (MB relaxation) was kicked-off at RAN5#NR4 (Jan-2019), and LS [1] to capture RAN5 assumptions was sent to RAN4. The purpose of this contribution is to list up the impacts on conformance test by introduction of MB relaxation with assumption that RAN5 view in [1] is same as RAN4.
Conclusion
  If RAN5 adopts MB relaxation into conformance test to align core requirement completely, following difficulties will be occurred.
    Current RAN5 and GCF validation process needs to be updated.
    TCs may be categorized as Low PSD.
    MU and associated TT become much larger.
    Increase of Testing time
  Considering observations above, following proposal can be provided.
    Proposal
    RAN5 applies MB relaxation into conformance test with some optimization to reduce difficulties listed in observations. (Optimization means UE declaration, Per band limit, etc.)

## Slide 3: 2. RAN5 assumptions in [1]
ΔMBP/S is defined based on measured value.
  If sum of ΔMBP/S is lower than ΣMBP/S, UEs are regarded as 3GPP compliant (PASS).
  Only one verdict (PASS/FAIL) will be concluded for UEs.
If sum of ΔMBP/S exceeds ΣMBP/S, UEs are regarded as FAIL among all supporting FR2 bands.
Only exceeded values (> 0) are considered for MB calculation. (ΔMBP/S ≥ 0)
Regarding Note 3 (Upper limit in Band n260), if ΔMBS exceeds 0.4 dB UEs are regarded as FAIL among all supporting bands.
Multi-band test verdict is the sum of results for each band across different test points.
  e.g. Frequency ranges, CHBW, SCS etc.

## Slide 4: 3.1 Test process (Impacts on conformance test)
This section describes the impacts of applying MB relaxation into conformance test to align core completely.
Difficulity 1
  Current test process about how to conclude verdict should be updated with introduction of MB relaxation.
    Test procedure in TS 38.521-2 should be updated.
  LTE, FR1 : Verdict per operating band and test point
  NR (MB relaxation) : Only one verdict among all operating bands and test points

## Slide 5: 3.2 Low PSD issue (Impacts on conformance test)
This section describes the impacts of applying MB relaxation into conformance test to align core completely.
Difficulity 2
  UE minimum peak EIRP can be reduced up to 1.7 dB with introduction of MB relaxation, and this may lead to Low PSD issue.
  According to analysis in [2], even MOP (Min Peak EIRP, PC3, FR2a) will be regarded as Low PSD to consider power reduction by MB relaxation (1.7 dB).
Test case | Applicable Frequency Range [GHz] | Estimated SNR [dB] | UL signal level [dBm] | Required relaxation to ensure SNR=10dB
MOP (Min Peak EIRP, PC3) | 23.45GHz ≤ f ≤ 32.125 GHz | 8.8 (BW ≤ 400MHz) | 15.9dBm/ChBW (20.6 – 3 – 1.7) 1.7 : Multi-band relaxation | 1.2 - DChBW

## Slide 6: 3.3 MU, TT (Impacts on conformance test)
This section describes the impacts of applying MB relaxation into conformance test to align core completely.
Difficulity 3
  There is also impact on MU (Measurement Uncertainty) and TT (Test Tolerance) value by adopting MB relaxation.
  In case verdict is concluded among more than one band, MU and TT value for these test cases should be updated as below.
Example [MOP (Min Peak EIRP) MU (PC3, DUT ≤ 30 cm)]
UE | Supporting FR2 bands | MU [dB] | TT (= 0.65 x MU) [dB]
A | n257 (FR2a) | ± 4.30 (captured in TS 38.521-2) | 2.8
B | n260 (FR2b) | ± 4.67 (captured in TS 38.521-2) | 3.0
C | n257, n260 | ± 6.35 (= SQRT [4.302 + 4.672]) | 4.1
D | n257, n258, n260, n261 | ± 8.79 (= SQRT [4.302 + 4.302 + 4.672 + 4.302]) | 5.7

## Slide 7: 3.4 Other impacts (Impacts on conformance test)
This section describes the impacts of applying MB relaxation into conformance test to align core completely.
Difficulity 4 “Testing time”
  Testing time will also increase with MB relaxation.
  If UE supports four FR2 bands, testing time becomes four times even if vendors/operators would like to confirm verdict of specific one band.
Difficulity 5 “TE implementation”
  In order to release corresponding test cases, test equipment needs to support all FR2 bands, and it is challenging especially in early period of NR.
Difficulity 6 “GCF validation”
  GCF validation scheme needs to be updated since current Sub-WIs in GCF CAG is established per EN-DC combination (e.g. WI-500-EN-DC_1A_n78A).
  Not only 3GPP RAN5 but also GCF CAG process shall be updated with MB relaxation, and this situation absolutely lead to delay of achieving validations.

## Slide 8: 3.5 Future impact (Impacts on conformance test)
This section describes the impacts of applying MB relaxation into conformance test to align core completely.
Difficulity 7
  Impact described in 3.1 to 3.4 will become prominent in the future when the number of FR2 band increase.
    RAN5 needs to define conformance test to consider future impacts.
  Example of future impacts
    Power level decreases additionally.
    MU and TT grow larger.
    TE implementation become more complicated
    Re-validation will be required if new FR2 band is added.

## Slide 9: 4. References
[1] R5-190729
  “LS on Multi-band relaxation”, TSG WG RAN5, RAN5#4-5G-NR Adhoc (Jan-2019)
[2] R5-190460
  “SNR estimation update for FR2 priority 1 and 2 TRx TCs”, Anritsu, RAN5#4-5G-NR Adhoc (Jan-2019)