## Slide 1: FR1 TT Way Forward update
3GPP TSG-RAN WG5 Meeting #83
Reno, USA, 13th – 17th May 2019
R5-194290
Telecom Italia

## Slide 2: Background FR1
At RAN5#79 the Maximum Test System Uncertainty for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952
At RAN5#79 a Way Forward on FR1 TTs for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952 (Except the FFS items)
At RAN5#80 New FR1 MU values introduced in R5-184484 for the following TCs: 6.3.4.2, 6.3.4.3, 6.3.4.4, 6.4.2.1, 6.4.2.2, 6.4.2.3, 6.4.2.4. New TT values agreed based on the WF assumption in R5-185564
At RAN5#80 RAN5 also agreed to maintain the document until the TT for FR1 and FR2 are finalized
At RAN5 5G-AH#3 a WF for FR1 NSA in TS 38.521-3 has been agreed in R5-185657
At RAN5#81 an update has been presented in R5-187813
At RAN5 5G-AH#4 an update has been presented in R5-190940
At RAN5#82 an update has been presented in R5-192596
At RAN5 5G-AH#5 an update has been presented in R5-193481

## Slide 3: Agreed FR1 Way Forward: TT < MU
At RAN5#79 TT WF agreed in R5-183952
WF: Except the FFS Items, the proposed FR1 TT Values are included in the spreadsheet file, based on the following assumption:
  The SA FR1 TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.

## Slide 4: Agreed FR1 NSA WF TS 38.521-3
At 5G-AH#3 RAN5 agreed NSA MU in R5-185641
At 5G-AH#3 RAN5 agreed WF in R5-185657 for TS 38.521-3 FR1 EN-DC as follow:
  In case TTLTE, TTSA = 0, TTNSA to be defined as zero.
  In case MUNSA = MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.
  In case MUNSA > MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.

## Slide 5: Attached Spreadsheets update
TS 38.521-1 SA FR1 TT
  UL-MIMO MU are requested to be further analysed due to the following discussion papers as RAN5 5G AH#5
    R5-192995, R5-193057
TS 38.521-3 NSA FR1 TT
  Added the following Test Cases (RAN5 5G AH#5):
    6.2B.2.4 (R5-193451), 6.5A.2.2 (R5-193459),
    7.3B.2.3.1 7.3B.2.3.2, 7.3B.2.6.1, 7.3B.2.6.2 (R5-193500)
    7.5B.4.1 (R5-193317), 7.5B.4.2 (R5-193467)