## Slide 1: WF on TX spherical coverage noise impact
Keysight Technologies, Anritsu, Rohde&Schwarz, Ericsson
R5-197588
3GPP TSG-RAN5 #84 Meeting
Ljubljana, Slovenia, 13th – 17th May 2019

## Slide 2: Background
In RAN5#83, [1] was endorsed including the following proposal:
  Proposal 1 : MTSU for PC3 EIRP spherical coverage is defined for
  the variation of 50%-tile EIRP based on 100% correlation of MU between grids
  This conclusion was obtained through an analysis considering
  a hypothetical CDF curve for Tx spherical coverage together with the argument that quantifying the degree of correlation is practically infeasible.
In RAN5#84, several contributions were presented:
  [2] includes the following proposal and proposes noise impact based on Proposal 1 in [1] and by theoretical analysis. Proposal 2 : Define , where SNR is defined for 50%-tile core requirement taking MBR and TE noise from 2 polarization into account for EIRP spherical coverage.
  [3] also includes the following proposal:
    Proposal 1 (MU): Clarify in TR38.903 table B.3.2-5 that the assessment is made at the 50%-tile power level 11.5 dBm minus worst case MB relaxation value and assumption of a constant measurement error across grid points.
  [4,5] provides noise of impact analysis considering the above proposal
As the outcome of AP#82.22
“Acceptable assumption for CDF curve”,
2 realistic CDF curves have been provided
by UE vendors ([6], [7])

## Slide 3: Way forward
Before concluding the noise impact for Tx spherical coverage, run simulations using realistic CDF curves provided by different UE vendors ([6], [7]), similar to the ones in [1].
To be clarified whether noise impact can be considered as a constant systematic offset or if it includes some randomness
To be clarified whether the determination of the impact of noise shall be based on the minimum requirement or on the test requirement

## Slide 4: References
R5-193834, “On the MU for EIRP spherical coverage”, Anritsu, RAN5#83
R5-195688, “On the MU for EIRP spherical coverage”, Anritsu, RAN5#84
R5-196789, “Discussion on MU, TT and UE fail rate for EIRP CDF”, Ericsson, RAN5#84
R5-194623, “On Correlation of MU contributors for EIRP and EIS spherical coverage”, Rohde & Schwarz, RAN5#84
R5-194133, “On noise impact”, Keysight Technologies, RAN5#84
R5-194361, “AP#82.22 Acceptable assumption for CDF curve”, Qualcomm, RAN5#83
R5-196360, “AP#82.22 Assumption for the CDF curve”, Apple, RAN5#84