## Slide 1: Discussion on handling of HP-UE requirements in FR1
Huawei, HiSilicon, CMCC
3GPP TSG-RAN5 Meeting #86-e R5-201181
Electronic Meeting, 17 - 28 Feb 2020

## Slide 2: Background for power class related requirements
Test cases with power class specific requirements – impacted by power class directly
  MOP, MPR, A-MPR, ACLR, Configured output power
Test cases with common requirements, ran at Pumax –impacted by power class indirectly
  Relative power control, Frequency Error, EVM, OBW, SEM, SE, SE-co-existence, A-SE, Transmit intermodulation
HP-UE dropping back to PC3
  P-max <= 23dBm
  Percentage of uplink symbols > maxUplinkDutyCycle or 50% (NOTE 1)
NOTE 1: maxUplinkDutyCycle is UE capability which ranges from 60%~100%

## Slide 3
Proposal 1: All the mentioned test cases shall be tested firstly based on the UE’s power class capability. This proposal apply to FR1, FR2 and EN-DC testing.
  Below is example of test configuration in FR1:
  PC3 UE shall be verified based on 23dBm MOP; PC2 UE shall be verified based on 26dBm MOP, etc.
  Test configurations and default parameters shall ensure above requirement
    Default P-max is ‘Not present’ (Defined in 38.508-1)
    For HP-UE, the percentage of uplink symbols is less than 50% according to RMC. (Ensured by RMC definition)

## Slide 4
Proposal 2: HP UEs shall also be verified that they fall back to PC3 correctly with P-max=23dBm. MOP needs to be verified with PC3 fallback. MPR/ACLR needs to be verified with PC3 fallback but only at power levels not covered by HP-UE testing. Other test cases are not applicable. This proposal apply to FR1 and EN-DC.
  Power class in FR2 are defined based on different UE types instead of UE output power capability. There is no need for a HP-UE to fall back to any lower power class.
  In test procedure, it shall be explicitly required that HP-UE verifies PC3 requirement.
  Adding parameter exception to ensure HP-UE drops back to PC3
    P-max = 23dBm
  For FR1 the test point for PC2 falling back to PC3 shall be only DFT-s-OFDM 256QAM Outer RB allocation, and CP-OFDM 256QAM Outer RB allocation, which provide extra power level test coverage of {16.5dBm, 18.5dBm}.

## Slide 5
Proposal 3: The testing of all power classes shall be within the same test case. The effective release of each power class shall be reflected in applicability. The test of PC3 fall back shall be within the same test case.

## Slide 6
Proposal 4: HP-UE is also defined for UL-MIMO. The same principle shall apply for relevant UL-MIMO testing.

## Slide 7
Proposal 1: All the mentioned test cases shall be tested firstly based on the UE’s power class capability. This proposal apply to FR1, FR2 and EN-DC testing.
Proposal 2: HP UEs shall also be verified that they fall back to PC3 correctly with P-max=23dBm. MOP needs to be verified with PC3 fallback. MPR/ACLR needs to be verified with PC3 fallback but only at power levels not covered by HP-UE testing. Other test cases are not applicable. This proposal apply to FR1 and EN-DC.
Proposal 3: The testing of all power classes shall be within the same test case. The effective release of each power class shall be reflected in applicability. The test of PC3 fall back shall be within the same test case.
Proposal 4: HP-UE is also defined for UL-MIMO. The same principle shall apply for relevant UL-MIMO testing.
Summary