## Slide 1: RRC - RAN5#86-e (Feb-20) SA NR (Option 2)
Progress
  Maintenance of 21 RRC Test case CR’s were agreed
  NR-DC test coverage has been added in WP
  Based on below updates in TS38.508-1, CA test cases are now marked as 100% for below cases
  Note 1: No SIG test frequencies introduced in TS 38.508-1 clause 6.2.3.4 yet.
  Note 2: No NR CA FR2 Inter-band configurations defined in TS 38.101-2 yet in Rel-15 or Rel-16.
Open issues for RAN5 attention
  NR-DC test cases have dependencies on 38.508-1, might require some updates
  FR2 and FR1 power levels are missing in certain test cases
  Data path verification still needs to be added for several test cases
Frequency range | Intra-band Contiguous | Intra-Band Non-Contiguous | Inter-band
NR CA FR1 | Ready | Not Ready (Note 1) | Ready
NR CA FR2 | Ready | Not Ready (Note 1) | Not Ready (Note 2)
NR CA FR1+FR2 | N/A | N/A | Ready

## Slide 2: RRC - RAN5#86-e (Feb-20) EN-DC (Option 3)
Progress
  Maintenance of 13 RRC Test case CR’s were agreed
  Based on below updates in TS38.508-1, EN-DC with NR CA test cases are now marked as 100% for below cases
  Note 1: No SIG test frequencies introduced in TS 38.508-1 clause 6.2.3.4 yet.
  Note 2: No NR CA FR2 Inter-band configurations defined in TS 38.101-2 yet in Rel-15 or Rel-16.
Open issues for RAN5 attention
  FR2 Power levels are missing for few test cases
  Data path verification still needs to be added for several test cases
Frequency range | Intra-band Contiguous | Intra-Band Non-Contiguous | Inter-band
EN-DC with 2CC NR CA FR1 | Ready | Not Ready (Note 1) | Ready
EN-DC with 2CC NR CA FR2 | Ready | Not Ready (Note 1) | Not Ready (Note 2)
EN-DC with 2CC NR CA FR1+FR2 | N/A | N/A | Ready