## Slide 1: Protocol Test Models - RAN5#86-e (Feb-20) SA NR (Option 2)
Progress
  Initial test model added for IMS over NR/5GC.
  Handling of intra-frequency cells updated to reduce inter-cell interferences.
  Random Access Msg4 for C-RNTI based CBRA for handover updated to 144 bits TBS.
  Paging frame calculation updated to align with TS 38.508-1.
  EAP Types added to the codec requirements.
  SA NR test case execution guidelines updated
Open issues for RAN5 attention
  None.

## Slide 2: Protocol Test Models - RAN5#86-e (Feb-20) EN-DC (Option 3)
Progress
  New PIXITS added to define a 3rd set of IP addresses.
  New PIXIT added for EN-DC CA Band Combination.
  EN-DC test case execution guidelines updated.
Open issues for RAN5 attention
  None.