## Slide 1: RAN5 5G NR STATUS, DELIVERY phases and targets (FEB-20)
3GPP TSG-RAN5#86-e R5-200493
Electronic Meeting, 17th – 28th February 2020

## Slide 2: Introduction & CONTENT
The purpose of this document is to give high level status of RAN5 completed 5GS test cases and the targets for the next RAN5 5GS delivery phases.
Content
Definitions of RAN5 5GS delivery phases and target dates
FR2 Measurement Uncertainty (MU) / Test Tolerances (TT) targets
Progress - Completed deliveries
Planning content for next deliveries
  Synchronous NR-DC plan
  NSA Option 3 (EN-DC)
  SA Option 2 (SA NR)
  SA Option 5, NSA Option 4 (NE-DC), NSA Option 7 (NGEN-DC)

## Slide 3: Definitions of RAN5 5GS delivery phases and target dates
Overview: Time line - RAN5 5G NR deliveries versus RAN5 meeting
  NSA Option 3 Phase 7 and SA Option 2 Phase 6 were completed at RAN5#86-e
  Options 4 (NE-DC), 5 (SA E-UTRA/5GC) and 7 (NGEN-DC):
    An anonymous re-confirming of MNO earliest date for conformance test cases to support deployments of option 4,5 and 7 have been conducted.
    Due to the RAN5#86 meeting was changed to an electronic meeting with reduced scope the RAN5 discussion of the responses in R5-200245 was deferred to RAN5#87.
    The Phase 1 planning for options 4, 5 and 7 have, pending on the outcome of the RAN5#87 decision, been moved 3 months.

## Slide 4
FR2 Measurement Uncertainty (MU) / Test Tolerances (TT) Target Completion Update (R5-200552)

## Slide 5: Progress - Completed deliveries
SA Option 2 Phase 6 and NSA Option 3 Phase 7 were completed at RAN5#86-e
  For additional details of progress for different areas see R5-200490
Completed test cases:
  For details see attached document “5GS WP complete test cases v9.0” for details
  Completion vs FR1, FR2 and configurations with FR1 and FR2 (FR1+FR2)

## Slide 6: Synchronous NR-DC PLAN
Task | Target
Complete impacted RF/SIG work plans for synchronous NR-DC including assignment of WP TCs/Tasks | RAN5#85 (Nov-19)
Complete RRM work plan for synchronous NR-DC including assignment of WP TCs/Tasks | RAN5#86 (Feb-20)
Complete synchronous NR-DC FR1-FR2 RF/SIG test cases | RAN5#87 (May-20)
Complete synchronous NR-DC FR1-FR2 RRM test cases | RAN5#88 (Aug-20)
MNO: Mid-20, FR1-FR1 & FR1-FR2
RAN4 completion target for NR-DC RRM (TS 38.133) for NR-DC is Feb-20 (core is completed)
Out of scope of RAN5 5G/NR WI:
  NR-DC Demodulation and CSI reporting (introduced in RAN4 under a separate Rel-16 WI (NR_perf_enh)
  FR1-FR1 (no NR-DC FR1-FR1 configurations included in TS 38.101-1)
 RAN5 5G/NR WI scope: Synchronous NR-DC for FR1-FR2,

## Slide 7
Planning for next deliveries:
NSA Option 3 (EN-DC) - Phase 8 content - Target RAN5#87 MAy-20
EN-DC configurations: LTE xCC + NR FR1/FR2 yCC, where x <= 4, y <=2
Test case completion targets
  RF EN-DC test cases (38.521-3), Note 1
    Remaining not completed test cases including EN-DC FR1 (anchor-agnostic) and FR2 tests with >=2 NR CCs
  Demodulation and CSI reporting (38.521-4):
    Complete MU analysis for FR2 Demod and CSI test cases
  RRM (38.533):
    Not completed LTE+NR FR1 test cases targeted for RAN5#87 (32)
    FR2 test cases where RAN4 requirements and MU/TT completed by May-20.
  Protocol
    Layer 2: Remaining MAC test case (1)
    RRC: Remaining NR single carrier (2) and NR CA (3) test cases
    Resolve FR2 Measurement interference issues and FR2 Power levels in test cases
    IMS IR.92 EN-DC test cases, Note 2
Other targets
  Common test environment (TS 38.508-1)
    Add test frequencies for EN-DC configurations with 2CC NR non-contiguous CA for protocol testing
Note 1: EN-DC FR2 test progress dependent on MU/TT analysis completion and other open items impacting SA FR2 tests. See slide 4.
Note 2: The need for EN-DC IMS test cases on top of the existing E-UTRA IMS test cases to be decided by RAN5#87 based on IR.92 v13.

## Slide 8
SC FR1+ SC FR2 + NR CA configurations for FR1 xCC,FR2 xCC, (FR1+FR2) xCC:, where x<=4 for FR1 and x<=8 for FR2
Test case completion targets
  RF FR1 (38.521-1):
    CA test cases with 3CC and forward
    Remaining SUL and UL MIMO test cases
  RF FR2 (38.521-2):
    Not completed RF FR2 priority 1 and 2 test cases including Beam Correspondence, OBW, ACLR, Spurious co-existence and Rx Spurious. Note 1.
    Not completed RF FR2 priority 3 test cases including MU/TT (TS 38.521-3)
  RF FR2 (38.521-3):
    Synchronous NR-DC RF FR1+FR2 test cases
  Demodulation and CSI reporting (38.521-4):
    Complete MU analysis for FR2 Demod and CSI test cases. See Note 1.
  RRM (38.533): Note 1
    Remaining FR1 test cases targeted for RAN5#87 (13)
    FR2 test cases where RAN4 requirements and MU/TT completed by Feb-20. See Note 1.
  Protocol test cases (34.229-5, 38.523-1):
    Layer 2: Remaining not completed MAC NR-DC (1), MAC single carrier (3) and PDCP test cases (4)
    RRC: Remaining NR single carrier (11), NR CA (14) and Synchronous NR-DC FR1+FR2 (11) test cases
    RRC: Resolve interference issues in FR1 measurement Intra-Freq test cases and complete FR2 power levels
    Idle mode: Resolve and update FR1 and FR2 power levels; and complete remaining test cases (4)
    Multilayer/Services: Remaining IMS Emergency services (3), EPC Fallback (2) and UAC (6) test cases.
    IMS: Current IMS content for IMS over 5GS to be moved to new TS 34.229-5 and additional test cases introduced.
  Other targets
    Complete RRM work plan for synchronous NR-DC including assignment of WP TCs/Tasks
    Common test environment (TS 38.508-1)
      Complete generic test procedure for synchronous NR-DC
      Add test frequencies for synchronous NR-DC and protocol testing
    Submit TS 34.229-5 on IMS over 5GS for RAN one-step-approval
Note 1: RF/Demod/RRM FR1 priority 1 test cases are test cases with only RAN5 dependencies, i.e. completed in RAN4 by March-19. RF/Demod/RRM FR1 priority 2 test cases are test cases not completed in RAN4 by March-19 (RF/Demod/RRM priorities as agreed at RAN5#82, ref: R5-192832).
Note 2: See slide 6 for MU/TT targets and definition of RF FR2 priority 1, 2 and 3 test cases.
Planned content:
SA Option 2 (SA NR) - Phase 7 - Target RAN5#87 MAY-20

## Slide 9
FFS. See slide 3 for further details
Planned content:
SA Option 5 (SA E-UTRA) - Phase 1 - Target RAN5#88 (AUG-20)

## Slide 10
FFS. See slide 3 for further details
Planned content:
NSA Option 4 & 7 (NE-DC & NGEN-DC) - Phase 1 - Target RAN5#88 (AUG-20)