## Slide 1: Discussion on testing of 4Rx vs 2Rx in FR1
Huawei, CAICT, OPPO, Samsung, Bureau Veritas, Sporton, Ericsson, Anritsu, AT&T, CMCC, Dish, Telecom Italia, Orange, Rohde&Schwarz
3GPP TSG-RAN5 Meeting #87-e R5-202811
Electronic, 18 - 29 May 2020

## Slide 2: Background
In TS 38.101-1 2Rx requirements are defined for all bands.
4Rx requirements are defined for a few bands as indicated in Table 7.3.2-2
If a UE supports 4Rx in a certain band, it’s required to be tested against both 2Rx and 4Rx requirements, including single carrier, CA and EN-DC
Testing both 2Rx and 4Rx requirements will lead to doubled testing time. Considering large amount of CA and EN-DC configurations, the workload can’t be ignored.

## Slide 3: Discussion 1 (3-1)
In 38.101-4, it’s clearly indicated if UE supports 4Rx, 2Rx testing is skipped.
4Rx requirements
2Rx requirements

## Slide 4: Discussion 1 (3-2)
For LTE Rx testing, a similar principle of skipping 2Rx testing is defined in section 7.2 of TS 36.101.
In addition, as per TS 36.521-2, 2Rx REFSENS is tested only in 2Rx bands, and 4Rx REFSENS is tested in 4Rx bands.
Same principle can be adopted in NR RF Rx testing for SA.
Proposal 1: 2Rx RF requirements can be skipped for all Rx test cases except for single carrier REFSENS on the bands that UE is equipped with 4Rx in FR1 SA.

## Slide 5: Discussion 2
For NSA testing, the combination of antenna numbers of LTE and NR needs to be considered.
  For test cases where LTE anchor agnostic approach applies, LTE link serves only as anchor and not measured.
    The maximum number of antenna ports of each band need be tested on NR carrier.
  For test cases where LTE anchor agnostic approach doesn’t apply, both LTE and NR carrier need to be measured.
    For all the Rx test cases only the combination of ‘max Rx LTE + max Rx NR’ need to be tested
    Proposal 2: Specify the test principle of NR NSA as in below table
 | NR NSA (LTE Anchor Agnostic) (38.521-3) | NR NSA (not LTE Anchor Agnostic) (38.521-3)
All Rx test cases | Maximum Rx on each NR CC | Maximum Rx on each LTE CC and each NR CC

## Slide 6: Proposals
Proposal 1: 2Rx RF requirements can be skipped for all Rx test cases except for single carrier REFSENS on the bands that UE is equipped with 4Rx in FR1 SA.
Proposal 2: Specify the test principle of NR NSA as in below table
 | NR NSA (LTE Anchor Agnostic) (38.521-3) | NR NSA (not LTE Anchor Agnostic) (38.521-3)
All Rx test cases | Maximum Rx on each NR CC | Maximum Rx on each LTE CC and each NR CC