## Slide 1: WF on SA 2Tx and NSA PC2
Huawei, [Anritsu, CMCC, Dish, Ericsson, Keysight, OPPO, Qualcomm, Rohde&Schwarz, Samsung]
3GPP TSG-RAN5 Meeting #88-e R5-204729
Electronic, 17 – 28 August 2020

## Slide 2: Background
Discussion on SA 2Tx and NSA PC2 has been carried out in RAN5 for several meetings, in order to facilitate definition of RAN5 test method and TE implementation, the WF of SA 2Tx and NSA PC2 is discussed and captured in this document.

## Slide 3: WF on Rel-16 EN-DC PC2
RAN4 has discussed on ambiguity on the available power on individual carriers when the UE is configured with an MR-DC configuration.
An LS RP-201392 was sent to RAN2 to ask RAN2 to develop new power class UE capability signalling applicable for the NR part of the MR-DC band combination.
Contents of RAN2 CR R2-2008077 and R2-2008078 are agreed, and the changes would be merged into RAN2 big CR and get agreed.
Draft CR R4-2010809 is likely to be agreed with possible updates to align with RAN2 CR.
Proposal 1: Contents in attached ‘draft 38.521-3 CR for Rel-16 EN-DC PC2’ is endorsed, which can be leveraged for TE designation.

## Slide 4: WF on Rel-16 2Tx requirements
Rel-16 2Tx requirements are being investigated in RAN4. It is discussed in RAN5 how to introduce the 2Tx requirements. Two possible options are:
  Option a: Rel-16 requirements of 2Tx shall be added in a separate test case.
  Option b: Rel-16 2Tx requirements can reuse current Rel-15 test case by making necessary changes. Concept of “branch” or “feature” needs to be considered in 38.522 to indicate the test case needs to be validated for 1Tx and 2Tx separately.
Proposal 2: Option b) is considered as default approach. Option a) can be adopted with proper justification per test case basis.

## Slide 5: WF on Rel-16 2Tx requirements (contd.)
RAN4/RAN2 are not going to introduce new UE capability for supporting 2Tx antenna connectors.
In conformance testing, the information of UE capability of 1Tx or 2Tx is required for selection of proper test branch.
Proposal 3: UE’s capability of 1Tx or 2Tx is declared during conformance testing. Contents in attached ‘draft 38.508-2 CR for Rel-16 2Tx’ is endorsed, which can be leveraged for TE designation.

## Slide 6: WF on Rel-16 2Tx requirements (contd.)
RAN4 has agreed with the power measurement method for 2Tx requirements with the understanding:
  Measure the power and emissions per connector and then sum them up afterwards
No other open issue related to MOP remains in RAN4.
Proposal 4: Contents in attached ‘draft 38.521-1 CR for Rel-16 2Tx’ is endorsed, which can be leveraged for TE designation.

## Slide 7: Conclusion
For Rel-16 EN-DC
Proposal 1: Contents in attached ‘draft 38.521-3 CR for Rel-16 EN-DC PC2’ is endorsed, which can be leveraged for TE designation.
For Rel-16 2Tx requirements
Proposal 2: Option b) is considered as default approach. Option a) can be adopted with proper justification per test case basis.
Proposal 3: UE’s capability of 1Tx or 2Tx is declared during conformance testing. Contents in attached ‘draft 38.508-2 CR for Rel-16 2Tx’ is endorsed, which can be leveraged for TE designation.
Proposal 4: Contents in attached ‘draft 38.521-1 CR for Rel-16 2Tx’ is endorsed, which can be leveraged for TE designation.