## Slide 1: 3GPP RAN5 #90-e 22-Feb to 05 Mar 2021 R5-210823 Summary of known issues for NR RRM Test cases in 38.533

## Slide 2: Current status
Anritsu said we would provide status and summary of open issues
This summary is a snapshot of the issues we are aware of
  it does not claim to be comprehensive
  many of the issues identified require work in both RAN4 and RAN5
  other issues may not have revealed themselves yet
Some companies in RAN4 are already working on some topics
  some CRs at RAN4#98-e addressed issues across multiple test cases
  ..but scope of work not visible, usually learnt when CRs uploaded
Some issues only identified when RAN5 implements test cases
  Either from TT analysis, or from TE vendor/UE vendor trials

## Slide 3: Known FR1 Test Case issues
Status based on Rel-15 test cases after RAN4#98-e, Feb 2021
Known issue | Test types | RAN4 status | RAN5 status | Comments
“Flatness” MU not applicable to RRM | RLM, BWP switch, Interruption | Not applicable | RLM resolved | BWP switch, Interruption need TT analysis update
FR1 link capability in FR1+FR2 test cases | Various | Unresolved | Unresolved | Test feasibility of some FR1+FR2 test cases needs review.

## Slide 4: Known FR2 Test Case issues
Status based on Rel-15 test cases after RAN4#98-e, Feb 2021
Known issue | Test types | RAN4 status | RAN5 status | Comments
Angle of Arrival or Beam type undefined | Various | Most done | Unknown | New-introduced RAN4 test cases may forget
Angle of Arrival gives insufficient dB range | CSI-RS based RLM | Unresolved | Unresolved | Change to Rx Beam peak in RAN4?
Full 66RBs gives insufficient dB range | Various | Some unresolved | Some unresolved | Reduce allocation to 24RBs for 120kHz SCS
Parameters don’t fit 240kHz SSB SCS | Various | Most unresolved | Most unresolved | Review each test case with 240kHz SSB SCS
Angle of Arrival/dB values incompatible | Various | Needs research | Unknown | Some progress in RAN4, resolvable
Set uplink power to defined target value | Random Access | N/A? | Not started | Any already-used methods for RF test?
Absolute thresholds /large UE gain range | Various | Needs research, not started | Unknown | Use RSRP calibration, like signalling tests?
Handling of 2 Angles of Arrival from 1 cell | RLM, TCI state switch | Needs research | Unknown | Define time-division multiplexing, like RLM?

## Slide 5: Thoughts on Way Forward
Most issues need targeted research to find out scope
  Which test cases affected, how many, common solution available?
Most issues have a solution already applied to at least one test
  Careful check needed to see whether it can be applied to other TCs
  ..for example, 240kHz SSB SCS Configs may be harder than 120kHz
  ..may require a “very draft” TT analysis to check feasibility
Does RAN5 want to actively manage the process?
  RAN5 has best tools and good visibility/experience across test cases
  Would companies be willing to “own” issues?
Higher frequency FR2 bands
  May affect all RRM Test cases (worse Refsens, increased path loss, higher MU..) and hence more pressure on already-tight dB range