## Slide 1: RAN5 5G NR FR2 Test Tolerance review training
3GPP TSG-RAN5#90-e R5-211207
Electronic Meeting, 22nd Feb – 05th March 2021

## Slide 2
Content of this document
  Basic information.
  Review of the analysis for a test case 5.7.1.1 focusing on .xls file.
The document focus is on .xls file.
This document covers technical aspects of TT review
  FR2 Test Tolerance review process is covered in R5-204848.
The FR2 Test Tolerance framework is based on FR1 which is covered in R5-211206. Most of the principles are the same. This document focuses on differences. It is advised to read R5-211206 first, followed by this document to get the understanding of both FR1 and FR2 TT analysis.
Scope
  This training covers an example RRM Test Case in 38.533, with the analysis stored in TS 38.903.
  The chosen test case is 5.7.1.1 – intra-frequency measurement accuracy.
  At the time of creating this document no formally agreed FR2 TT is completed. TT analysis used as example is draft which contains the main features for the test cases covered.
OVERview (1/2)

## Slide 3
A few parameters are required to define a Test Case in 38.133 Annex A – similar as in FR1.
Main differences here are additional rows (i.e. Angle of arrival configuration and Assumptions on UE beams).
Additionally, Es/Iot is specified at UE baseband, including the effect of UE internal noise.
In this particular case in time phase T2 no artificial noise is transmitted, thus Noc and Es/Noc in T2 are N/A. Only Es is considered a settable parameter in such case.
Section a) Original specified key parameters
(1/4)

## Slide 4
In this particular case, not to overcomplicate already complicated tables, it was decided to split the time phases T1 and T2 on separate tabs.
For time phase T1: Parameters highlighted on previous slide (Noc and Es/Noc) go directly to Test system part of section a) of the analysis .xls
Some other parameters such as subcarrier spacing, allocated RBs, channel bandwidth are also displayed in section a) as later are used during calculations. This is aligned with the approach used in FR1.
Main difference comparing to FR1 here are:
  Separation of time phases T1 and T2 using two different tabs.
  More parameters introduced to section a) of the worksheet as more will be needed for further calculations
  Introduction of parameters relating to the OTA nature of testing such as Angle of Arrival and RX Beam assumption which are needed in further calculations.
Section a) Original specified key parameters
(2/4)

## Slide 5
Similar excersice is done for time phase T2
Parameters highlighted on previous slide (Es) go directly to Test system part of section a) of the analysis .xls
Section a) Original specified key parameters
(3/4)

## Slide 6
Additionally, there are number of parameters in UE part of section a) which will be needed in further calculations (e.g. UE internal noise).
The parameters are per band and the source of each value is given in the comment section.
The same values apply for both time phases T1 and T2
Modelling of variation within spherical coverage directions explained in TS 38.903 in Annex A.2.1.2
Modelling of Fine beams and Rough beams is explained in TS 38.903 in Annex A.2.2.2
UE gain is explained in TS 38.903 in Annex A.2.6
Section a) Original specified key parameters
(4/4)

## Slide 7
Other parameters are derived in section b) of the spreadsheet – same as for FR1
To check if they have been correctly calculated by RAN4
Some additional parameters needed for the analysis are also derived
Section B) Derived parameters for T1 (1/4)

## Slide 8
Some additional parameters needed for the analysis are also derived
UE gain G midpoint
  The UE Gain from the reference point (where test case parameters are specified) to the SS-RSRP measurement point is specified in TS 38.133 clause B.2.1.5
UE Spherical coverage gain midpoint.
  greyed out as in this case AoA is Rx Beam peak
  UE Spherical coverage gain midpoint in dB is derived as (UE Refsens - UE Spherical coverage)/2
  More details in 38.903 A.2.1.2
Section B) Derived parameters for T1 (2/4)

## Slide 9
UE internal noise at the reference point
  Calculation method is explained in TS 38.903 A.2.3
  Relevant parameters used in calculations are listed in section a)
Section B) Derived parameters for T1 (3/4)

## Slide 10
Methods for deriving the parameters in section b) in FR2 follow the same principles as in FR1
Main differences:
  Including UE internal noise
  Es/Iot at UE baseband
  UE-measured SS-RSRP include the effect of UE gain and UE spherical coverage variation gain (only for spherical coverage AoA). In this case AoA is UE Rx Beam peak so spherical coverage midpoint is 0 in below example:
Section B) Derived parameters for T1 (4/4)

## Slide 11
Parameters derived in section b) of time phase T2 tab of the spreadsheet follow the same principles and calculation methods as those used in T1 tab and will be skipped in this presentation.
From now we will focus on time phase T1 only.
Section B) Derived parameters for T2

## Slide 12
Test system uncertainties for FR2 follow the same principles as those for FR1…
… except that for now some values are provisional (not yet agreed)
  (i.e. Average Noc, Es level, Es relative)
… and that UE gain and spherical coverage gain variations are specified as UE uncertainties in section c)
Section c) uncertainties

## Slide 13
Parameters in section d) follow the same principles as those for FR1…
… with additional UE uncertainties caused by spherical coverage and UE gain variations
Section d) controlled parameters critical to verdict
  - In Rx Beam peak direction spherical coverage variation does not apply (greyed out, sensitivity factor =0)
  - UE gain cancels out for Cell 2 – Cell 1 SS-RSRP measurements when both cells are from the same direction.
  - More details on UE Reported RSRP and UE gain in TS 38.903 Annex A.2.6
UE-related values have been added arithmetically to the overall uncertainty, as each could be systematic not random.

## Slide 14
In this section applied test tolerance value are explicitly called
… same as in FR1, this part of the spreadsheet is usually filled at the end
Section e) determine parameters to offset

## Slide 15
In section f) original specified key parameters from section a) are listed again
Applied offset field is used to make provision of applied Test Tolerance and calculate new value, the same as in FR1.
Section f) parameters modified by test tolerances

## Slide 16
Same as for FR1, list again the Controlled parameters critical to verdict, this time using the uncertainties from d) to calculate the Min and Max values:
Uncertainty values are per-controlled-parameter, and per-band. They are copied directly from section d)
Offsets in section f) are adjusted and Min / Max values in section g) are compared against the conditions listed in the comment section
Section g) Check controlled parameters Min/Max

## Slide 17
When the solution has been found it is summarized here in section e)
The solution is often found by trial and error, sometimes after many iterations
The aim is to use the smallest offset needed to meet all requirements
Back to Section e) determine parameters to offset

## Slide 18: Rest of the procedure
The analysis .doc
Applied Test Tolerances in 38.533
Test case grouping in 38.903
… all follow the same principles as for FR1 and will be skipped in this presentation.