## Slide 1: RAN5 5G NR FR1 Test Tolerance review training
3GPP TSG-RAN5#90-e R5-211206r1
Electronic Meeting, 22nd Feb – 05th March 2021

## Slide 2
The analysis always includes text document
  .doc file with written explanation of the analysis process
In most cases it contains also accompanying spreadsheet
  .xls file with all necessary calculations
  One document can contain more than one sheet if necessary – for sub-test with different values
  Each calculation sheet is divided into sections a) – g) matching corresponding sections in .doc for easier reading
…And sometimes graphs
  .vsd file, only when necessary
The above 1-3 files are zipped together and form the TT analysis
  Zip file naming example: 38.533 6.1.1.1 TT.zip
TT analysis in form of a zip file is then attached to a CR to 38.903
  Using following text in CR body
    ” Add the following attached .zip file to TR 38.903 Annex A:
    “38.533 6.1.1.1 TT.zip”
OVERview (1/2)

## Slide 3
Content of this document
  Why do we need an analysis
  Review of the analysis for a simple intra-frequency re-selection test case 6.1.1.1
  High level summary of the analysis .doc
  Test Tolerances in 38.533
  Test Case Grouping in 38.903
The document focus is on .xls file
This document covers technical aspects of TT review
  FR1 Test Tolerance review process is covered in R5-192615
OVERview (2/2)

## Slide 4
A few parameters are required to define a Test Case (in 38.133 Annex A)
These parameters go directly to section a) of the analysis .xls
All settable parameters are marked with pale yellow color in the excel. Those are ones that need to be filled, the rest calculates automatically.
The thin diagonal pattern shows cells that differ between different configurations for the test case.
  It is to remind to change those parameters when creating new tab by copying for other test configuration
Section a) Original specified key parameters

## Slide 5
Other parameters are derived in section b) of the spreadsheet
To check if they have been correctly calculated by RAN4
Some additional parameters needed for the analysis are also derived
Section B) Derived parameters (1/3)

## Slide 6
Example of derivation for absolute linear power:
Example of derivation for Es/Iot:
Section B) Derived parameters (2/3)

## Slide 7
Why do we need to derive parameters?
  Absolute power in linear units is needed to calculate Es/Iot and to calculate sensitivity factors in the spreadsheet section d)
  Some parameters need to stay within side conditions defined in 38.133
  Some core requirement apply to the parameters which are not given directly in the test case. For example, in re-selection test cases, we need to derive SS-RSRP difference between cells to check if it fulfils the “better ranked” condition specified in 38.133 clause 4.2.2.3.
Section b) Derived parameters (3/3)

## Slide 8
Test system uncertainties apply to original specified parameters (from section a)
… and match the values in 38.533 Annex F
The uncertainties are orthogonal to each other and form a minimum set.
  Superposition and other principles used in TT analysis can be found in 38.903 clauses 4 and 5
Derived parameters from section b) do not need uncertainties in section c)
Section c) uncertainties

## Slide 9
Define the parameters that are critical to the verdict by study of the test case and by careful reading of the relevant clauses in TS 38.133
Section d) controlled parameters critical to verdict (1/4)

## Slide 10
Calculate the sensitivity factor
  Sensitivity factor is defined as the ratio of how the parameters critical to verdict are affected by the parameters that are set by the test equipment,
  In other words, how sensitive each parameter is to each test equipment uncertainty
Section d) controlled parameters critical to verdict (2/4)
The sensitivity of Cell 1 Es/Iot to Noc (AWGN) is 0
The sensitivity of Cell 1 Es/Iot to Cell 1 Es/Noc is 1.000
The sensitivity of Cell 1 Es/Iot to Cell 2 Es/Noc is 0.975, = (interference from Cell 2/Total interference) = 6.310/(6.310+0.158)
In many RRM test cases sensitivity can be derived by inspection and equals to zero or one
Sometimes, like in case of sensitivity of Cell 1 Es/Iot to Cell 2 Es/Noc the value is an intermediate value and pie-chart can be useful to illustrate it
The sensitivity factors are differentiated per-controlled-parameter, per-uncertainty, and per-time-period

## Slide 11
For each controlled parameter, in each time period, multiply each uncertainty by its sensitivity factor
The result is how much effect the uncertainty will have on the controlled parameter. Example for T2
  Cell 1 Es/Iot has a sensitivity factor of 0 to AWGN Noc uncertainty. So (+/-1dB x 0) = 0dB
  Cell 1 Es/Iot has a sensitivity factor of 1 to Cell 1 Es/Noc uncertainty. So (+/-0.3dB x 1) = 0.3dB
  Cell 1 Es/Iot has a sensitivity factor of 0.975 to Cell 2 Es/Noc uncertainty. So (+/-0.3dB x 0.975) = 0.293dB
Section d) controlled parameters critical to verdict (3/4)

## Slide 12
Sum the effects of all the uncertainties
Uncertainties are normally added root-sum-square, as they are statistical 90% confidence values.
The overall uncertainties are per-controlled-parameter and per-time-period
Section d) controlled parameters critical to verdict (4/4)

## Slide 13
In this section applied test tolerance value are explicitly called
This part of the spreadsheet is usually filled at the end
  After trying out values in section f) and checking the values in section g) to determine weather the conditions were met
Section e) determine parameters to offset

## Slide 14
In section f) original specified settable key parameters from section a) are listed again together with re-derived parameters
Applied offset field is used to make provision of applied Test Tolerance and calculate new value (value modified by Test Tolerance)
Section f) parameters modified by test tolerances (1/2)

## Slide 15
All parameters from section b) are now re-derived using values modified by Test Tolerance
The same selection of parameters as in section b)
The same calculations methods…
…different values if any offset was applied
Section f) parameters modified by test tolerances (2/2)

## Slide 16
List again the Controlled parameters critical to verdict, this time using the uncertainties from d) to calculate the Min and Max values:
Uncertainty values are per-controlled-parameter, and per-time-period. They are copied directly from section d)
Section g) Check controlled parameters Min/Max (1/4)

## Slide 17
Determine the requirements for each parameter
Section g) Check controlled parameters Min/Max (2/4)
The thin diagonal pattern shows cells that differ between different configurations for the test case.
  It is to remind to change those parameters when creating new tab by copying for other test configuration

## Slide 18
Adjust the offsets applied in section f) and check values Min / Max values in section g) if the core requirements are met
  In Test Case 6.1.1.1 for example if all offset values were set to 0dB
  The minimum RSRP difference between Cell 1 and Cell 2 is not big enough to meet the “3dB better ranked” requirement, and a good UE could fail the Test Case
Section g) Check controlled parameters Min/Max (3/4)

## Slide 19
Sometimes the amount of offset can be calculated from the uncertainty
  For example, the offset is made equal to the (Cell 2 SS-RSRP – Cell 1 SS-RSRP) uncertainty:
  But this is a rare case. Most of the times the offset is found by trial and error and watching section g) carefully
Section g) Check controlled parameters Min/Max (4/4)

## Slide 20
When the solution has been found it is summarized here in section e)
The solution is often found by trial and error, sometimes after many iterations
The aim is to use the smallest offset needed to meet all requirements
Back to Section e) determine parameters to offset

## Slide 21
Content of the word document
  Includes an extract of the Test Case copied from TS 38.133 Annex A
  Includes explanation of the uncertainty values
  Includes relevant Core requirement and side condition extracts from TS 38.133 and/or other specs when necessary
  Often includes additional diagrams to explain the reasoning
  Often includes information about differences/similarities across the sub-test cases covered by the analysis
  Often includes information about differences/similarities across the other test cases covered by the analysis
The analisys.doc

## Slide 22
Test Tolerance calculated in TT analysis must match what can be found 38.533 in Annex F
… and in the test case
Test tolerance values 38.533

## Slide 23
Test cases sharing one TT analysis are added one group into 38.903 Clause 8 Grouping of test cases defined in TS 38.533
v2 in the zip file name means that this is already second version of the analysis
  Every time TT analysis is for any reason updated, “v” is incremented
  versions in the zip file attached to 38.903 and the one in the grouping table need to match
Test case grouping in 38.903