## Slide 1: Discussion on how to handle test coverage across 5G NR connectivity options
CMCC, Deutsche Telekom, MCC TF160, Orange
3GPP TSG-RAN5 Meeting #93-e R5-217993
Electronic Meeting, 8 – 19 November 2021
0
0

## Slide 2: Background - SA2 TS 23.501 (1/5)
In Section “3.1 Definitions” of TS 23.501 [1], there is clear definitons of “NG-RAN”:
Observation 1: There are definitions of “NG-RAN” which connects to 5GC in 3GPP core specifications , and it includes so-called “Option 2”, “Option 4”, “Option 5” and “Option 7”.
It can be interprepted as below:
1) Standalone New Radio >>> Option 2
2) New Radio is the anchor with E-UTRA extensions >>> Option 4
3) Standalone E-UTRA >>> Option 5
4) E-UTRA is the anchor with New Radio extensions >>> Option 7

## Slide 3: Background - RAN2 TS 37.340 (2/5)
In Section “4.1.2 MR-DC with the EPC” and “4.1.3 MR-DC with the 5GC” of TS 37.340 [2], there are clear descriptions of “MR-DC” as well as “EN-DC”, “NGEN-DC”, “NE-DC” and “NR-DC”:
Observation 2: There are definitions of “MR-DC” as well as “EN-DC”, “NGEN-DC”, “NE-DC” and “NR-DC” in 3GPP core specifications. Although it can be inferred that “EN-DC = Option 3”, “NE-DC = Option 4” and “NGEN-DC = Option 7”, but there are no formal definitions of “Option X” in 3GPP specifications.

## Slide 4: Background - RAN2 TS 38.331 (3/5)
In Section “3.2 Abbreviations” of TS 38.331 [3], there are clear definitions of “EN-DC”(Option3), “E-UTRA/5GC”(Option5), “E-UTRA/EPC”(Option1), “NE-DC”(Option4), “NR/5GC”(Option2) and “NGEN-DC”(Option7).
Observation 3: The definitions of “EN-DC”(Option3), “E-UTRA/5GC”(Option5), “NE-DC”(Option4), “NR/5GC”(Option2) and “NGEN-DC”(Option7) in TS 38.331 go well with the definitions in Section “3.1 Definitions” of TS 23.501 [1] as well as in Section “4.1.3 MR-DC with the 5GC” of TS 37.340 [2].
Option3
Option5
Option4
Option2
Option7
Option1

## Slide 5: Background - RAN5 TS 38.508-1 (4/5)
Observation 4: “NR” in TS 38.508-1[4] means “NR/5GC”(Option2) in TS 38.331[3].
“E-UTRA/5GC”(Option5), “EN-DC”(Option3), “NGEN-DC”(Option7), “NE-DC”(Option4) and “E-UTRA/EPC”(Option1) have been used in Section “4.5 Generic procedures” of TS 38.508-1 [4], well aligning with the Abbreviations of TS 38.331 [3].
Only “NR” is NOT aligned with the Abbreviation “NR/5GC”(Option2) in TS 38.331 [3].

## Slide 6: Background - RAN5 TS 38.521-4 (5/5)
Observation 5: “NSA” in TS 38.521-4 can not match the descriptions in TS 38.508-1[4].
There are no consensus reached on which connectivity options should belong to “NSA”.
There are “NSA” wording in the test cases of TS 38.521-4. And the “test description” of TS 38.521-4 has suggested readers to check TS 38.508-1 clause 4.5 for “NSA” to implement the test. However, there are only specific connectivity options (EN-DC, NE-DC, NGEN-DC...) list in TS 38.508-1 clause 4.5 rather “NSA”.
Notes: TC titles as well as in the “test description” of

## Slide 7: Proposals
Proposal 1: To clarify the wording of “Option 2” into “NR/5GC” in RAN5 documents to align with 3GPP core specifications.
Proposal 2: To clarify the wording of “Option 3” into “EN-DC” in RAN5 documents to align with 3GPP core specifications.
Proposal 3: To clarify the wording of “Option 4” into “NE-DC” in RAN5 documents to align with 3GPP core specifications.
Proposal 4: To clarify the wording of “Option 5” into “E-UTRA/5GC” in RAN5 documents to align with 3GPP core specifications.
Proposal 5: To clarify the wording of “Option 7” into “NGEN-DC” in RAN5 documents to align with 3GPP core specifications.
Proposal 6: To clarify the wording of “Option 1” into “E-UTRA/EPC” in RAN5 documents to align with 3GPP core specifications.
Proposal 7: To clarify the wording of “SA” into specific connectivity options (e.g. “NR/5GC” or “E-UTRA/5GC”) in RAN5 documents to avoid confusion. “SA” in the test case title can be kept as it is if the clarifications to be made in the test case applicability.
Proposal 8: To clarify the wording of “NSA” into specific connectivity options (e.g. “MR-DC” or “EN-DC” or “NE-DC” or “NGEN-DC”) in RAN5 documents to avoid confusion. “NSA” in the test case title can be kept as it is if the clarifications to be made in the test case applicability.

## Slide 8: Reference
[1] TS 23.501 V16.10.0 (2021-09) 3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; System architecture for the 5G System (5GS); Stage 2(Release 16)
[2] TS 37.340 V16.7.0 (2021-09) 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA) and NR; Multi-connectivity; Stage 2(Release 16)
[3] TS 38.331 V16.6.0 (2021-09) 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; NR; Radio Resource Control (RRC) protocol specification (Release 16)
[4] TS 38.508-1 V17.2.0 (2021-09) 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; 5GS; User Equipment (UE) conformance specification; Part 1: Common test environment (Release 17)

## Slide 9: Thank you!