## Slide 1: Discussion on test procedure for SCell drop issue
Anritsu
3GPP TSG-RAN5 Meeting #94-e
Online, 21st Feb – 4th Mar 2022
R5-220889

## Slide 2: Introduction
There are 2 options to solve the SCell drop issue based on R5-218400 [1].
Option 1: Use TPC to limit PCell Power
Applicable from Rel.15 but additional analysis needed for testability items
Implementation to TS 38.521-2 was shown in R5-218399 [2]
Option 2: Use Conformance Test Function to apply limit on PCell Power
Potentially simplifying procedure but applicable from Rel.16
Implementation to TS 38.521-2 was shown in R5-217652 [3]
There is a concern with the procedure of Option 1.
If all CCs power are controlled by power window Pw, it cannot be guaranteed that UE transmits the maximum output power.
It is because Pw has a range caused by UE’s power step tolerance and TE’s uncertainty (MU).

## Slide 3: Concern with limitting CCs by TPC command
CCs are controlled to within Pcmax – Xmax +/- Pw/2.
Total power at step 8 could be different from step 6.
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
6. PCell reaches to Pcmax by TPC up but SCells drop.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
7. PCell is reduced to within Pcmax – Xmax +/- Pw/2.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
8. SCells are increased to within Pcmax – Xmax +/- Pw/2.
Pw
Pw
Test procedure in R5-218399:
6. Send continuously uplink power control "up" commands in every uplink scheduling information to the UE; allow at least 200 msec starting from the first TPC command in this step to ensure that the UE transmits at its maximum output power PUMAX. Allow at least BEAM_SELECT_WAIT_TIME (NOTE 1) for the UE Tx beam selection to complete.
7. Send uplink power control “down” commands on PCell in every uplink scheduling information to the UE; Proced until power control has reduced the UE output power by Xmax,i,PCell dB (defined in clause 6.2A.2.4)from PCMAX. Target power on TE shall be PCMAX minus Xmax,i,PCell.
8. TE shall send uplink power control “up” commands on SCell only until power on the secondary component carrier equals the target power set on TE defined as (PCMAX minus Xmax,i,PCell).

## Slide 4: Proposal for the test procedure – Option 1A
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
6. PCell reaches to Pcmax by TPC up but SCells drop.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
7. PCell is reduced to within Pcmax – Xmax +/- Pw/2.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
8. SCells are increased to their maximum output power.
Pw
Pw
Test procedure:
6. Send continuously uplink power control "up" commands in every uplink scheduling information to the UE; allow at least 200 msec starting from the first TPC command in this step to ensure that the UE transmits at its maximum output power PUMAX. Allow at least BEAM_SELECT_WAIT_TIME (NOTE 1) for the UE Tx beam selection to complete.
7. Send uplink power control “down” commands on PCell in every uplink scheduling information to the UE; Proceed until power control has reduced the UE output power by Xmax,PCell dB (defined in clause 6.2A.2.1.4) from PCMAX. Target power on TE shall be (PCMAX minus Xmax,PCell).
8. Send continuously uplink power control “up” commands on every SCell in every uplink scheduling information to the UE; allow at least 200 msec starting from the first TPC command in this step to ensure that the UE transmits at its maximum output power PUMAX. Allow at least BEAM_SELECT_WAIT_TIME (NOTE 1) for the UE Tx beam selection to complete.
Total power at step 8 can be the same as step 6 by continuously sending TPC “up” to SCells.

## Slide 5: Proposal for the test procedure – Option 1B
Xmax
PCell
Pcmax
9. Each Cell is sequentially increased in order from the lowest one, until total output power reaches Pcmax.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
At last, all Cells are at similar levels around Pcmax – Xmax.
Test procedure:
6. Send continuously uplink power control "up" commands in every uplink scheduling information to the UE; allow at least 200 msec starting from the first TPC command in this step to ensure that the UE transmits at its maximum output power PUMAX. Allow at least BEAM_SELECT_WAIT_TIME (NOTE 1) for the UE Tx beam selection to complete.
7. Send uplink power control “down” commands on PCell in every uplink scheduling information to the UE; Proceed until power control has reduced the UE output power by Xmax,PCell dB (defined in clause 6.2A.2.1.4) from PCMAX. Target power on TE shall be between (PCMAX minus Xmax,i,PCell) and (PCMAX minus Xmax,i,PCell minus PW).
8. Send uplink power control “up” commands on SCell only until power on the secondary component carrier is less than the target power set on TE defined as (PCMAX minus Xmax,i,PCell).
9. Send uplink power control “up” commands on PCell and SCells in order from the Cell with the lowest level using 1dB power step size, until the total output power is not increased by command sending to ensure that the UE transmits at its maximum output power PCMAX.
Xmax
SCell
(1)
PCell
SCell
(2)
SCell
(3)
Pcmax
8. All CCs are controlled to be within Pcmax – Xmax – Pw.
Pw
SCell
(3)
SCell
(1)
SCell
(2)
1
4
2
3
5
Pw
Pw

## Slide 6: Summary
Proposal 1: Improve the test procedure by adopting either of the following options if it is agreed to use Option 1 for SCell drop issue.
Option 1A
Procedure: Send TPC up to ensure PUMAX
-> Send TPC down to set PCell to (PCMAX – XMAX)
-> Send TPC up to set SCell to (PCMAX – XMAX)
The procedure is simpler than Option 1B, but there could be additional SCell drop issue.
Option 1B
Procedure: Send TPC up to ensure PUMAX
-> Send TPC down to set PCell between (PCMAX – XMAX)
and (PCMAX – XMAX – PW)
-> Send TPC up to set SCell between (PCMAX – XMAX)
and (PCMAX – XMAX – PW)
-> Send TPC 1dB up in order from the lowest Cell to ensure PUMAX
All Cells are at similar levels around (PCMAX – XMAX).

## Slide 7: Attached files
CR implementation example for Option 1A
CR implementation example for Option 1B

## Slide 8: Reference
[1] R5-218400, “Avoiding Scell Drop in FR2 RF UL-CA tests”, Apple, RAN5#93-e
[2] R5-218399, “Text Proposal CR to avoid Scell Drop in FR2 UL-CA tests”, Apple, RAN5#93-e
[3] R5-217652, “Preventing SCell drop in FR2 CA MPR test cases”, Ericsson, RAN5#93-e

## Slide 9
Appendix

## Slide 10: Power window
When TE controls UE output power, the actual value becomes target level +/- power window.
Power window size is the sum of
UE power step size
UE power step tolerance
TE relative MU
TE absolute MU *2
(F.4.4.2 in TS 38.521-3)
e.g.) Pw = 13.18dB
UE power step size = 1dB
UE power step tolerance = 1dB
TE relative MU = 1.4dB
TE absolute MU = 4.89dB
(FR2a, Target level = PUMAX)