## Slide 1: Discussion on R17 configuration DC_20A_n257A handling in RAN5
Huawei, Hisilicon
3GPP TSG-RAN5 Meeting #95-e R5-223128 Electronic Meeting, May 9th– May 20th, 2022

## Slide 2: General sections in TS 38.521-3
Proposal 1: DC_20A_n257A need to be added in Table 5.5B.5.1-1 in TS 38.521-3.
Observation 1: DC_20A_n257A is absent in general section (clause 5) in TS 38.521-3. The basic information in TS 38.101-3 clause 5 need to be included in TS 38.521-3.
TS 38.101-3

## Slide 3: Tx test cases in TS 38.521-3
Proposal 2: No need to modify clause 6 in TS 38.521-3 for DC_20A_n257A.
Observation 2: For Tx test cases for Inter-Band EN-DC including FR2 (1 NR CC), the progress for a specific EN-DC combo depends on the completeness of NR single carrier FR2 Tx test cases in TS 38.521-2 for the NR band. No changes need to be done to the existing TS 38.521-3 Tx test cases. Taking test case 6.2B.1.4.1 as an example:
TS 38.521-3

## Slide 4: Rx test cases in TS 38.521-3
Proposal 3: No need to modify clause 7 in TS 38.521-3 for DC_20A_n257A.
Observation 3: For Rx test cases for Inter-Band EN-DC including FR2 (1 NR CC), the same situation of Tx test cases applies. No changes need to be done to the existing TS 38.521-3 Rx test cases. Taking test case 7.4B.4 as an example:
TS 38.521-3

## Slide 5: Thank you!