## Slide 1: Disc on handling of MOP with UE capability maxUplinkDutyCycle
CMCC, Huawei, Hisilicon
3GPP TSG-RAN5 Meeting #96-e R5-224214
Electronic Meeting, Aug 15 – 26, 2022

## Slide 2: maxUplinkDutyCycle is defined in TS 38.331 and TS 38.306
Observation 1: FR1 UE capability maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 are well defined in TS 38.331 and TS 38.306.
38.331 >>> 6.3.3 UE capability information elements >>> RF-Parameters
maxUplinkDutyCycle-PC2-FR1 ENUMERATED {n60, n70, n80, n90, n100} OPTIONAL maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 ENUMERATED {n10, n15, n20, n25, n30, n40, n50, n60, n70, n80, n90, n100} OPTIONAL
38.306 >>> 4.2.7.2 BandNR parameters
Definitions for parameters | Per | M | FDD-TDDDIFF | FR1-FR2DIFF
maxUplinkDutyCycle-PC2-FR1 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable for FR1 power class 2 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field is absent, 50% shall be applied. Value n60 corresponds to 60%, value n70 corresponds to 70% and so on. This capability is not applicable to IAB-MT. | Band | No | N/A | FR1 only
maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable for FR1 power class 1.5 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field is absent, UE shall mitigate MPE autonomously by P-MPR or by other means and no restriction on scheduled uplink duty cycle is needed. | Band | No | N/A | FR1 only
Notes: maxUplinkDutyCycle is not covered by MOP test cases in TS 38.521-1/2/3, while

## Slide 3: maxUplinkDutyCycle is defined in TS 38.101-1
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class: - if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or - if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC2-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or - if the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is not absent and half the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC1dot5-MPE-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or - if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower; - shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4; - else if the UE does not support a power class with higher maximum output power than PC2; or - if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or - if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 0.5*maxUplinkDutyCycle-PC2-FR1 (The exact evaluation period is no less than one radio frame); or - if the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC1dot5-MPE-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or - if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower; - shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4; - else shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.
Observation 2: FFR1 UE capability maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 are well defined in Section 6.2.1 MOP of TS 38.101-1.
Notes: any configuration specific change requests to Chapter 5 ONLY shall NOT be accepted by RAN5

## Slide 4: maxUplinkDutyCycle is NOT covered in RAN5 specs
Observation 3: FR1 UE capability maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 are not covered in RAN5 specs.
Observation 4: For the existing TDD UL-DL patterns in Table C.2-3 (UplinkDutyCycle≈22.86%) and Table C.2-4, the UplinkDutyCycle≈22.86%, which is not good enough for the “most critical” testing of maxUplinkDutyCycle.
Notes: TDD Slot Configuration patterns

## Slide 5: To define TDD UL-DL pattern for maxUplinkDutyCycle=20% MOP testing
Proposal 1: Basing on the TDD Slot Configuration patterns already supported by the industry, UplinkDutyCycle=20% can be defined for testing (SCS=15KHz, 30KHz) as below.
When maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16=20% and UplinkDutyCycle=20%, the UE shall apply all requirements for the supported power class 1.5
Notes: TDD Slot Configuration patterns

## Slide 6: To define TDD UL-DL pattern for maxUplinkDutyCycle=30% MOP testing
Proposal 2: Basing on the TDD Slot Configuration patterns already supported by the industry, UplinkDutyCycle=30% can be defined for testing (SCS=15KHz, 30KHz) as below.
When maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16=30% and UplinkDutyCycle=30%, the UE shall apply all requirements for the supported power class 1.5
Notes: TDD Slot Configuration patterns

## Slide 7: To define TDD UL-DL pattern for maxUplinkDutyCycle=40% MOP testing
Proposal 3: Basing on the TDD Slot Configuration patterns already supported by the industry, UplinkDutyCycle=40% can be defined for testing (SCS=15KHz, 30KHz) as below.
When maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16=40% and UplinkDutyCycle=40%, the UE shall apply all requirements for the supported power class 1.5
Notes: TDD Slot Configuration patterns

## Slide 8: To define TDD UL-DL pattern for maxUplinkDutyCycle=60% MOP testing
Proposal 4: Basing on the TDD Slot Configuration patterns already supported by the industry, UplinkDutyCycle=60% can be defined for testing (SCS=15KHz, 30KHz) as below.
When maxUplinkDutyCycle-PC2-FR1=60% and UplinkDutyCycle=60%, the UE shall apply all requirements for the supported power class 2
When maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16=60% and UplinkDutyCycle=60%, the UE shall apply all requirements for the supported power class 1.5
Notes: TDD Slot Configuration patterns

## Slide 9: To define RF Baseline Implementation Capabilities for maxUplinkDutyCycle
Proposal 5: To define NR FR1 maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 RF Baseline Implementation Capabilities in TS 38.508-2 as below.
Notes: TDD Slot Configuration patterns

## Slide 10: To define UE capability information elements for maxUplinkDutyCycle
Proposal 6: To define RF-Parameters maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 in TS 38.508-1 as below.
Notes: TDD Slot Configuration patterns

## Slide 11: To define RRC UE capability for maxUplinkDutyCycle
Proposal 7: To define RRC UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 in TS 38.523-1 as below.
Notes: TDD Slot Configuration patterns

## Slide 12: Thank you!