## Slide 1: Discussion – Software Implementation of NR Applicability Specifications
Qualcomm
3GPP TSG-RAN5 Meeting #99 R5-233200
Incheon, South Korea, May 22-26th, 2023

## Slide 2: Background
3GPP Test Case Selection is a tedious process, due to complex nature of NR device options (NSA, SA, Verticals etc) and related UE capabilities. There is no uniform process to derive applicable tests in certification industry.
RAN5 Signaling Specifications are translated to TTCN code for further SW implementation of test suites, applicability and test environment by Test Equipment Vendors. This provides consistency and reliability in test ecosystem.
RAN5 Performance specifications, by their innate nature, are left to be implemented by Test Equipment Vendors. There are no RAN5 “checks” on implementation.
RAN5 has capability to provide partial or full SW implementation of applicable specifications.

## Slide 3: Background – Overall Industry value
3GPP Test Selection can be Automated per device capability providing uniformity across Industry
RAN5 Applicability and PICS definition Specifications are already in pseudo-code format, easily implementable in software i.e based on given input of PICS data, output the applicable tests.
3GPP RAN5 Defined Tests
Extracted OEM PICS Compliance
TS 38.508-2
TS 38.523-2
Protocol
TS 38.522
RF+Perf (RRM, Demod)
OEM Augments Band, CA and other Information
TS 34.229-2
IMS (5G, 4G)
Output = No. of Applicable Tests per Device Capability
(All Automated in RAN5)
Execution Rules (Cert Industry Logic)
Final List of Test Cases

## Slide 4: Proposal-1 – SW implementation of SIG Applicability Specs
Identify Relevant PICS, (ex. from TS 38.508-2) for the DUT
Feed These to Condition
Set (C) in TS 38.523-2 or TS 34.229-2
TTCN/Non-TTCN
Implementation of TS 38.523-2 or TS 34.229-2
PICS | PICS Def | TRUE/FALSE
pc_5GCN | UE Supporting 5GS | TRUE
pc_as_ReflectiveQoS | Support of reflective QoS | TRUE
Output = No. of Applicable Tests for Band Under Test
Test Case Selected
Test Case 7.1.4.1
7.1.4.1 | SDAP Data Transfer and PDU Header Handling UL/DL | Rel-15 | C21A | UEs supporting 5G Core and reflective QoS
C21A | IF A.4.1-5/1 AND A.4.3.7-1/4 THEN R ELSE N/A | UEs supporting 5G Core and reflective QoS
Test Case selection is currently limited to validating the tests prior to execution for the PICS support
With Proposal-1, a new SW entity will generate the list of applicable tests. This new SW entity can be standalone or can also be used a plug-in for outside solutions (For ex – Test equipment vendor SW using RAN5 API’s)

## Slide 5: Proposal 2 – SW implementation of TS 38.522 (RF, RRM, Demod)
Identify Relevant PICS (including bands), from TS 38.508-2 for the DUT
Apply CA/DC Configuration (E) in TS 38.522
New SW Implementation of TS 38.522
(Handle Additional Comments, Notes)
Output = List of Applicable Tests per Device Capability
UE Features in Condition
Set (C) in TS 38.522
Apply Tested Bands Selection
Set (D) in TS 38.522
Apply Branching Criteria –
PC, RX
TS 38.522 can be implemented in SW and added as part of RAN5 deliverable
With Proposal-2, a new SW entity will generate the list of applicable tests per device capability. This new SW entity can be standalone or can also be used a plug-in for outside solutions (For ex – Test equipment vendor SW using RAN5 API’s)

## Slide 6: Proposal – Pro’s and Con’s
Cons
  Extra burden on RAN5 - $$, Scalability, Maintenance
  Need long term commitment; representation and SW implementation
  Difficult to implement non-implementable notes or exceptions, comments
  Independent SW distribution vs TTCN style
Pro’s
  Leaves no room for error in TC selection; benefits certification ecosystem by providing a degree of uniformity in test case selection
  Improves clarity on what is applicable for a particular device type;
  Helps overall Cert Ecosystem
  Provides RAN5 applicability specification more meaning & accountability.

## Slide 7: Summary/ Impact of proposals
TS 38.522, which includes applicability and selection expression is a binary spec and if implemented in SW shall result in consistent, reliable test case selections
Overall Test Industry will greatly benefit from resulting output of TS 38.522 i.e Applicable tests for RF, RRM and Demod across Band, BW, CA and Branch Config.
TS 38.523-1 and TS 34.229-2 Signaling applicability and test case selection can be implemented independently or with leverage from existing TTCN implementation.
TS 38.508-2 also will have to translated in appropriate SW implementation to cater as input to Proposal-1 and Proposal-2.
With Proposal-1 and Proposal-2 implemented in SW and delivered from RAN5 as standalone SW or as plugin/API’s, the test case selection can be made uniform.
Continuous maintenance\release of these SW versions along with Specifications release