## Slide 1: DRAFT WF on RF/RRM test frequency and selection approach
Dish, Ericsson, Qualcomm, …
3GPP RAN WG5 NB-IoT Ad-hoc#1 R5-164125
Sophia Antipolis, France, 28 – 30 June, 2016

## Slide 2: General
Rx tests : total 7 tests
Tx tests: total 19 tests
Demod Performance & RRM: [TBD] tests
NB-IoT operating bands 1, 2, 3, 5, 8, 12, 13, 17, 18, 19, 20, 26, 28, 66
Nominal channel spacing between 2 adjacent carriers
  In Stand-alone mode : 200kHz
  In Guard band mode and In-band mode : 180kHz
Channel raster: 100kHz
Operating mode assumption for all Rx/Tx tests: Standalone mode (may vary depending on the TC)
UL BW assumed to be single tone 15kHz for all DL tests

## Slide 3: Assumption for TRx
NB-IoT core requirements for reference design architecture are based on one wideband filter across all bands in low frequencies (729MHz – 1GHz) and one across higher frequencies (1805MHz – 2200MHz), which is reflected in the RAN4 WF for OOBB, in R4-164900.
Based on this approach the test frequency selection for all TRx test cases will be made across all the bands UE supports in these lower or higher frequencies
  E.g. Tested Frequency: Low range of the lowest supported band in 729MHz-1GHz frequencies
For most cases the test frequency selection can be generic across chapters 6 & 7, but some requirements need exceptions :
  E.g. Occupied bandwidth, UE Co-existence, Out-of-band blocking

## Slide 4: Agreements for RF
Define a low and a high test frequency point for each operating band into TS 36.508 Ch.5:
  As far as possible, frequency points should be made common to all operation modes
  Specify all these frequency points in common tables and indicate which band they belong to:
    Table for bands in 729MHz – 1GHz range
    Table for bands in 1805MHz – 2200MHz range
Tested bands/frequency assumption is
  Most TRx requirements are band independent within the frequency group (729-1000 or 1805-2200)
  As a starting point for all TRx cases, 2 test frequency points are selected across the bands UE supports in the following way;
    @ low range of the lowest supported band
    @ high range of the highest supported band
  of the supported bands in (729MHz – 1GHz) AND (1805MHz – 2200MHz)
  For other requirements that have a clear dependency on the band or exception otherwise, need further analysis:
    Examples TCs that may require specific testing:
    6.6.1F Occupied bandwidth  May require testing in all supported bands
    6.6.3.2F UE co-existence  Requires band specific testing on the protected frequency ranges
    7.6.2F Out-of-band blocking  Requires testing based on RAN4 OOBB WF in R4-164900
    7.7F Spurious response  Based on exceptions in OOBB
For RAN5#72: Test frequency selection, using low & high frequencies, for each TC needs an analysis of the requirement and a discussion paper explaining it.

## Slide 5: Agreements for other areas
For Demodulation Performance and RRM conformance requirements
  Test point shall be made applicable for operation modes as defined in the core specification for each test
    Test frequency is defined for each mode
  Requirements are operating band independent
For other conformance testing & future requirements
  Define frequency test points from each operating band into TS 36.508 Ch. 4 as needed
  As far as possible, the frequency points should be made common to all operation modes.

## Slide 6: RF Test Cases for NB-IoT
6.2.2F | UE Maximum Output Power
6.2.3F | Maximum Power Reduction (MPR)
6.2.5F | Configured UE transmitted Output Power
6.3.2F | Minimum Output Power
6.3.3F | Transmit OFF power
6.3.4F.1 | General ON/OFF time mask
6.3.4F.2 | NPRACH time mask
6.3.5F.1 | Power Control Absolute power tolerance
6.3.5F.2 | Power Control Relative power tolerance
6.5.1F | Frequency Error
6.5.2.1F.1 | Error Vector Magnitude (EVM)
6.5.2.2F | Carrier leakage
6.5.2.3F | In-band emissions for non allocated RB
6.6.1F | Occupied bandwidth
6.6.2.1F | Spectrum Emission Mask
6.6.2.3F | Adjacent Channel Leakage power Ratio
6.6.3.1F | Transmitter Spurious emissions
6.6.3.2F | Spurious emission band UE co-existence
6.7F | Transmit intermodulation
7.3F | Reference sensitivity level
7.4F | Maximum input level
7.5F | Adjacent Channel Selectivity (ACS)
7.6.1F | In-band blocking
7.6.2F | Out-of-band blocking
7.7F | Spurious response
7.8.1F | Wide band Intermodulation