## Slide 1: Discussion on adding a check point for SA Option 2
CMCC, China Telecom, China Unicom, CAICT, Huawei, Hisilicon, MediaTek, Spreadtrum, Keysight, CATT, StarPoint, vivo, Anritsu, Tejet, ZTE, SRTC, Lenovo
RAN5#3-NR-Adhoc meeting R5-185660
Jaipur, India, 8th-12th October 2018

## Slide 2: RAN5 phases and targets
The endorsed RAN5 NR phases and targets is extracted as below (R5-185183)
For SA Option 2 there are 2 phases targeted at Nov-18 and May-19.
It is proposed to have an additional SA Option 2 phase 1.5 (Feb-19)
SA Option 2 Phase 1.5
WIs for SA Original Option 2 Phase 2
WIs for SA Option 2 Phase 1.5
WIs for SA New Option 2 Phase 2

## Slide 3: Consideration of adding a check point of SA Option 2 phase 1.5
There are 3 meetings between Phase 1 and Phase 2: #4-NR-Adhoc, RAN5#82, and RAN5#83. Having phase 1.5 as an additional check point can help plan and progress for NR work on schedule.
The completion date of RAN4 performance part is Dec-18, but further corrections can be expected according to LTE’s experience. Moving the target of RAN5 work other than performance part to Phase 1.5 will bring early RAN5 progress based on relatively steady core specifications and will leave more reasonable and sufficient time to both performance part and non-performance part.
Operators that are interested in NR SA network are looking forward to getting conformance testing specification ready by 19H1, especially the high priority test cases. The sub-6GHz large-scale field trial will be kicked off by 19Q1 and the sub-6GHz friendly-user test will be started by 19Q4. The 5G industry eco-system will suffer huge risks and properly gain poor user experiences/feedbacks if the devices without conformance testing used in the friendly-user test which will cause a very bad influence on the whole 5G communication eco-system.

## Slide 4
TARGETED TO BE INCLUDED:
  SC FR1 and FR2
  RF - TS 38.521-1, TS 38.521-2, TR 38.903, TR 38.905
    Test definition, MU and TT for all NR FR1 Rx and Tx test cases (including UL MIMO, SUL), Note 1
    Test definition, MU and TT for NR FR2 RF MU/TT Target 1 and Target 2 test cases (including UL MIMO), Note 2
  Protocol - TS 38.523-x
    Basic NR SA Layer 2 including SDAP, Idle Mode and RRC test cases
    Basic NAS 5GC test cases
    Identify and draft in prose the SA Golden TCs target for TTCN development
  Test environment - TS 38.508-1, TS 38.508-2
    Common test environment to enable NR FR1 and FR2 testing
  UE test functions - TS 38.509
    UE test loop mode A and UE test loop mode B for SA NR
    UBF, SS-RSRPB UE reporting, UE Positioning test functions, SDAP test loop
NOT INCLUDED:
  RF MU/TT for RF MU/TT Target 3 test cases (TS 38.521-3)
  No NR FR1 or FR2 Demod/CSI reporting (TS 38.521-4)
  No NR FR1 or FR2 RRM (TS 38.533)
Note 1: Dependency: RAN4 progress until RAN4#89 (Nov-18)
Note 2: Dependency: RAN4 progress until RAN4#89 (Nov-18) + RAN5 RF MU/TT progress. For RF MU/TT target 1 and 2 test cases MU is planned to be completed by RAN5#NR3 (Oct-18) and TT is targeted to be completed by RAN5#81 (Nov-18) (Ref R5-183257)
Proposed SA Option 2 (SA NR) Phase 1 content
- Target RAN5#81 Nov-18

## Slide 5
Proposed SA Option 2 (SA NR) Phase 1.5 content
- Target RAN5#82 Feb-19
TARGETED TO BE INCLUDED:
  CA configurations for FR1 xCC, where x<=4
  RF - TS 38.521-1, TR 38.905
    Test definition, MU and TT for all NR FR1 CA Rx and Tx test cases
    Test definition and MU/TT for NR FR1 Demod/CSI reporting (TS 38.521-4), Note 3
    Test definition and MU/TT for NR FR1 RRM (TS 38.533) test definition and TT, Note 3
  Protocol - TS 38.523-x, TS 34.229-x
    For CA protocol testing it is assumed that max 2CC need to be covered.
    Enhanced test coverage for NR SA Layer 2 including SDAP, idle mode and RRC test cases, Note 1
    SUL
    Verifiable Golden Protocol Testcase for NR SA covering all Layers, Note 2
    Inter-RAT to/from LTE
    5GS IMS (EPS Fallback), Note 1
  Test environment - TS 38.508-1, TS 38.508-2
    Common test environment to enable NR FR1 CA configurations
  UE test functions - TS 38.509
    TBD if any additional UE test functions needed
NOT INCLUDED:
  RF MU/TT for RF MU/TT Target 3 test cases (TS 38.521-3)
  SA NR positioning test cases
  Synchronous NR-NR DC
Note 1: Dependency: RAN2/CT1 progress until RAN2#105 & CT1#114 (Feb-19)
Note 2: Dependency: The delivery of Dec-18 will use Sep-18 baseline unless critical issues are found, if so Dec-18 baseline shall be used on a timely updated verifiable delivery.
Note 3: Dependency: Limited to “RAN4 Phase I” described in RP-182149 and RAN4 progress until RAN4#88-Bis (Oct-18)

## Slide 6
Proposed SA Option 2 (SA NR) Phase 2 content
- Target RAN5#83 MAY-19
TARGETED TO BE INCLUDED:
  SC FR2 + CA configurations for FR2 xCC, (FR1+FR2) xCC + Synchronous NR-NR DC for FR1 xCC,FR2 xCC, (FR1+FR2) xCC:, where x<=4
  RF - TS 38.521-1, TS 38.521-2, TS 38.521-3 (FR1+FR2), TS 38.521-4, TS 38.533, TR 38.903, TR 38.905
    Test definition and MU/TT for NR FR2 Rx and Tx RF MU/TT target 3 test cases where MU/TT analysis completed (including UL MIMO), Note 2
    Test definition and MU/TT for NR FR1 Demod/CSI reporting (TS 38.521-4), Note 1
    Test definition and MU/TT for NR FR1 RRM (TS 38.533) test definition and TT, Note 1
    Test definition for NR FR2 Demod/CSI reporting (TS 38.521-4), Note 1
    Test definition for NR FR2 RRM (TS 38.533), Note 1
  Protocol - TS 38.523-x, TS 34.229-x, TS 37.571-x
    For DC protocol testing it is assumed that max 2CC need to be covered.
    Synchronous NR-NR DC
    SA NR positioning test cases
    5GS IMS (VoNR), Note 4
  Test environment - TS 38.508-1, TS 38.508-2
    Common test environment to enable FR2/FR1+FR2 CA configurations
NOT INCLUDED:
  MU/TT part of NR FR2 Demod/CSI reporting (TS 38.521-4), Note 2
  MU/TT part of NR FR2 RRM (TS 38.533), Note 2
Note 1: Dependency: Limited to “RAN4 Phase II” described in RP-182149 and RAN4 progress until RAN4#89 (Nov-18)
Note 2: Dependency: RAN4 progress until RAN4#91 (May-19) + RAN5 RF MU/TT progress. For RF MU/TT target 3 test cases MU is planned to be completed by RAN5#81 (Dec-18) and TT is targeted to be completed by RAN5#NR4 (Jan-19) (Ref R5-183257)
Note 3: There will be a need for a SA Opt.2 Phase 3 to be added when MU/TT targets for Demod/CSI and RRM test cases becomes available.
Note 4: Dependency: GSMA progress and RAN2/CT1 progress until RAN2#106 & CT1#115 (May-19)

## Slide 7: Proposal
RAN5 endorses the proposal of adding a new check point for SA Option 2 in Feb-19 and the contents proposed in this slide.

## Slide 8: Thank you!