## Slide 1: Multi PDU Session and IMS in SA Option-2 Singapore, 5G Adhoc# 4
Jan 22, 2019
R5-190175

## Slide 2: Background
A 5GS UE can initiate –
  IMS PDU session only
  Internet PDU session only
  IMS and Internet both (in any order)
In EUTRA the PDN was part of the “Attach” process and hence it was predictable which PDN was being used by UE and in which order as such based on what UE behavior was, the assignment of EPS Bearer ID and DRB id and QFI flows was made
In 5GS, after REGISTRATION complete, UE can trigger any PDU session and the behavior is dynamic and the assignment of corresponding QFI flow, DRB id and QFI\QRI
RRC_IDLE and some key generic procedure SHALL account for handling of multi PDU session and the behavior in 5GS shall be made “dynamic” rather than “static”
RF TC doesn’t want to involve IMS signaling during RF tests

## Slide 3: Background
Issue#1
UE Usage Setting (TS 24.501) --> Indicate to support voice (support any – Voice or Data), Spec reference below, including this IE means UE is configured to support IMS voice
8.2.6.14 UE's usage setting
This IE shall be included if the UE is configured to support IMS voice.
àRAN5 may have to consider the case where this is included and not-included (as well as Account for all devices - No IMS, IMS, Data (or rather voice or no-voice))
but most likely VoPS indication in Registration Accept SHALL be 1.
This is addressed in Registration Accept
Definitions for parameters | Per | M | FDDTDD DIFF | FR1 FR2 DIFF
voiceOverEUTRA-5GC Indicates whether the UE supports IMS voice over E-UTRA via 5GC. | UE | No | No | No
voiceOverNR Indicates whether the UE supports IMS voice over NR. It is mandated to the IMS voice capable UE in NR otherwise optional. | UE | No | No | Yes
Observation#1
UE Capability
VoNR - voice over MCG bearer in UE Capability Message
Also capability for FR1, FR2 defined in RAN2 (38.331)
Inter-rat capability for eLTE
No capability for IMS voice for EPS fallback
  Per 38.306 -4.2.13 IMS Parameters
This is addressed by introduction of new PICS for 5G UE support of IMS

## Slide 4: Background
Issue#2
Order of IMS PDU or Internet in RRC IDLE and other generic procedure–
  Handle IMS, Internet and combination in any order along with both IMS and Internet requested at the same time
  Scale the solution in case more PDU sessions are requested
Possible Solution –
Identify the PDU session, Transaction ID of IMS PDU session, assign it the IMS values (QFI flow, DRB, QoS)
Complete the assignment of PDU session and in parallel handle Internet PDU session
This if the UE only request any order of number of PDU sessions, those can be handled
Have a set table for IMS and Internet PDU assignment which can be mapped once those PDU session are identified.
PICS/PIXIT for UE to declare no. of PDU session supported
One such solution is proposed in R5-190131r1 (4.5.2 IDLE, PDU) and R5-190019r2 Updates to PDU session establishment 5GSM messages (attached)
Any solution for Issue#2 will have a MAJOR impact on almost ALL TEST CASES in TS 38.523-1. As such, we need to be careful in adopting this, suggest thorough review by all.
Issue#3
RRC_IDLE call flow will depend how the UE sets FoR bit.
RRC Release might be part of the RRC_IDLE procedure

## Slide 5: Background
Observation#2
Test loopback Mode –
Same solution which we had in EN-DC should be fine.
Issue#4
Once common procedure for Issue#2 is agreed, for IMS Registration – Only minor changes needed (For ex)
24.229 - Re-use it for NR, RAT will use "NR" in PANI header.
PANI Header - Cell Network Identifier, 5G Cell is 36 bit compared to 28 bit for LTE. Several other places where the RAT setting are needed.
34.229 can be updated to add 5G RAT and Cell Identity wherever needed in Annexes for Rel-15 5G NR
MO, MT and EPS Fallback related changes may be required
5.3.2 Close UE test loop
Same as TS 36.509 [6], subclause 5.4.2 with the following exceptions:
- where E-UTRA is mentioned the same applies for NR;
- the NB-IoT mode is out of the scope of the present specification
- where different UE test loop modes are mentioned only those applicable to 5GS should be taken into account (see subclause 5.3.4 for the applicable 5GS UE test loop modes).
- where EPS bearers are mentioned the same applies for 5GS QoS flows; and

## Slide 6: Requirements for RF
- In LTE, RF tests indicated no VOPS allowed based on the pc_Disable_E-UTRA_NOIMSVoIP
After closing the UE Test loop mode activation, IMS signaling was suppressed in E-UTRA, this behavior is still the same in 5GS
In 5GS, if the UE usage setting is “set” then IMS voice is supported and NW shall indicate VOPS=1 otherwise UE may have unintended consequences (EPS fallback during Domain Selection)
With test loop ON = IMS signaling will be suppressed by IMS PDU session can be allowed, will this work for RF tests?