## Slide 1: Review on RAN4 pending issue after RAN4#89
NTT DOCOMO, INC.
3GPP TSG-RAN WG5 Meeting #4-5G-NR Adhoc R5-190265
Singapore, Singapore, January 21th - 25th 2019

## Slide 2: Introduction
RAN4 pending issues was updated based on the latest TS 38.101-1, 2, 3 (V15.4.0).
  Updated list was captured in LS R5-190376 (RAN5#NR4, Jan-2019)
RAN5 response was drafted in attached XLS, while some specific items require additional discussion in RAN5.
  The purpose of this document is to list complicated items and achieve RAN5 conclusion.
In addition, new pending issues added during RAN5#NR4 were also captured in this contribution.

## Slide 3: [TS 38.101-1_#01] Pi/2 BPSK in MOP
Pi/2 BPSK is out of scope of MOP according to R4 reply.
  However UL RMC for DFT-s-OFDM Pi/2 BPSK is defined in TS 38.101-1.
  Pi/2 BPSK is already defined as test point in MOP case in R5.
Questions
  Should RAN5 test Pi/2 BPSK in MOP?
  If R5 test Pi/2 BPSK, is UL RMC defined in core spec enough for R5? (Is this still pending issue?)

## Slide 4: [TS 38.101-1_#02] Discontinuous measurement
Pending issue about discontinuous was updated according to R4 reply.
Questions
  Is this item still pending issue? How about FR2?

## Slide 5: [TS 38.101-1_#03] MPR for PC2
Pending issue (brackets for PC2) will be removed according to R4 reply and R4 has closed this topic.
  However brackets are still remain in the latest TS 38.101-1.
Questions
  Could RAN5 regard this item as closed, or wait R4’s update?

## Slide 6: [TS 38.101-1_#04] A-MPR
There are still many brackets, TBD in TS 38.101-1.
  In addition, number of NS to apply A-MPR will increase in the future.
Questions
  When can RAN5 conclude this pending item as closed?
    When all items are completed for at least one NS.
    When all items are completed for all NSs.

## Slide 7: [TS 38.101-1_#05] Duration for mean power
R4 recommendation (1ms) is captured while there is still TBD in the spec.
Questions
  Is this item still pending issue?

## Slide 8: [TS 38.101-1_#06] IE AdditionalSpectrumEmission
Required values are captured in core spec, however more clarification is needed according to R4.
Questions
  Is this item still pending issue?

## Slide 9: [TS 38.101-1_#07] Annexes
Corresponding items are out of scope according to R4 reply.
Assumption
  R5 could close these items now.

## Slide 10: [TS 38.101-2_#08] Testability of Receiver tests
Question
  Are these items still pending issue?

## Slide 11: [TS 38.101-2_#09] Max input level (64QAM)
R4 asks R5 whether 64QAM requirement can be tested in OTA.
  R5 conclusion is that Not only 64QAM but also QPSK can’t be tested by High PSD issue as described in LS.
Question
  Is this item still pending issue?

## Slide 12: [TS 38.101-3_#10] Power sharing in EN-DC
Question
  Is this item still pending issue? Is R4 update enough for R5 to make conformance test?

## Slide 13: [Newly added] Definition of UL-MIMO OFF power (TS 38.101-1)

## Slide 14: [Newly added] BC requirement (TS 38.101-2)

## Slide 15: [Newly added] Tx IM for EN-DC (TS 38.101-3)