## Slide 1: WF on MU Threshold
Qualcomm, Verizon, AT&T, Orange, Vodafone, Nokia, Sprint, CAICT, Dish, Ericsson, CMCC, Samsung, Motorola

## Slide 2: MU Threshold
The MU Threshold, MUThreshold, is used
  To determine the Test Tolerance (TT) that test requirements are relaxed by, i.e., 0≤TT≤MUThreshold
  To determine whether a test system installed at a test lab and whose MU has been assessed can be used for certification purposes, i.e., MUTS≤MUThreshold the test system can be used for certification purposes
Reducing the MU Threshold over time could result in authorized labs to become unauthorized
MU Thresholds for conducted test cases have traditionally not evolved over time
The MU threshold (Maximum Test System Uncertainty) will be captured in Annex F of TS38.521-2

## Slide 3: MU Assessment & Expanded Uncertainty
For every test case, a detailed and exhaustive MU assessment needs to be performed
  For each MU element proper documentation and evidence must be presented to be included in the MU table, e.g., experimental data, simulation results, datasheets, research papers, etc.
For every test case, an expanded uncertainty (1.96σ - confidence interval of 95 %) is determined

## Slide 4: MU Threshold vs Expanded Uncertainty
Generally in 3GPP, MU Threshold has been defined to be within 90% to 100% of the Expanded Uncertainty
Currently, there is no framework in place on how to determine the MU threshold for FR2 OTA test cases

## Slide 5: Evolution of MU vs MU Threshold
TE Vendors are committed to improving the MU of test systems over time by evolution in technology, HW, and SW
Reducing the MU threshold over time could have significant consequences for labs with existing test systems by getting unauthorized. Potentially significant investments might be required to get authorized again

## Slide 6: Evolution of Expanded Uncertainty
For the last 2 years, TE and TS vendors have been working on MU assessments in RAN4 and later in RAN5.
Analyses were based on
  state of the art equipment (highest performance) and components
  optimized algorithms and procedures (measurement grids, calibrations, etc.)
Group/TR | TRP | EIRP | EIS
RAN4 (TR38.810) | 5.13 | 5.99 | 6.49
RAN5 (TR38.903) | 4.29-4.69 | 4.38-4.78 | 5.02

## Slide 7: Way Forward-1
Proposal 1: RAN5 defines all FFS MU Thresholds in TR 38.903 Annex B.x for each test case to correspond to Expanded Uncertainty*[1.00]. Include MU threshold table with FFS values in TS38.521-2 Annex F.1.2 & F.1.3.
Proposal 2: VOID
Proposal 3: RAN5 should define a MU threshold improvement percentage (TBD) that would trigger an update to the MU threshold limit and implement it based on input from certification bodies and accordingly define the transition period for the industry to accept these updated MU thresholds.