## Slide 1: Way Forward on SNR estimation assumptions
Anritsu, Keysight Technologies, R&S
R5-190980

## Slide 2: Discussion in RAN5 NR#4 AdHoc
Following papers are provided in RAN5 NR#4 AdHoc meeting are discussed
This paper summarize the assumption that shall be used for deriving SNR estimation for FR2 test cases.
R5-190601 | On relaxation of test requirements for Low and High PSD test cases | Keysight
R5-190446 | On the power level to derive SNR for FR2 TRx tests | Anritsu
R5-190460 | SNR estimation update for FR2 priority 1 and 2 TRx TCs | Anritsu
R5-190059 | Impact from noise for FR2 TRx MU | Anritsu

## Slide 3: Agreements (1/4)
Estimation on SNR is required to address testability issue due to low SNR
Threshold SNR or Threshold Systematic Error of any in-band TRx test will not be determined before having all the SNRs for below TCs to see the SNR of the test system which support variety of test cases in terms of target power level to be measured.
  MOP (Represents Mid-High Power TC)
  OFF Power (Represents Low Power TC)
  SEM, ACLR (Represents Low Power Measurement under the existence of high power carrier in vicinity)
Estimation of SNR for other Priority 1 and Priority 2 test are not deprioritized and are still encouraged to be provided in RAN5#82.

## Slide 4: Agreements (2/4)
Adopt following general assumptions for deriving estimated SNR
  UE power class 3 requirements
  Channel bandwidth : 400 MHz
  Frequency ranges:
    FR2a: 23.45 GHz≤f≤32.125GHz, SNR derived for 32.125GHz
      Add note that SNR estimation does not apply between 30.3GHz - 32.125GHz
    FR2b: 32.125 GHz<f≤40.8GHz, SNR derived for 40.8GHz
  MOP:
    Max peak EIRP: +43 dBm/ChBW
    Min peak EIRP: 22.4 dBm for FR2a and 20.6 dBm for FR2b – Multi-band relaxation
      Multiband relaxation for peak EIRP:
        FR2a UE: 22.4d Bm -1.7 dB (multi-band relaxation)
        FR2b UE: 20.6 dBm -1.7 dB (multi-band relaxation)
    TRP: 23 dBm
    Spherical coverage: 11.5 dBm for FR2a and 8 dBm for FR2b – Multi-band relaxation
      Multiband relaxation for EIRP spherical coverage:
        FR2a UE: 11.5 dBm -1.75 dB (multi-band relaxation)
        FR2b UE: 8 dBm -0.4 dB (multi-band relaxation)

## Slide 5: Agreements (3/4)
Adopt following general assumptions for deriving estimated SNR(Cont’)
  OFF Power
    TRP : -35dBm/ChBW
  SEM
    TRP : -13dBm/MHz
  ACLR
    Adjacent channel power
      FR2a UE : 23dBm(TRP)-17dBc
      FR2b UE : 23dBm(TRP)-16dBc
    Adjacent channel BW is 400MHz

## Slide 6: Agreements (4/4)
Adopt following general assumptions for deriving estimated SNR(Cont’)
  SNR is calculated for total component power of both polarization
  Impact from the noise (systematic error) is calculated with (SNR as linear value) [R5-190059, R5-190446]
  SNR estimation is provided assuming single test setup.
  Size of QZ 30cm for IFF
Following information should be provided in addition to estimated SNR
  Temperature range for conformance test system
After collecting the estimated, define an acceptable limit on influence of noise for each Tx test case that will be added into MU budget considering a trade off between higher MU vs core requirement relaxation