## Slide 1: WF on Low PSD issue
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #5-5G-NR Adhoc R5-193383
Xi'an, China, 9th Apr 2019 - 12th Apr 2019
Agenda Item : 4.1.16
Document for : Discussion and Endorsement

## Slide 2: Summary
NOTE
  This WF to be applied only for Priority 1,2 Low PSD cases (Off power, SEM, ACLR, Rx Spurious).
  “Relaxation” = “Relax_1 (Required relaxation value to avoid Low PSD)” + “Relax_2 (legacy TT based on MU)”
    Test requirement = Min req. + Relaxation = Min req. + Relax_1 + Relax_2 (Relax_1 = 0 in LTE, FR1)
Process for how to treat Low PSD items
  Required relaxation value (Relax_1) to be analyzed / endorsed by MU contributors per TC.
  Following inputs to be prepared by operators using attached XLS format
    Upper limit of acceptable relaxation value per TC
    Acceptable options per TC
    TC list of regulatory items for each regulatory bodies (e.g. FCC, CE)
  RAN5 concludes which option to be applied for each TC considering inputs above.
    Conclusion will be defined TC by TC, and applied relaxation value and options will be updated in the future.
Action points
  [May-19, RAN5#83] Operators to be submit there views (acceptable relaxation value, options) with attached XLS

## Slide 3: AP to Operators for RAN5#83 (May-2019)
Possible options for how to treat Low PSD items are listed as below.
  Option 1 : Test with relaxation
  Option 2 : Test without relaxation
  Option 3a : Don’t test (Test requirement including relaxation to be captured in TS 38.521-2)
  Option 3b : Don’t test (Test requirement not including relaxation to be captured in TS 38.521-2)
  Option 4 : Don’t test (TC to be removed from TS 38.521-2)
  Option 5 : Decision based on regulatory bodies
Operators to fill attached XLS
  Both options for 1) Relaxation is within limit and 2) Relaxation exceeds limit, should be considered.
  Discussions with your regulatory bodies are highly required.
  Example (following value / options are not proposal)
TC | Title | Limit of acceptable relaxation (Z) |  | Proposed Option | Proposed Option
 |  | FR2a | FR2b | (when Relaxation <= Z) | (when Relaxation > Z)
6.3.2 | OFF power | 20 dB | NA | Option 1 | Option 3a
6.5.2.1 | SEM | - | NA | NA | NA
6.5.2.3 | ACLR (absolute) | 0 dB | NA | Option 2 | Option 3a
6.5.2.3 | ACLR (relative) | 5 dB | NA | Option 1 | Option 3a
7.9 | Rx Spurious | 30 dB | NA | Option 1 | Option 3a

## Slide 4: Proposal (NTT DOCOMO, INC.)
Following options are DCM’s proposal for each TC.
  NOTE 1 : Proposals are for FR2a (Band n257) which is Japanese FR2 band.
  NOTE 2 : SEM is “NA” since this TC is not Low PSD item with FR2a.
  NOTE 3 : Proposal for ACLR (absolute) is to skip this requirement in conformance test.
    To adopt 1 step approach (relative) instead of existing 2 step approach (absolute -> relative)
  NOTE 4 : Proposed options will be updated according to approved Relax_1 value.
Reference
  Option 1 : Test with relaxation
  Option 3b : Don’t test (Test requirement not including relaxation to be captured in TS 38.521-2)
TC | Title | Proposed option
6.3.2 | Off power | Option 1
6.5.2.1 | SEM | NA2
6.5.2.3 | ACLR (absolute) | Option 3b3
6.5.2.3 | ACLR (relative) | Option 1
7.9 | Rx Spurious | Option 1

## Slide 5: Topics in RAN5#NR5 (Apr-2019)
LS from RAN4 (R4-1905100) was received with following RAN4 intention.
  Regarding regulatory items, testing even with relaxation is required.
    RAN4 would like to respectfully suggest re-evaluation of the current test method towards removal of relaxation due to testability limitations. Re-evaluation of alternative test methods are not precluded.
    RAN4 prefers that core requirements that ensure regulatory compliance be verified with no relaxation. RAN4 further advises that these regulatory-facing test cases have higher priority for resolution.
    RAN4 defers to RAN5 judgment, however, on relaxations needed during verification, to accommodate testability issues.
Some contributions to estimate required relaxation (Relax_1) were treated.
  Off power, Rx Spurious, ACLR (absolute, relative), [SEM (FR2b)] are categorized as Low PSD.
    SEM (FR2a) is not categorized as Low PSD while SEM (FR2b) is TBD.
Discussions in MU session
  From perspective of operator, Option 4 (Don’t test / To remove TC) can not be acceptable.
  Option 2 (Test without relaxation) is unrealistic for TCs which require much relaxation since MU becomes much larger.
  Relaxation can be acceptable even to regulatory items depended on value and TC.