## Slide 1: WF on MB relaxation
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #5-5G-NR Adhoc R5-193384
Xi'an, China, 9th Apr 2019 - 12th Apr 2019
Agenda Item : 4.1.16
Document for : Discussion and Endorsement

## Slide 2: Agreements / Assumptions
Based on RAN4 LS (R5-192901), RAN5 applies MB relaxation into conformance test with following assumptions except for verdict for certification / validation.
  MB relaxation value for each FR2 band are based on “UE declaration”.
  “Verdict per band”, which is same approach as legacy LTE.
Time plan
  Pre meeting discussions : 1) Proposed approach to remaining issues, 2) Raise additional issues
  [RAN5#83] (May-2019) : CR implementation to reflect agreements in this WF
  [RAN5#84] (Aug-2019) : Completion target of MB relaxation except for MU, TT
Process of UE declaration (Definition of verdict is TBD.)
  UE manufacturers declare each MB relaxation value to satisfy core requirement.
  Test houses, labs implement declared value into TE by manual since there is no capability for this relaxation.
  TE concludes verdict considering implemented declared value.

## Slide 3: Remaining issues [1/3]
UE declaration
  How to declare MB relaxation value
    One option is to use applicability spec TS 38.522 or TS 38.508-2.
  Whether declared value can be updated
    Option 1 : UE declared value shall not be updated.
    Option 2 : UE declared value can be modified during UE development period.
MU, TT, SNR estimation
  Whether MUMB = MUSB, TTMB = TTSB for each TC.
  Whether SNR estimation to be done TC by TC.
    Current analysis is based on assumption that maximum MB relaxation value (e.g. 1.7 dB) is applied.
Impact on certification bodies
  After completion of RAN5 work, we will send LS to certification bodies (e.g. GCF CAG, PTCRB).

## Slide 4: Remaining issue [2/3]
Definition of verdict
  Assumptions (TC : MOP EIRP)
    Number of Test point : 3 (1 env x 3 freq ranges x 1 ChBW x 1 SCS) according to Table 6.2.1.1.4.1-1
    FR2 bands supported by UE : Band n257, 258, 261 (MB relaxation ∑MBP is 1.7 dB)
    UE declaration : 1.0 dB (n257), 0.7 dB (n258), 0.0 dB (n261)
  Whether testing all FR2 bands at the same time with same TE is required?
Band | Test point | Applied MB relaxation | “Inter” Verdict | Verdict
n257 | #1 | 1.0 dB | PASS | FAIL
 | #2 | 1.0 dB | FAIL | 
 | #3 | 1.0 dB | PASS | 
n258 | #1 | 0.7 dB | PASS | PASS
 | #2 | 0.7 dB | PASS | 
 | #3 | 0.7 dB | PASS | 
n261 | #1 | 0.0 dB | FAIL | FAIL
 | #2 | 0.0 dB | FAIL | 
 | #3 | 0.0 dB | PASS | 

## Slide 5: Remaining issue [3/3]
Specification structure
  Test applicability for each TC (TC without MB relaxation and TC with MB relaxation)
  Test procedure for MB should be updated.
    Whether following points to be captured in the procedure.
      1) Process of UE declaration, 2) Process of implementing declared value into TE, and more
  Description of test requirement
    How to apply MB relaxation into test requirement. (e.g. 22.4 – TT – MB)
  TCs, Annex F (TS 38.521-2), TCs (TS 38.521-3), and applicability spec (TS 38.522) should be updated accordingly.
  Whether additional TCs for MB relaxation are required except for TCs captured in the latest WP
    MOP (EIRP, TRP, SC), MPR, A-MPR, configured output power, [ACLR?]…

## Slide 6: Spec structure
TCs of transmit power to be divided as below based on the latest WP of TS 38.521-2.
  Contents of TRP (6.2.1.1) and TRP (6.2_1.1.1) are completely same since there is no MB relaxation.
    6.2.1.1 : UE maximum output power - EIRP and TRP
    6.2.1.2 : UE maximum output power - Spherical coverage
    6.2.2 : UE maximum output power reduction
    6.2.3 : UE maximum output power with additional requirements
    6.2.4 : Configured transmitted power
    6.2_1.1.1 : UE maximum output power - EIRP and TRP with multi-band relaxation
    6.2_1.1.2 : UE maximum output power - Spherical coverage with multi-band relaxation
    6.2_1.2 : UE maximum output power reduction with multi-band relaxation
    6.2_1.3 : UE maximum output power with additional requirements with multi-band relaxation
    6.2_1.4 : Configured transmitted power with multi-band relaxation