## Slide 1: Progress on Proposal-1 : SW Implementation of NR Applicability Specs
Qualcomm
3GPP TSG-RAN5 Meeting #100 R5-234320
Toulouse, France, Aug 21-25th

## Slide 2
Updates, Agenda for Discussion
Recap of Overall Scope
High level SW Architecture of Qualcomm Prototype Design (Proposal-1)
Extraction of PICS in Machine Readable Format from relevant Spec (Ex-TS 38.508-2, 36.523-2, 34.229-2)
Extraction of “Conditions” from Applicability Specs (Ex-TS 38.523-2, TS 34.229-2)
User Input of DUT PICS Support
Final Output of the SW – List of Applicable Tests
Editorial CR’s
Next Steps

## Slide 3: Background – Overall Industry value
Updates:
Based on proposal in R5-233200 and outcome in RAN5#99, a separate exploder has been created - 3GPP_TSG_RAN_WG5_APPLICABILITY
Green items above now have Prototype SW Implementation
3GPP RAN5 Defined Tests
Extracted OEM PICS Compliance
TS 38.508-2
TS 38.523-2
Protocol
TS 38.522
RF+Perf (RRM, Demod)
OEM Augments Band, CA and other Information
TS 34.229-2
IMS (5G, 4G)
Output = No. of Applicable Tests per Device Capability
(All Automated in RAN5)
Execution Rules (Cert Industry Logic)
Final List of Test Cases

## Slide 4: Proposal-1 – SW implementation of SIG Applicability Specs
Identify Relevant PICS, (ex. from TS 38.508-2) for the DUT
Feed These to Condition
Set (C) in TS 38.523-2 or TS 34.229-2
TTCN/Non-TTCN
Implementation of TS 38.523-2 or TS 34.229-2
PICS | PICS Def | TRUE/FALSE
pc_5GCN | UE Supporting 5GS | TRUE
pc_as_ReflectiveQoS | Support of reflective QoS | TRUE
Output = No. of Applicable Tests for Band Under Test
Test Case Selected
Test Case 7.1.4.1
7.1.4.1 | SDAP Data Transfer and PDU Header Handling UL/DL | Rel-15 | C21A | UEs supporting 5G Core and reflective QoS
C21A | IF A.4.1-5/1 AND A.4.3.7-1/4 THEN R ELSE N/A | UEs supporting 5G Core and reflective QoS
Test Case selection is currently limited to validating the tests prior to execution for the PICS support
With Proposal-1, a new SW entity will generate the list of applicable tests. This new SW entity can be standalone or can also be used a plug-in for outside solutions (For ex – Test equipment vendor SW using RAN5 API’s)

## Slide 5: Proposal 1 - SW Implementation Design (Python with Doc-x, Pandas, JSON)
Step1: Extract all PICS from Spec (e.g. TS 38.508-2)
Step2: Extract Condition Set (C) from TS 38.523-2 or TS 34.229-2 and Combine with PICS Extracted from Step1
Step3: Logic for Applicability (Condition turned into If Else log with PICS support from UE)
Output = No. of Applicable Tests for Band Under Test
38.508-2
38.523-2
GUI
JSON
Excel
User Input (DUT Support for PICS)
'pc_5GC_NSSAA_EAP_AKA_Prime': True, 'pc_5GC_RACS': False,
38.508-2

## Slide 6: Extraction of PICS in Machine Readable
Implementation of PICS – High Level Design
Step1: Extract all PICS from Spec (e.g. TS 38.508-2)
38.508-2
Design Aspects:
Read the DOCX file specified or latest version
Extract all tables from above DOCX contents
Read Tables and Rows
Key\Value Mapping of Table\Items no. to PICS
  Demo xls1_PICS
Generate user input File\Template From extracted PICS
  Demo xls2_DUT_PICSupport

## Slide 7: Extraction of “Conditions” from Applicability Specs
Step2: Extract Condition Set (C) from TS 38.523-2 or TS 34.229-2 and Combine with PICS Extracted from Step1
38.523-2
Read the DOCX file specified or latest version
Extract all tables from above DOCX contents
Read Tables and Rows
Assign Key\Value Mapping of PICS to Test Case Selection Expression
Design Aspects:

## Slide 8: Final Output – List of Applicable Tests
Step3: Logic for Applicability (Condition turned into If Else log with PICS support from UE)
Output = No. of Applicable Tests for Band Under Test
GUI
JSON
Excel
User Input (DUT Support for PICS)
'pc_5GC_NSSAA_EAP_AKA_Prime': True, 'pc_5GC_RACS': False,
38.508-2
User Select Band Under Test
Assign Key\Value Mapping of PICS to Test Case Selection Expression
Apply DUT PICS (Machine Readable) Support as input & apply it to Test Case Selection Logic including band specific criteria (ex 38.523-3 cl11)
Output list of test cases per Band
  Demo xls3_FinalList
Design Aspects:

## Slide 9: Proposed Editorial changes to the spec
Issue1: Merges Cells
  The way merged cells are stored in DOCX Creates issues while parsing
  Example Tables: 38.508-2-h90 - Table A.4.3.9-2, Table A.4.3.9-3, Table A.4.3.9-4b, Table A.4.3.9-4d, Table A.4.4-2A
Issue 2: Duplicate elements and Inconsistent Duplicates in DOCX Source
  Example Impacted Tables: 38.523-2-h21 - Table 4.1-3a
These changes are brought in via following RAN5 Edirotial CRs:
R5-234376
R5-234377
R5-234378
R5-234379
R5-234380
Notes: Mursalin to updateImpacted Tables: And proposed changes

## Slide 10: Proposal 1 - SW Implementation Design (Python with Doc-x, Pandas, JSON)
Step1: Extract all PICS from Spec (e.g. TS 38.508-2)
Step2: Extract Condition Set (C) from TS 38.523-2 or TS 34.229-2 and Combine with PICS Extracted from Step1
Step3: Logic for Applicability (Condition turned into If Else log with PICS support from UE)
Output = No. of Applicable Tests for Band Under Test
38.508-2
38.523-2
GUI
JSON
Excel
User Input (DUT Support for PICS)
'pc_5GC_NSSAA_EAP_AKA_Prime': True, 'pc_5GC_RACS': False,
38.508-2

## Slide 11
Ongoing\Next Steps
Open Items in PICS Extraction
  Extraction of Bands and related tables without direct PICS (ex – pc_xyz)
Quality Assurance testing on SW for Proposal-1
  Taking PICS set from GCF validated tests and produce the same tests with SW Implementation
Further feedback on Input and Output Format desired, share info with Cert Orgs through LS (?)
Long Term SW maintenance in RAN5
  Choice of SW
  Funding, Resources
Performance TS 38.522 early study and challenges in implementation
  How to classify sub-tests? Needs harmonization

## Slide 12
References:-
RAN5#100 R5-233200 SW Implementation of RAN5 Applicability, Qualcomm