## Slide 1: Discussion on inter-band CA&DC UE co-existence test
ZTE Corporation
3GPP TSG-RAN5 Meeting #100 R5-235200r1 Toulouse, France, August 21– 25, 2023

## Slide 2: Simplification on inter-band CA/DC UE co-existence
References
[1] R4-2212357, On FR1 2UL inter-band CA coexistence requirements , Apple, RAN4#104-e, August 15th – 26th, 2022
[2] R4-2300398, LTE inter-band 2UL CA co-ex simplification R16, Nokia, RAN4#105, November 14th – 18th, 2022
[3] R4-2300399, LTE inter-band 2UL CA co-ex simplification R17, Nokia, RAN4#105, November 14th – 18th, 2022
[4] R4-2300400, LTE inter-band 2UL CA co-ex simplification R18, Nokia, RAN4#105, November 14th – 18th, 2022
Background in RAN4:
In RAN4#104-e meeting, a proposal in [1] initiated the discussion on how to simplify the FR1 2UL inter-band CA coexistence requirements.
The FR1 uplink inter-band CA (two bands) spurious emission for UE coexistence requirements has been derived based on the requirements for single carrier operation from each constituent UL band.
The protected bands and frequency ranges for a band combination in principle should be specified based on the intersection set from each constituent band coexistence requirements.
  For example, if Band A needs to protect bands A, B, C, D, E, F, G and Band B needs to protect A, B, E, F, G, H, I, then CA_A-B only needs to protect bands A, B, E, F, G.
In RAN4#105 meeting, the following agreements have been achieved:
Extend the scope of these simplifications to include all specifications that have 2-band uplink CA/DC coexistence requirements
  To include FR1 CA/DC cases in TS 38.101-1.
  To include FR1 EN-DC / NE-DC cases in TS 38.101-3.
  To include LTE CA cases in TS 36.101.
In RAN4#106 meeting, based on the agreements on LTE cases, 3 CRs in [2-4] starting from Rel-16 for LTE were agreed for simplify the inter-band CA co-existence table.
  Requirements which are expressed as frequency range are kept with an exception that if such requirement is due to close proximity of two bands, those can also be removed as single band case is more stringent.
  For example, for CA_1-5, the frequency range 859-869 MHz is kept, and other requirements are removed.

## Slide 3: Simplification on inter-band CA/DC UE co-existence
Progress in RAN4 & 5:
In RAN4#107 meeting, based on the changes made for LTE UE co-existence, 3 CRs starting from Rel-16 for inter-band 2UL NR CA co-existence simplification have been approved in [5-7] for FR1 CA configurations.
Furthermore, it is discussed in [8] that for EN-DC configurations there are also a lot of redundancy over single band requirements. Thus in [9-11], it is agreed to extend 2UL UE to UE co-existence simplification for EN-DC table using the same method as was done for LTE.
In RAN5#99 meeting, a discussion paper in [12] introduced the current status on 2UL UE co-existence in RAN4 and proposed possible actions in RAN5. After online discussion, the following decision has been made.
  LTE alignment with RAN4 spec needs to be handled as a discussion before CR.
  NR discussions to wait for RAN4 conclusion.
References
[5] R4-2308826, NR interband 2UL CA co-ex simplification R16, Nokia, RAN4#107, May 22 – 26, 2023
[6] R4-2307862, NR interband 2UL CA co-ex simplification R17, Nokia, RAN4#107, May 22 – 26, 2023
[7] R4-2307863, NR interband 2UL CA co-ex simplication R18, Nokia, RAN4#107, May 22 – 26, 2023
[8] R4-2307867, 2UL UE to UE co-ex simplification for EN-DC, Nokia, RAN4#107, May 22 – 26, 2023
[9] R4-2310373, CR to 38.101-3 reduction of UL EN-DC UetoUe co-ex R16, Nokia, RAN4#107, May 22 – 26, 2023
[10] R4-2310374, CR to 38.101-3 reduction of UL EN-DC UetoUe co-ex R17, Nokia, RAN4#107, May 22 – 26, 2023
[11] R4-2310375, CR to 38.101-3 reduction of UL EN-DC UetoUe co-ex R18, Nokia, RAN4#107, May 22 – 26, 2023
[12] R5-233205, Discussion on test simplification for inter-band 2UL coexistence, ZTE, RAN5#99, May 22 – 26, 2023

## Slide 4: Simplification on inter-band CA/DC UE co-existence
What changes in RAN4 spec？
What to remove?
  Remove all entries that are E-UTRA or NR band number.
  Remove those “frequency range” entries that are close proximity protection, in which the close proximity means 0 gap with the emission values of +1.6/-15.5/-40 dBm.
What to keep?
  Keep all other “frequency ranges” except the “close proximity frequency range”
What to add?
  No additional requirements are added.

## Slide 5: Simplification on inter-band CA/DC UE co-existence
What to do in RAN5？
  Considering that both LTE (36.101) and NR (38.101-1/-3) core requirements for UE co-existence have already been changed in the latest RAN4 spec, the evaluation work should be started ASAP in RAN5.
  With regard to the wording “When both constituent bands have common coexistence band protection requirements as specified in clause 6.5.3.2, the requirements are also applied to the carrier aggregation configuration”, RAN5 has two different understandings.
    Understanding 1: There is no need to have additional tests for the intersection constituent bands protection since they have already tested in the single band requirements.
    Understanding 2: The requirements for intersection constituent bands are still needed. The simplification in RAN4 only indicates the removing of the redundant part in the specification while the requirements for UE CA/DC co-existence has no change.
  Proposal 1: It is suggested to send a LS to RAN4 asking which of the above understanding is correct.
  To continue RAN5 work in UE co-existence, it is necessary for RAN5 to decide the working procedure before the LS is replied from RAN4.
  Proposal 2: It is suggested in RAN5 to follow the current working procedure before the feedback is received from RAN4.
    RAN5 keep the current template for analyzing UE co-existence.
    RAN5 use the last version of UE co-existence requirements before it was simplified in RAN4 as the core requirements.
    Whether the changes are needed in RAN5 and whether the changes apply to newly introduced TCs or to all TCs including the completed TCs will be decided after the response from RAN4.

## Slide 6: Thank you!