## Slide 1: Discussion on handling of MDT IDC problem
China Mobile
3GPP TSG-RAN5 Meeting #101 R5-237317
Chicago, USA, Nov 13 – 17, 2023

## Slide 2: UEs with good IDC mechanism may fail TC 8.1.6.1.2.14 in TS 38.523-1
Observation 1: For TC 8.1.6.1.2.14 in TS 38.523-1 V17.4.0 (2023-09), it is assumed once UEs are configured as per “T1”, IDC problems will be detected by the UEs.
Actually, for UEs with good IDC mechanism and solutions, no IDC problems might be detected by the UEs. Hence, UEs may NOT suspend measurement logging or tag MDT report with inDeviceCoexDetected-r17 flag as expected. And these conformance UEs will fail TC 8.1.6.1.2.14.
TS 38.523-1 V17.4.0 (2023-09)
Proposal 1: To revise TC 8.1.6.1.2.14 in TS 38.523-1 V17.4.0 (2023-09) to exclude the DUT w/o IDC problems from failure.

## Slide 3: How IDC problems happened?
Observation 2: In cl. 23.4, it says “IDC problem can happen when the UE (intends to) uses WLAN on the overlapped carrier/band or adjacent carrier/band to the unlicensed carrier used for LAA operation, e.g. when related UE hardware components, such as antennas, are shared between LAA and WLAN operations”.
TS 36.300 cl. 23.4

## Slide 4: How to exclude DUT w/o IDC problems from failure? (1/3)
Proposal 2.1: To further test and check(St. 23-24) Reference Sensitivity of NR Cell with the same time instances configurations. The DUT w/o IDC problems will still “PASS” the test even if the measurement logging was not suspended or MDT report was not tagged with inDeviceCoexDetected-r17 flag. Further steps (St. 23-24) will be saved for the DUT with “P” Verdict in Step 22.
TS 38.523-1

## Slide 5: How to exclude DUT w/o IDC problems from failure? (2/3)
Proposal 2.2: To test (St. 3aa, 4aa)and further check(St. 23) Reference Sensitivity of NR Cell with the same time instances configurations. The DUT w/o IDC problems will still “PASS” the test even if the measurement logging was not suspended or MDT report was not tagged with inDeviceCoexDetected-r17 flag. Further step (St. 23) will be saved for the DUT with “P” Verdict in Step 22.
TS 38.523-1

## Slide 6: How to exclude DUT w/o IDC problems from failure? (3/3)
Proposal 2.3: Before the IDC mechanism test procedure, confirm whether the UE detected IDC problem. Only the UE detected IDC problems is applicable to this test case.
TS 38.523-1
Observation 3:
For Prop 2.1 , only the DUTs w/o “P” Verdict in Step 22 need to test NR Reference Sensitivity and confirm IDC problem being detected.
For Prop 2.2 and Prop 2.3, all the DUTs need to test NR RefSense and confirm IDC problem being detected first.

## Slide 7: Thank you!