## Slide 1: Way Forward for R18 IoT NTN WI
China Mobile, MediaTek
3GPP TSG-RAN5 Meeting #101 R5-237674
Chicago, USA, Nov 13 – 17, 2023

## Slide 2: The scope for TS 36.521-4 (v18.0.0)
Observation 1: There is alredy clear and urgent industry commercialization deployment plan for NB-IoT NTN, but no clear deployment plan for eMTC NTN yet.
WF 1: TS 36.521-4 (v18.0.0) will mainly focus on NB-IoT NTN. Once there is clear industry commercialization deployment plan for eMTC NTN in the future, eMTC NTN could be well covered and polished in the future released versions for TS 36.521-4 .
Observation 2: As per RAN4 Reply-LS “on applicability of UE demodulation and CSI requirements for IoT-NTN UE” to RAN5 (R5-236039), according to RAN2 specification TS 36.306 Clause 4.3.38.1, the field “ntn-Connectivity-EPC-r17” indicates whether the UE supports NTN access, and is only applicable if the UE supports ce-ModeA-r13 or any ue-Category-NB. As per R4 Reply-LS (R5-236039), there are no Category M1 NTN UEs only supporting NTN access.
WF 2.1: There are no eMTC IoT NTN UEs NOT supporting TN access defined in 3GPP specs so far unless otherwise stated in the future released 3GPP specs.
WF 2.2: For the IoT NTN UEs,
  for the NTN access testing, the test cases in TS 36.521-4 (v18.0.0) apply to both NGSO and GSO(with inclination different from zero)/GEO UEs.
  for the TN access testing, TS 36.521-1 is still applied.

## Slide 3: AT commands or preconfigured means adoption
Observation 3: As endorsed in Way forward RP-232682, “Further discuss TE-emulated channel model with delay and Doppler shifts matching the satellite propagator model in future release i.e. Rel-19”.
WF 3.1: For the RF/RRM/Demod test cases in TS 36.521-4 (v18.y.z) and TS 36.521-3(v18.y.z), AT commands or other preconfigured means are adopted to fix the constant zero/non-zero doppler and constant non-zero delay issues.
WF 3.2: For the furture release IoT NTN UEs (i.e. Rel-19), AT commands or any other preconfigured means shall be considered to be terminated and replaced with TE-emulated channel model method once TE-emulated channel model with dealy and Doppler shifts matching the satellite propagator model is available.

## Slide 4: Thank you!