## Slide 1: Discussion on handling of MDT IDC problem
China Mobile
3GPP TSG-RAN5 Meeting #102 R5-240096r1
Athens, Greece, Feb 27th - Mar 3rd, 2023

## Slide 2: UEs with good IDC mechanism may fail TC 8.1.6.1.2.14
Observation 1: For TC 8.1.6.1.2.14, it is assumed once UEs are configured as “T1”, IDC problem will be detected by the UEs.
Actually, for UEs with good IDC mechanism and solutions, no IDC problems might be detected by the UEs. Hence, UEs may NOT suspend measurement logging or tag MDT report with inDeviceCoexDetected-r17 flag as expected. And these UEs will FAIL TC 8.1.6.1.2.14.
TS 38.523-1 V17.5.0 (2023-12)
Proposal 1: Before testing the IDC mechanism, to confirm UE will detect IDC problem with “T1”configuration.
Notes: Before testing the IDC mechanism, to confirm UE will NOT detect IDC problem with“T0/T2”configuration, also to confirm UE will detect IDC problem with “T1”configuration.

## Slide 3: UEs with “T0/T2” configuration may still detect IDC problem
Observation 2: For TC 8.1.6.1.2.14, it is assumed once UEs are configured as “T0/T2”, IDC problem will NOT be detected by the UEs.
Actually, UEs with “T0/T2” configuration may still detect IDC problems. Hence, UEs may NOT resume logging as expected. And these UEs will FAIL TP2 of TC 8.1.6.1.2.14.
TS 38.523-1 V17.5.0 (2023-12)
Proposal 2: Before testing the IDC mechanism, to confirm UE will NOT detect IDC problem with “T0/T2”configuration.
Notes: Before testing the IDC mechanism, to confirm UE will NOT detect IDC problem with“T0/T2”configuration, also to confirm UE will detect IDC problem with “T1”configuration.

## Slide 4: How IDC problems happened?
Observation 3: In cl. 23.4, it says “IDC problem can happen when the UE (intends to) uses WLAN on the overlapped carrier/band or adjacent carrier/band to the unlicensed carrier used for LAA operation, e.g. when related UE hardware components, such as antennas, are shared between LAA and WLAN operations”.
TS 36.300 cl. 23.4

## Slide 5: How UE informs IDC problems?
Observation 4: As per cl.5.7.4.2 in TS 38.331, UE detecting IDC problem will providing IDC assistance information in RRC_CONNECTED if the UE was configured to do so.
TS 38.331 cl. 5.7.4

## Slide 6: How to confirm UE detects IDC problems?
Observation 5: If UEAssistanceInformation message including IDC-Assistance-r16 is received by NW/SS, it is confirmed that UE can detect IDC problem.
TS 38.331

## Slide 7: How to make DUT (NOT) detect IDC problem?
Proposal 4: When checking whether UE will resume logging when IDC problem is resolved, if UE does NOT detect IDC problem in RRC_CONNECTED with some configuration, to configure the IDLE UE with the same configuration as in RRC_CONNECTED to make the UE NOT detect IDC problem in RRC_IDLE.
Proposal 3: When checking whether UE will suspends measurement logging when IDC problem is detected, if UE detects IDC problem in RRC_CONNECTED with some configuration, to configure the IDLE UE with the same configuration as in RRC_CONNECTED to make the UE detect IDC problem in RRC_IDLE.
For details of “Main behaviour”, see related CR R5-240095r1

## Slide 8: Thank you!