## Slide 1: Progress and Way Forward on SW Implementation on Machine Readable PICS and Applicability
Qualcomm
3GPP TSG-RAN5 Meeting #103
Fukuoka City, Fukuoka, Japan, 20th May 2024 – 24th May 2024
R5-242560

## Slide 2
Updates, Agenda for Discussion
Recap: Industry Value and Progress
Update - Machine-Readable PICS File from TS 38.508-2
  Formatting issues in current specs
  Procedural Proposals and overall W/F
Further Proposals on PICS processing
  Allow DUT Declaration i.e allow user to enter PICS value
  Data Processing of DUT Declaration (for ex - in a separate tab)
  Meaningful association of extracted data to be used for outside automation

## Slide 3: Background – Overall Industry value
Progress Updates:
Based on proposal in R5-233200 and outcome in RAN5#99, a separate exploder has been created - 3GPP_TSG_RAN_WG5_APPLICABILITY
Green items above now have Prototype SW Implementation as demonstrated in RAN5#100 - R5-234320
As per outcome of R5-237464 in RAN5#101, it was agreed to explore providing the solution in steps, with initial focus on releasing machine readable PICS
As per Outcome of R5-240664 in RAN5#102, Qualcomm helped generate the draft Machine-Readable PICS
3GPP RAN5 Defined Tests
Extracted OEM PICS Compliance
TS 38.508-2
TS 38.523-2
Protocol
TS 38.522
RF+Perf (RRM, Demod)
OEM Augments Band, CA and other Information
TS 34.229-2
IMS (5G, 4G)
Output = No. of Applicable Tests per Device Capability
(All Automated in RAN5)
Execution Rules (Cert Industry Logic)
Final List of Test Cases

## Slide 4: Tool Generated Machine Readable PICS File
Shared with Applicability Reflector
Tool generated Column B for easier condition evaluation for both Tool and Human user a well as enable further automation
Column C and onward columns exactly follow the TS 38.508-2 format

## Slide 5: Spec Formatting Issues: Solutions (38.508-2 and 38.523-2)
Merged header rows are replaced with single row.
For 38.523-2 Merged header rows are replaced with single row for section 9 and subsequent sections, like it is already there in spec for section 6,7,8 tables.
Replaced multiple table object table with a single object table in 38.508-2
For 38.523-2 Section 8 table replaced with a new table due to ill-formatted rows
Replaced merged rows
Replaced Table

## Slide 6
Further Proposal#1. Allow DUT input i.e enter the value of PICS and Other Tables
User input format: Key-Value mapping of PICS
Basic Excel translation of TS 38.508-2
(Completed)
Read the DOCX file specified or latest version
  Extract all tables from above DOCX contents
  Read Tables and Rows
Key\Value Mapping of Table\Items no. to PICS
Generate user input File\Template From extracted PICS >Input to B.
User Input template
User filled in based on
DUT Support
User input can be of following forms for PICS or Data:
  True/False
    E.g.: pc_downlinkSPS
    Some of these are independent, some of these are dependent.
      E.g.: pc_recommendedBitRateQuery
  Enumeration
    E.g. pc_APN_Default_Configuration
  Char String:
    E.g.:pc_APN_ID_Internet;
    Non PICS - Bandwidth or Bandwidth, Bandwidth Class etc

## Slide 7
    Example Use Case:
    This Can be used for test case selection
Ex- Gives the list of test cases that can be executed and can be used as an input to external automation i.e derive conditions
Further Proposal #2,3. Extract DUT Supported PICS (Mnemonic ) and associated selection parameter
Using this information,
the test case selection expression
can be evaluated and
hence the list of TCs applicable for a DUT
Applicable TCs for a given DUT

## Slide 8
W/F Updates
SW Tool will not be shared publicly-
  Development and Maintenance for Output A
    Alt.1: Qualcomm
      Provide the python code to ETSI for use.
        RAN5#103 Update: The python code is shared with ETSI
    Alt.2: 3GPP/ETSI – Needs further discussion within ETSI - Ongoing
      MCC (Ingo’s team), or
      Some SW-capable team within ETSI (e.g. TNM ‘Tools & Methods’), or
      TF160
        TF160 ToR & budgeting would need to be discussed for this option.
  Qualcomm to generate first version with own SW, during spec released post RAN5#102, while Alt2 is investigated – Qualcomm already generated the first version and shared to the applicability reflector
Release Process
  At the same time as the new version of TS 38.508-2 is created. Once the clean of the new version of TS 38.508-2 is ready, RAN5 TO, MCC can run the tool against TS 38.508-2 to produce the machine readable PICS file except for the first time.
Storage of “Machine Readable PICS” or excel file
  Alt.1: Within the zip file of TS 38.508-2
  Alt.2: On 3GPP Forge: https://forge.3gpp.org/
    We would need to create a RAN5 area.
    A link to the 3GPP Forge area could be added within a new Annex of TS 38.508-2.
  Both Alt.1 + Alt.2.
Formatting Issues for Spec
  Tdoc contributed for corrections during RAN5#103
Notes: MH: Check previous contributions regarding challenges

## Slide 9
Proposals and Updates
RAN5 to endorse creation of “machine readable PICS” during every spec release of TS 38.508-2
  Draft version already shared with the applicability reflector for the latest version
Further enhancement of Machine-Readable PICS
  [In progress, Can be delivered Pre RAN5#104] Allow DUT Declaration i.e allow user to enter PICS value
  [In Progress]Data Processing of above(ex - in a separate tab of excel) will be required
3. Providing all above as an output will be most valuable to ecosystem as Step-1, this will allow to
  Fill DUT PICS compliance in standard format
  Help further automation to derive test case applicability

## Slide 10
References:-
RAN5#99
    R5-233200 SW Implementation of RAN5 Applicability
  RAN5#100
  R5-234320 Progress on Proposal-1 : SW Implementation of NR Applicability Specs
RAN5#101
  R5-237464 - Discussion – Software Implementation of NR Applicability Specifications -SIG - Conclusions and Next Steps
  R5-237465 - Discussion – Software Implementation of NR Applicability Specifications - RF Updates, Conclusions and Next Steps
RAN5#102
  R5-240664 - Way Forward on SW Implementation on Machine Readable PICS and Applicability