## Slide 1: Discussion on handling of PRD21 and PRD20
China Mobile, ZTE, Bureau Veritas, Huawei, Hisilicon
3GPP TSG-RAN5 Meeting #103 R5-243069
Fukuoka, Japan, May 20 - 24, 2024

## Slide 2: Only NR bands and 5G NR CADC configurations should be covered by PRD21
Observation 1.1: Only NR bands and 5G NR CADC configurations should be covered by PRD21.

## Slide 3: NR NTN satellite operating bands are defined in NR NTN spec TS 38.101-5
Observation 1.2: NR NTN satellite operating bands should be covered by PRD21.
TS 38.101-5

## Slide 4: IoT-NTN operating bands are defined in E-UTRA spec TS 36.102
Observation 1.3: IoT-NTN satellite operating bands should NOT be covered by PRD21.
TS 36.102

## Slide 5: Where to trace IoT-NTN bands?
Proposal 1: PRD20 to revise the title into “E-UTRA bands and CA configuration handling”, and to trace IoT-NTN bands in PRD20 (word file and excel file). All the IoT-NTN related parts to be removed from PRD21 (word file and excel file) into PRD20. IoT-NTN bands will be handled in an individual sheet in PRD20 excel.

## Slide 6: How to trace IoT-NTN bands in PRD20?
Observation 2: Compared with PRD21, PRD20 has no Columm “Interested deployer” yet.
Proposal 2: Similar as PRD21 excel, to add Column “interested deployer” in PRD20 excel also. Only when there is industry need, the corresponding E-UTRA bands/CA configuration can be tagged as “Ongoing” and related contributions are acceptable in RAN5.

## Slide 7: How to trace NR NTN bands in PRD21?
Proposal 3: NR NTN bands to be handled in an individual sheet in PRD21 excel.

## Slide 8: 3Tx inter-band CA/DC configs are defined in TS 38.101-1 and 38.101-3
Some CA/DC configs which have 3Tx capability, however, are already marked as “completed” status in PRD21 excel. Taking CA_n5A-n77A as an example: CA_n5A-n77A with UL -/CA_n5A-n77A have been completed in PRD21, thus the current status of CA_n5A-n77A in PRD21 excel is not suitable for trace CA_n5A-n77A 3Tx configuration.
Observation 3.1: 3Tx inter-band CA/DC configuration information is not captured in the current PRD21 excel.
Observation 3.2: PRD21 excel needs to be updated to trace the status of 3Tx inter-band CA/DC configs.
TS 38.101-1
TS 38.101-3
PRD21 excel v1.8.0

## Slide 9: How to trace 3Tx inter-band CA/DC configs in PRD21?
PRD21 excel v1.8.0
Proposal 4: It is proposed to add new rows in PRD21 excel to trace 3Tx inter-band CA/DC configs.

## Slide 10: Thank you!