## Slide 1: Discussion on handling of RAN5 AI
China Mobile, CAICT, MediaTek, ZTE, Telecom Italia, Huawei, AT&T,
China Telecom
3GPP TSG-RAN5 Meeting #104 R5-244507r2
Maastricht, Netherlands, August 19 – 23, 2024

## Slide 2: Background Information
Proposal 1: RAN5 leadership to coordinate meeting TimeTables to enable RAN5 delegates with an interest in AI/ML to participate in RAN4 AI/ML discussions.
Observation 1.1: As per the approved R19 WID “NR_AIML_Air” RP-240774 [1] for the “Testability and interoperability” topic, RAN5 aspects related to testability and interoperability to be addressed on a request basis.
Observation 1.2: AIML has totally new requirements for RAN5. RAN5 needs to keep abreast of the AIML WI progress in RAN4 and do early contributions when necessary.
RP-240774

## Slide 3: “General Issues” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “General issues” for RAN4 AIML topic is as below.
R4-2410570
Issue 1-1: Post deployment testing
Interested companies are invited to bring analysis on the feasibility of the options proposed so far.
Issue 1-4: Inference latency handling
Agreement:
Use the following as the starting point
n Inference latency can be implicitly captured in the delay of corresponding procedures (e.g. reporting delay) and/or performance requirements.
n Inference latency is part of delay of the corresponding procedure and no separate requirement will be specified for inference latency.
Check the above bullets based on per use case, and if other WGs define the inference latency, RAN4 can revisit the above bullets.
Observation 2: Being quite different from the traditional UEs, considering AIML models will be constantly updated after the devices are officially announced, AIML UEs will need a brand new conformance testing/certification methodology. RAN5 has rich experiences in UE conformance testing/certification, which will probably be very helpful to devise a new scheme to test/certify AIML models before and/or after the AIML devices hit the market.

## Slide 4: “General Issues” for RAN4 AIML topics that may impact RAN5 (2/2)
Proposal 2: RAN5 should consider to join RAN4 discussion on Issue 1-1.
Issue 1-5: LCM Requirements
Agreement:
n RAN4 considers defining RRM requirements for LCM procedures based on the specific use cases (beam management and positioning), and candidates are:
· identification
· selection
· activation
· deactivation
· switching
· fallback to non-AI operation
· performance monitoring
· Others are not precluded
Issue 1-6: Legacy RRM requirements handling
Agreement:
UE shall meet all legacy RRM requirements (non-AI/ML) even during the AI/ML operation mode.
R4-2410570

## Slide 5: “Testability and interoperability issues for beam management” for RAN4 AIML topics that might impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for beam management” for RAN4 AIML topic is as below.
Issue 2-3: Reported measurements and ground truth
Agreement:
n The ground truth for the predicted RSRP is the ideal measurement of RSRP on the predicted Tx beam
n In RAN4, the ground truth is the approximate as the reported RSRP measurement under the certain SNR on the predicted Tx beam
u FFS on SNR level to ensure that SNR is high enough for sufficient accuracy of reported RSRP
u FFS on impact of multiple-AoA test setup
u FFS on the channel condition
u FFS on whether the ground truth will be changing or not
Other solutions are not precluded
R4-2410570
Observation 3.1: It deserves RAN5’s early attention on the following items to avoid potential testability issues, including
  SNR power level is high enough
  impact of multiple-AoA test setup
  the channel condition
  whether the ground truth will be changing

## Slide 6: “Testability and interoperability issues for beam management” for RAN4 AIML topics that might impact RAN5 (2/2)
Issue 2-5: Test setup needs
Agreement:
maximum number of set B Tx beams that test system should be able to emulate: [8-16]
maximum number of set A Tx beams that test system should be able to emulate: [64-128]
FFS on AoAs
UE rotation during the test: FFS
UE rotation/repositioning between different tests: Yes
Issue 2-6: Datasets for training/testing
Agreement:
l Vendors may take into account the test environment/conditions defined by RAN4 when training the UE
Ø sufficient test environment/conditions should be defined to enable vendors to create the data needed for training
l FFS on proposals to augment training data to avoid overfitting of UE models to the test environment
l RAN4 to strive to make the test conditions similar to field deployment conditions
Proposal 3: RAN5 should consider to join RAN4 discussions on Issue 2-3, 2-5 and 2-6.
R4-2410570
Observation 3.2: It deserves RAN5’s early attention on the following items to avoid potential testability issues, including how to implement AoAs during the test, whether/how to implement UE rotation during the test, how similar we can make the test conditions to field deployment conditions.

## Slide 7: “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topic is as below.
Issue 3-2: Requirements for case 2a
Agreement:
No requirements on LMF for positioning accuracy
FFS on RAN4 requirements for any UE reported measurements defined by other groups
Issue 3-3: Requirements for case 2b
Agreement:
No requirements on LMF for positioning accuracy
FFS on RAN4 requirements for any UE reported measurements defined by other groups
Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning
R4-2410570
Notes: Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 8: “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topics that may impact RAN5 (2/2)
Proposal 4: RAN5 does NOT need to directly participate in RAN4 discussions on Issue 3-2 or 3-3, and only monitor progress and conclusions.
Observation 4: There seems to be no test plans/needs on the table for positioning accuracy enhancements at the moment.
Notes: Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 9: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topic is as below.
Issue 4-1: Reference encoder/decoder
Agreement:
Reference encoder:
The reference encoder is used in RAN4 discussions at least for simulation alignment/requirement derivation, test decoder derivation and/or test decoder verification. It could be documented (in TR, WF, etc) or captured in the specifications as necessary.
Reference decoder:
The reference decoder is used in RAN4 discussions at least for simulation alignment/requirement derivation and/or verification of the decoder implemented by the TE. It could be documented (in TR, WF, etc) or captured in the specifications as necessary.
For Option 3, for each test, a test decoder needs to be captured in the specs, a reference encoder might be needed to derive the test decoder and/or requirements and/or to validate the test decoder implementation in the TE. The same decoder might be used in multiple tests or each test could have a difference decoder.
In Option 3 the Reference decoder is the test decoder.
For Option 4, there might be a need to have reference encoder and/or reference decoder.
R4-2410570
Notes: Option3：To define specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.
Option 4：Only some guidance on how to implement the encoder/decoder models for testing, without any specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.

## Slide 10: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5 (2/2)
Observation 5: RAN5 needs to consider how to apply the encoder and decoder in the conformance testing. Inputs from TF160 might also be needed to make sure the conformance among the different encoders/decoders implemented by different TE vendors.
Proposal 5: RAN5 should consider to join RAN4 discussion on Issue 4-1.
Option1: DUT provides the decoder;
Option2: Infra vendor provides the decoder[3]
Option3: Full decoder specification in standard. Option 3 target is that a single decoder defined in the specifications for at least a single test for any DUTs.[3]
Option4: TE vendor provides the decoder. Option 4 target is that a single decoder implemented by each TE vendor will be enough for at least a single test for any DUTs. TE vendor should be able to implement the test decoder for Option 4 without any involvement from another party.[3]
Notes: Option3：To define specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.
Option 4：Only some guidance on how to implement the encoder/decoder models for testing, without any specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.

## Slide 11: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5
Observation 6.1: As per [2], agreements about the parameters used in the simulations for checking the feasibility of testing options for CSI compression and prediction is as below.
Agreement:
Parameters agreed are just for the feasibility study of testing options.
If/when RAN4 discusses requirement definition, RAN4 will define a new test decoder which may or may not reuse any of the parameters agreed in the feasibility study.
Proposal 6: RAN5 does NOT need to directly participate in RAN4 discussions on “Test decoder derivation procedure” and only monitor progress and conclusions.
Observation 6.2: As per [2], agreements regarding the process for checking the feasibility of deriving a test decoder for Option 3 is as below.
Test decoder derivation procedure:
Option 1
companies bring encoder + decoder set based on agreed parameters. RAN4 chooses one of the decoders and interested companies further check if an encoder can be trained with this decoder to obtain similar performance/complexity (or other evaluation criteria)
Option 2
companies bring training data for encoder + decoder pair, interested companies train an encoder + decoder pair based on the aggregated dataset from all companies to check decoder derivation feasibility and performance/complexity (or other evaluation criteria)
RAN4 agrees to work on Option 1.
Interested companies are invited to bring further feasibility analysis for Option 2
R4-2410570
R4-2410570

## Slide 12: RAN2 AIML discussions on “Functionality based LCM for NW-sided model” that may impact RAN5 (1/3)
Proposal 7: For RAN2 AIML “NW-sided model” discussions for “General”, RAN5 should pay close attention to the discussion progress and conclusions on data collection procedure from UE to NW for the sake of NW-sided model LCM.
Observation 7: Agreements for “General” from RAN2#125bis@2024.04
1 RAN2 confirms that UE will not be informed about any gNB/LMF-sided model/functionality management decision (e.g., selection, (de)activation, switching, fallback, etc.) 2 RAN2 confirms that UE will not be involved in any gNB/LMF-sided model/functionality management decision making (e.g., selection, (de)activation, switching, fallback, etc.), except being configured to provide the required measurement/data. 3 RAN2 focuses on the data collection procedure from UE to NW (e.g., gNB, LMF, or OAM) for the sake of NW-sided model LCM (including training, inference, management).
R2-2404102
newly added in r1

## Slide 13: RAN2 AIML discussions on “Functionality based LCM for NW-sided model” that may impact RAN5 (2/3)
Proposal 8: For RAN2 AIML “NW-sided model” discussions for “Positioning”, RAN5 to monitor progress and conclusions which have impacts on call flows if any in the future.
Observation 8.1: Agreements for “Positioning” from RAN2#125bis@2024.04
1 RAN2 to consider an RRC configuration to configure radio measurements and the related reporting to enable data collection for NW-side training
2 For AI/ML based beam management, RAN2 assumes the L1 measurement framework shall be used for configuring the input data of the NW side AI/ML model inference. FFS if further enhancements are needed
3 There is no specification impact associated to gNB-side model inference, depending on further RAN1 input.
4 FFS whether there is specification impact associated to gNB-side model monitoring.
5 For POS, RAN2 assumes gNB or LMF could perform performance monitoring for case 3a and LMF is responsible for the performance monitoring for case 3b and wait for any further inputs from other WGs
6 For POS, RAN2 assumes that NRPPa is used for the signalling between gNB and LMF for case 3a and 3b and the detailed signalling design is up to RAN3.
Observation 8.2: Agreements for “Positioning” from RAN2#126@2024.05
1 RAN2 to await RAN1 progress to determine need for any specification work on AI/ML positioning Case 3a and Case 3b.
R2-2404102
R2-2406202
newly added in r1

## Slide 14: RAN2 AIML discussions on “Functionality based LCM for NW-sided model” that may impact RAN5 (3/3)
Proposal 9: For RAN2 AIML “NW-sided model” discussions for “BM”, RAN5 to monitor progress and conclusions which have impacts on call flows if any in the future.
Observation 9: Agreements for “Beam Management” from RAN2#126@2024.05
1 For the network-side model, required network side additional condition is left up to the network implementation
2 RAN2 will wait for RAN1 for any required UE side additional conditions.
3 For network-sided model for BM use case, RAN2 confirms that UE inputs for inference at network-sided model will rely on L1 signaling, RAN2 will not further spend time on this aspect.
4 The gNB is responsible for monitoring its own performance. RAN2 will work on RAN2 specifications enhancements associated to gNB-side model monitoring, only based on RAN1 inputs, if any
R2-2406202
newly added in r1

## Slide 15: RAN2 AIML discussions on “Functionality based LCM for UE-sided model” that may impact RAN5 (1/5)
Proposal 10: For RAN2 AIML UE-sided model “Functionality granularity and capability” discussions, RAN5 should pay close attention to the AI/ML related UE capability definition for the supported AI/ML-enabled Features/FGs and supported functionalities.
Observation 10: Agreements for “Functionality granularity and capability” from RAN2#125bis@2024.04
1. Which AI/ML-enabled Features/FGs and functionalities are supported should be standardized. The details wait for RAN1’s progress. “supported” means that the UE is capable of supporting the functionality and doesn’t mean neccesarily that the UE has the model available. FFS what functionality refers to.
2. Supported AI/ML-enabled Features/FGs and supported functionalities are included in UE capability
R2-2404102
newly added in r1

## Slide 16: RAN2 AIML discussions on “Functionality based LCM for UE-sided model” that may impact RAN5 (2/5)
Observation 11.1: Agreements on “Applicability/additional conditions” for positioning and beam management from RAN2#125bis@2024.04
1 Support proactive reporting of UE-sided applicable functionality, e.g., the UE reports its applicable AI/ML functionalities via UAI message/LPP message.
2 Support reactive reporting of UE-sided applicable functionality. The NW configures AI/ML functionalities via RRC/LPP message. FFS what the configuration contains. FFS how to report applicable functionality and what is applicable functionality
3 FFS how the two approaches will be specified and whether we can combine them into one procedure. FFS how to report applicable functionality, what is applicable functionality, how the UE determines which function is applicable or not (if it is needed)
R2-2404102
Proposal 11.1: For RAN2 AIML UE-sided model “Applicability/additional conditions” discussions for positioning and beam management, RAN5 should pay close attention to the impacts on call flows from “proactive reporting of UE-sided applicable functionality”, “reactive reporting of UE-sided applicable functionality” and “NW configures AI/ML functionalities via RRC/LPP message”.
newly added in r1

## Slide 17: RAN2 AIML discussions on “Functionality based LCM for UE-sided model” that may impact RAN5 (3/5)
Observation 11.2: Agreements on “Applicability/additional conditions” for beam management from RAN2#126@2024.05
1 RAN2 will support functionality activation/deactivation after inference configuration. FFS initial state of configuration and how activation/deactivation is achieved. FFS what Deactivation refers to: examples discussed: 1) fallback to legacy 2) switching, etc.
2 We will work offline on the definitions for functionality types and define what is availability.
3 The UE will indicate the gNB/LMF whether the AI/ML functionality is available/applicable. For a functionality to be applicable at least there should at least one model available within it. FFS other details on what is applicability/non-applicability.
4 For NW-side additional conditions, RAN2 assumes that RRC signaling from gNB to UE can be designed for consistency between inference and training. RAN2 will wait for RAN1 input for further details. FFS if the same applies to positioning.
5 For BM use case, as a baseline the UE determines whether a functionality is applicable. Existing UAI framework is used at least for proactive reporting of applicable functionality. FFS reactive
R2-2406202
Proposal 11.2: For RAN2 AIML UE-sided model “Applicability/additional conditions” discussions for BM, RAN5 should pay close attention to the impacts on call flows from “functionality activation/deactivation”, “the indication on whether the AI/ML functionality is available/applicable” and “Existing UAI framework to be used for proactive reporting of applicable functionality”.
newly added in r1

## Slide 18: RAN2 AIML discussions on “Functionality based LCM for UE-sided model” that may impact RAN5 (4/5)
Proposal 11.3: For RAN2 AIML UE-sided model “Applicability/additional conditions” discussions for positioning, RAN5 should pay close attention to the impacts on call flows from “the indication on supported AI/ML positioning capabilities” and “Existing LPP procedures to be used for providing the results of the UE sided model inference operation”.
Observation 11.3: Agreements on “Applicability/additional conditions” for positioning from RAN2#126@2024.05
1 The LPP Capability Transfer procedures (RequestCapabilities/ProvideCapabilities messages) are used to indicate supported AI/ML positioning capabilities. FFS how to handle dynamic capabilities, depending on further RAN1 progress and understanding of the functionality.
2 wait for RAN1 for associate ID discussion
At least for Case 1, existing LPP procedures related to Location Information Transfer (RequestLocationInformation/ ProvideLocationInformation messages) are used for providing the results of the UE sided model inference operation. FFS further details on signaling enhancements
R2-2406202
newly added in r1

## Slide 19: RAN2 AIML discussions on “Functionality based LCM for UE-sided model” that may impact RAN5 (5/5)
Proposal 12: For RAN2 AIML UE-sided model “Common LCM framework/signalling” discussions, RAN5 should pay close attention to the impacts on the call flows from “Common LCM framework/signalling” discussions.
Observation 12: Agreements on “Common LCM framework/signalling” from RAN2#125bis@2024.04
1 For UE-sided model, for the functionality management, the “network decision, network-initiated” AI/ML management is supported as a baseline. The following can be considered further “UE autonomous, decision reported to the network”, “Network decision, UE-initiated” (i.e. proactive approach).
2 “UE-autonomous, UE’s decision is not reported to the network” is not considered for Rel-19
R2-2404102
newly added in r1

## Slide 20: RAN2 AIML discussions on “NW side data collection” that may impact RAN5
Proposal 13: For RAN2 AIML “NW side data collection” for Beam Management discussions, RAN5 should pay close attention to the impacts to call flows from “the measurement framework applied to both gNB-centric data collection and OAM-centric data collection for NW-side data collection” and “the enhanced MDT for data collection framework for training”.
Observation 13: Agreements on “NW side data collection” for Beam Management from RAN2#125bis@2024.04
1 For the NW-side data collection related to beam management use cases, RAN2 to consider gNB-centric and OAM-centric approaches
2 We aim that the same measurement framework is applied to both gNB-centric data collection and OAM-centric data collection for NW-side data collection.
3 RAN2 supports enhancements to MDT for data collection framework for training. FSS Whether to enhance logged or immediate MDT
R2-2404102
newly added in r1

## Slide 21: RAN2 AIML discussions on “UE side data collection” that may impact RAN5
Proposal 14: Considering “UE side data collection” discussions are still in SI status in RAN2, RAN5 does not need to monitor progress or conclusions before Rel-19 RAN2 functional freeze@2025Q3.
Observation 14:
For UE sided data collection, it is still in Study Item status in RAN2 Release 19 discussion.
newly added in r1

## Slide 22: Reference
[1] RP-240774, Revised WID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface, 3GPP TSG RAN Meeting #103; Maastricht, NL, March 18-21, 2024.
[2] R4-2410570, WF on AI/ML, 3GPP TSG-RAN WG4 Meeting #111; Fukuoka city, Japan , May 20th – 24th, 2024
[3] TR 38.843, Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface
[4] R2-2404102, Report of 3GPP TSG RAN WG2 meeting #125bis, Changsha, China, 15 - 19 April, 2024
[5] R2-2406202, Report of 3GPP TSG RAN WG2 meeting #126, Fukuoka, Japan, 20 - 24 May, 2024
Notes: Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface

## Slide 23: Thank you!