## Slide 1: Discussion on simplifying RF testing among different features
Huawei, HiSilicon, ZTE Corporation
3GPP TSG-RAN5 Meeting #104 R5-244881r2
Maastricht, Netherlands, Aug 19-23, 2024

## Slide 2: Background
RAN4 SI: Study on simplification of band combination specification for NR and LTE (FS_SimBC, UID 950067, closed in RAN4#109)
TR 38.846 captured the RAN4 agreements on Test burden reduction for band combinations in clause 7. The general guidelines could be summarized as below:
RAN5#103: discussion paper R5-243305, prop1 is noted with comments below:
  This discussion paper is to:
    Provide more background and details for discussing test burden reductions
    Discuss the specific approach to implement test burden reduction in RAN5
Proposal 1 | Conlcusion/comments
RAN5 to consider if there is a need to develop a common test method for different features with the same frequency band combination. | prop1 needs more specific examples from ran5 spec and background for change
  Band combo specific RF requirements mainly include: MOP, Spurious emission for UE co-ex, general REFSENS and MSD
  RF implementations are similar and RF architectures can be reused for different features on the same band combination. i.e. CA_nA-nB (NR CA), DC_nA-nB (NR-DC), DC_A_nB (EN-DC), DC_B_nA (EN-DC), DC_nB_A (NE-DC), DC_nA_B (NE-DC) (different features on same band combination) can use same RF implementation
  The final decision whether to reduce testing burden should be taken by RAN5 based on the industry certification testing needs

## Slide 3: Test burden reduction for MOP – RAN4 guideline
MOP requirement for the same frequency range with different features
Part of table 7.2.1-1 in TR 38.346 :
  TR 38.346 cl.7.2.1: Taking PC3 MOP requirements for all the UL NR CA, UL NR DC, EN-DC and NE-DC band combinations in table 7.2.1-1 based on the TS 38.101-1-h60 and TS 38.101-3-h60 as an example. One band combination may be chosen to verify MOP testing for some band combinations in same row.
Uplink NR CA Configuration | Uplink NR DC Configuration | Uplink EN-DC Configuration | Uplink NE-DC Configuration | Class 3 (dBm) | Tolerance (dB)
CA_n1A-n3A | DC_n1A-n3A | DC_1A_n3A DC_3A_n1A DC_1A_n80A DC_3A_n84A | DC_n3A_1A | 23 | +2/-3
CA_n1A-n5A |  | DC_1A_n5A |  | 23 | +2/-3
CA_n1A-n7A | DC_n1A-n7A | DC_1A_n7A DC_7A_n1A |  | 23 | +2/-3
CA_n1A-n8A |  | DC_1A_n8A DC_8A_n1A | DC_n8A_1A | 23 | +2/-3
CA_n1A-n18A |  |  |  | 23 | +2/-3
CA_n1A-n20A |  | DC_1A_n20A DC_20A_n1A |  | 23 | +2/-3
CA_n1A-n28A | DC_n1A-n28A | DC_1A_n28A DC_28A_n1A | DC_n1A_28A | 23 | +2/-3

## Slide 4: Test burden reduction for MOP – RAN5 testing
MOP testing for same band combination among different features in RAN5:
  * MU/TT for the E-UTRA carrier and NR carrier are the same when the FC and CBW for E-UTRA carrier and NR carrier are same.
Observation 1:
  RAN4 guildline: different features on the same band combination have same MOP minimum requirements
  RAN5 testing aspects: except for the EN(NE)-DC configurations requiring singleUL-Transmission, MOP testing for same band combination among different features have same measurement procedure, requirements and MU/TT value.
Proposal 1: When UE supports different features on the same band combination, the measured MOP for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply when UE supporting singleUL-Transmission on certain EN-DC (NE-DC) configuration. This rule only apply to same power class for all involved configurations.
Features | NR CA | NR-DC | EN-DC | NE-DC
UL configuration type | CA_nXA-nYA | DC_nXA-nYA | DC_XA-nYA | DC_nXA-YA
Test case No. | 38.521-1 6.2A.1 | 38.521-1 6.2B.1 | 38.521-3 6.2B.1.3 | 38.521-3 6.2B.1.3a
Measured by | sum of mean transmitted power over all component carriers | sum of mean transmitted power over all component carriers | not supporting UE singleUL-Transmission: sum of mean transmitted power over all EN-DC component carriers supporting UE singleUL-Transmission: mean transmitted power over E-UTRA carrier or NR carrier | 
MU | MAX (MUCC1, MUCC2) | MAX (MUCC1, MUCC2) | MAX (MULTE, MUSA) | MAX (MULTE, MUSA)
TT | MAX (TTCC1, TTCC2) | MAX (TTCC1, TTCC2) | MAX (TTLTE, TTSA) | MAX (TTLTE, TTSA)

## Slide 5: Test burden reduction for Spurious UE co-ex – RAN4 guideline
Spurious emission UE co-existence requirement for the same frequency range with different features
Analysis of minimum requirements: The requirements are consist of…
Observation 2a:
  For a specific configuration, the protected frequency range (known as “additional requirements”) requirement is same across different releases
  Spurious UE co-ex requirements are same for the band combination among difference features , except EN-DC testing for R15 UE and NE-DC configurations without corresponding defined EN-DC.
  It’s better to ask RAN4 group to align the spurious UE co-existence requirements in Rel-15 with Rel-16 and onwards
  TR 38.346 cl.7.2.2: Generally, if CA_nA-nB, DC_A_nB, DC_B_nA, DC_nB_A, DC_nA_B have same spurious emission requirements for UE to UE coexistence, it may not be needed to test the spurious emission requirements for UE to UE coexistence for each UL configuration again and again. Once one of these UL configurations is verified, the other UL configurations for different feature in same band combination can be considered as being capable of meeting these requirements.
Uplink NR CA | Uplink NR DC | Uplink EN-DC | Uplink NE-DC
Intersection of requirements for the individual bands + additional protected frequency range |  | R15: defined protected band and protected frequency range | WITH corresponding defined EN-DC: same as EN-DC
 |  | R16-R18: Intersection of requirements for the individual bands + additional protected frequency range | WITHOUT corresponding defined EN-DC: defined protected band and protected frequency range

## Slide 6: Test burden reduction for Spurious UE co-ex – RAN5 testing
MOP testing for same band combination among different features in RAN5:
  * NSA only capable UE is not involved in this discussion
Observation 2b:
  RAN5 testing aspects: NE-DC spurious UE co-ex testing hasn’t been defined in RAN5. The testing results for NR CA testing applies for the same band combination of NR-DC
Proposal 2: When UE supports different features on the same band combination, the measured Spurious UE co-existence for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply to EN-DC testing for R15 UE.
Features | NR CA | NR-DC | EN-DC | NE-DC
UL configuration type | CA_nXA-nYA | DC_nXA-nYA | DC_XA-nYA | DC_nXA-YA
Test case No. | 6.5A.3.2.1 | 6.5B.3 | 6.5B.3.3.2 | 6.5B.3.3a.2
Measured by | Step by step measuring spurious emission as per the test requirement for both PCC and SCC; During measurement the spectrum analyser shall be set to 'Detector' = RMS. |  | Step by step measuring spurious emission as per the test requirement for both E-UTRA CC and NR CC; During measurement the spectrum analyser shall be set to 'Detector' = RMS. | FFS
MU | inter-band CA: same as 6.5.3.2 for each CC |  | Same as 6.5.3.2 in TS 38.521-1 | FFS
TT | 0 dB |  | 0 dB | FFS

## Slide 7: Test burden reduction for REFSENS – RAN4 guideline
Generally speaking, REFSENS requirement for a combination includes:
  general REFSENS without exceptions
  REFSENS exceptions due to 1) harmonic/harmonic mixing; 2) inter-modulation distortion; 3) cross band isolation interference
REFSENS without exception requirement for different features (inter-band):
However, the single-band REFSENS requirements are not exactly the same for E-UTRA and NR. For example:
  TR 38.346 cl.7.3.4: For band combinations DL_nA-nB_UL_nA-nB / DL_B_nA_UL_B_nA / DL_A_nB_UL_A_nB / DL_nB_A_UL_nB_A / DL_nA_B_UL_nA_B which doesn’t have any MSD requirements, it’s suggested to test one of them in order to reduce the test burden for REFSENS requirements and final decision is up to RAN5. The reason is that the same Rx RF implementation is used to achieve these band combinations.
NR CA | NR DC | EN-DC | NE-DC
Same as single-band requirements for each component carrier uplink is assigned to one NR |  | Same as single-band requirements for each E-UTRA carrier and NR carrier | NA: only REFSENS exception requirements defined
FDD E-UTRA | FDD NR | TDD E-UTRA | TDD NR
Band 3, 20MHz@15kHz: REFSENS = -91 | n3, 20MHz@15kHz: REFSENS = -90.8 | Band 41, 20MHz@15kHz: REFSENS = -92 | n41, 20MHz@15kHz: REFSENS = -91.7
Band 66, 10MHz@15kHz: REFSENS = -96.5 | Band 66, 10MHz@15kHz: REFSENS = -96.3 | Band 39, 10MHz@15kHz: REFSENS= -97 | n39, 10MHz@15kHz: REFSENS= -96.8

## Slide 8: Test burden reduction for REFSENS – RAN5 testing
And the testing in RAN5 for REFSENS without exception is extracted as below:
Observation 3a:
  The single-band REFSENS requirements for the same band in LTE and NR usually have 0.2dB difference, which might be acceptable since the MU and TT is larger than the difference
  In EN-DC test case, only the NR band will be measured due to LTE anchor agnostic approach. The testing result of EN-DC configuration cannot apply to the same CA configuration. Instead, the testing results of CA configuration could be applied to the same EN-DC configuration.
Features | NR CA | NR-DC | EN-DC | NE-DC
UL configuration type | CA_nXA-nYA | DC_nXA-nYA | DC_XA-nYA | DC_nXA-YA
Test case No. | 7.3A.1 | 7.3B.1 | 7.3B.2.3 | -
Measured by | Measure the average throughput for each component carrier |  | LTE anchor agnostic approach | -
MU | Same 7.3.2 for each component for each CC (0.7-1.5 dB) |  | Same 7.3.2 (38.521-1) for NR carrier (0.7-1.5 dB) | -
TT | Same 7.3.2 for each component for each CC (0.7-1.0 dB) |  | Same 7.3.2 (38.521-1) for NR carrier (0.7-1.0 dB) | -

## Slide 9: Test burden reduction for REFSENS – RAN4 guideline
As for the REFSEN exception requirements, there’s some slight difference for NR-CA and EN-DC for some of the same band combination. For example:
Observation 3b:
  Some band combinations have exactly the same MSD requirements between CA and EN-DC features.
  The other band combinations have different MSD requirements between different features. For these band combinations, they have to be tested individually.
NR CA
EN-DC

## Slide 10
Test burden reduction for REFSENS – RAN5 testing
In REFSENS with exception for CA test cases, the average throughput are measured on both the aggressor band and victim band. Both the aggressor band and victim band need to meet the test requirements.
In REFSENS with exception for EN-DC test cases, the average throughput are requested to be measured on both the aggressor band and victim band, but only test requirements for victim band are given in the Test Requirement tables (i.e. table 7.3B.2.3.5-1/-2/-3) except MSD due to dual uplink operation (i.e. table 7.3B.2.3.5-4)
Observation 3c:
  For same band combinations with exactly the same MSD requirements between CA and EN-DC features:
  The testing result of REFSENS exception due to 2UL CA for CA configuration is applicable to the REFSENS exception due to dual uplink operation for the same EN-DC configuration, and vice versa
  The testing result of REFSENS exception due to harmonic / harmonic mixing / cross band isolation for CA configuration is applicable to the corresponding REFSENS exception testing for the same EN-DC configuration, but not vice versa
Proposal 3:
  When UE supports different features on the same band combination:
  the REFSENS without exception testing results of CA configuration could be applied to the same EN-DC configuration
  If same MSD requirements are defined for CA and EN-DC configuration, the REFSENS with exception testing results of CA configuration could be applied to the same EN-DC configuration. The testing result of REFSENS exception due to dual uplink operation for EN-DC configuration is applicable to the REFSENS exception due to 2UL CA for the same CA configuration

## Slide 11: Summary of Proposals
Based on above analyses, proposals for simplification on RF testing among different features can be summarized as below:
Proposal 1:
  When UE supports different features on the same band combination, the measured MOP for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply when UE supporting singleUL-Transmission on certain EN-DC (NE-DC) configuration. This rule only apply to same power class for all involved configurations.
Proposal 2:
  When UE supports different features on the same band combination, the measured Spurious UE co-existence for for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply to EN-DC testing for R15 UE.
Proposal 3:
  When UE supports different features on the same band combination:
  the REFSENS without exception testing results of CA configuration could be applied to the same EN-DC configuration
  If same MSD requirements are defined for CA and EN-DC configuration, the REFSENS with exception testing results of CA configuration could be applied to the same EN-DC configuration. The testing result of REFSENS exception due to dual uplink operation for EN-DC configuration is applicable to the REFSENS exception due to 2UL CA for the same CA configuration
Proposal 4:
  Ask for RAN4 group to align the spurious UE co-existence requirements in Rel-15 with Rel-16 and onwards

## Slide 12: Thank you!