## Slide 1: Discussion on updating test requirement tables in REFSENS for CA test cases
Huawei, Hisilicon
3GPP TSG-RAN5 Meeting #105 R5-247010
Orlando, United States, Nov 18-22, 2024

## Slide 2: Background
In TS 38.521-1 test case 7.3A.1_1, the test requirements for each CA configuration are specified in terms of:
  NR band: both aggressor band and victim band in the configuration
  Number of Rx antenna ports: 2Rx requirements and 4Rx requirements for each band
During last several meetings A lot of efforts has been put into the maintenance of the test requirement tables in 7.3A.1_1. With the introduction of 8Rx antenna ports, the CA REFSEN test requirements will become more burdensome to maintain.

## Slide 3: Calculation of test requirements
Based on the description in 7.3A.1 in TS 38.101-1, the MSD value is increased for 4Rx or 8Rx antenna ports:
And the value of ΔRIB,4R and ΔRIB,8R for each band in TS 38.101 are pasted as below:

## Slide 4: Calculation of test requirements
The value of CA REFSENS test requirement for each band is calculated as below:
Observation:
For the victim band, the REFSENS test requirement is same value for UE with different Rx antenna ports
For the aggressor band, the REFSENS test requirement is same value as that of the single band
NR band of CA | Rx | Test requirement is… | comment
Victim band (with MSD applied) | 2R | REFSEN2R+ MSD | Same value across different numbers of Rx antenna ports
(MSD applied on this band) | 4R | REFSENS2R+ ΔRIB,4R + MSD +¦ΔRIB,4R ¦ =REFSEN2R+ MSD | 
 | 8R | REFSENS2R+ ΔRIB,8R + MSD +¦ΔRIB,8R ¦ =REFSEN2R+ MSD | 
Aggressor band (without MSD applied) | 2R | REFSEN2R | Same value as single carrier test requirement for each Rx antenna port
 | 4R | REFSENS2R+ ΔRIB,4R | 
 | 8R | REFSENS2R+ ΔRIB,8R | 

## Slide 5: Updates of test requirements
Proposal 1:
Update the format of CA REFSENS test requirement table 7.3A.1_1.5-1 and 7.3A.1_1.5-1a:
  For the bands without MSD applied (aggressor band): Using symbol “REFSENS” , which refers to the reference sensitivity values for single carrier specified in 7.3.2 for 2Rx / 4Rx / 8Rx, to replace specific values in test requirement tables.
  For the bands with MSD applied (victim band): Using symbol “REFSENS2Rx” + MSD value as the test requirements for UE with different Rx antenna ports.
Proposal 2:
Apply same changes in proposal 1 to table 7.3A.2_1.5-1 and 7.3A.2_1.5-1a for 3DL CA REFSENS testing.
For example:

## Slide 6: Summary
Observation:
For the victim band, the REFSENS test requirement is same value for UE with different Rx antenna ports
For the aggressor band, the REFSENS test requirement is same value as that of the single band
Proposal 1:
Update the format of CA REFSENS test requirement table 7.3A.1_1.5-1 and 7.3A.1_1.5-1a:
  For the bands without MSD applied (aggressor band): Using symbol “REFSEN” , which refers to the reference sensitivity values for single carrier specified in 7.3.2 for 2Rx / 4Rx / 8Rx, to replace specific values in test requirement tables.
  For the bands with MSD applied (victim band): Using symbol “REFSENS2Rx” + MSD value as the test requirements for UE with different Rx antenna ports.
Proposal 2:
To keep in alignment, apply same changes in proposal 1 to table 7.3A.2_1.5-1 and 7.3A.2_1.5-1a for REFSENS for 3DL CA exceptions testing.
* Proposal 1 is implemented in CR R5-247014, Proposal 2 is implemented in CR R5-247015.

## Slide 7: Thank You!