## Slide 1: Disc on handling power class info of FR2 TCs applicability
CMCC
3GPP TSG-RAN5 Meeting #106
Athens, Greece, February 17 – 21, 2025 R5-250141

## Slide 2
Some FR2 TCs applicability power class information are incorrect
Observation 1: Some FR2 TCs applicability in TS 38.522 are not aligned with the status in TS 38.521-2. The power class information for FR2 TCs in TS 38.522 are incorrect.
TS 38.521-2 i52
TS 38.522 i50

## Slide 3
Some FR2 TCs power class information in editor notes lack consistency
Observation 2: The completion status of different power class in TS 38.521-2 TCs editor notes lack consistency. Some editor notes shows which power classes are completed. But others shows which are incomplete.
TS 38.521-2 i52
TS 38.521-2 i51

## Slide 4
How to handle power class information misalignment of FR2 TCs in TS 38.522
Proposal 1: It is proposed to check all FR2 TCs status case by case, in order to give a clear view whether TCs are related to power classes and whether power classes have been completed or not. And then update TCs applicability in TS 38.522 accordingly.
Table 1 Power class completion status of TS 38.521-2 TCs
TC | Involved power classes | Completed | Incomplete
6.2.1.1 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
6.2.1.2 | PC1,2,3,4,5,7 | PC1,3,5,7 | PC2,4
6.2.1.1_1 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
6.2.1.2_1 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
6.2.2 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
6.2.2_1 | PC3 | PC3 | -
6.2.3 | PC1~PC7 | PC1,3,5,7 | PC2,4,6
6.2.4_1 | PC1~PC4 | PC3 | PC1,2,4
6.2.5 | PC1~PC7 | PC1,3 | PC2,4,5,6,7
6.2A.1.1.1~3 | PC1,2,3,4,5,7 | PC3 | PC1,2,4,5,7
6.2A.1.2.1~3 | PC1,2,3,4,7 | PC1,3 | PC2,4,7
6.2A.2.1~3 | PC1~PC4 | PC3 | PC1,2,4
6.2A.3.1~3 | PC1~PC5 | PC1,3,5 | PC2,4
6.2D.1.1~2 | PC1~PC6 | PC1,3,5 | PC2,4,6
6.2D.2 | PC1~PC7 | PC3,5 | PC1,2,4,6,7
6.2D.3 | PC1~PC4 | PC3 | PC1,2,4
6.3.1 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
6.3.2 | PC1,3,5,6 | PC1,3,5,6 | -
6.3.3.2 | PC1,2,3,4,6,7 | PC3 | PC1,2,4,6,7
6.3.3.4 | PC3 | - | PC3
6.3.4.2 | PC1,2,3,4,6,7 | PC3 | PC1,2,4,6,7
6.3.4.3 | PC3 | - | PC3
6.3.4.4 | PC1,2,3,4,6,7 | PC3 | PC1,2,4,6,7
6.3A.1.1~7 | PC1~PC4 | PC3 | PC1,2,4
6.3A.3.1.1~3 | PC1~PC7 | PC3 | PC1,2,4,5,6,7
6.3A.4.2.1~3 | PC1~PC5 | PC3 | PC1,2,4,5
6.3A.4.2.4~7 | PC1~PC4 | - | PC1,2,3,4
6.3A.4.4.1~3 | PC1~PC5 | PC3 | PC1,2,4,5
6.3A.4.4.4~7 | PC1~PC4 | - | PC1,2,3,4
TC | Involved power classes | Completed | Incomplete
6.3D.1 | PC1~PC6 | PC1,3,5 | PC2,4,6
6.3D.2 | PC1~PC6 | PC3 | PC1,2,4,5,6
6.3D.3.1 | PC1~PC4 | - | PC1,2,3,4
6.4.1 | PC3 | PC3 | -
6.4.2.1 | PC1,2,3,4,5,7 | PC1,3,5 | PC2,4,7
6.4.2.1_1 | PC1,2,3,4,5,7 | - | PC1,2,3,4,5,7
6.4.2.2 | PC1,2,3,4,6,7 | PC3,7 | PC1,2,4,6
6.4.2.3 | PC1,2,3,4,6,7 | - | PC1,2,3,4,6,7
6.4.2.4 | PC3 | - | PC3
6.4.2.5 | PC3 | - | PC3
6.4.2.6 | PC1,2,3,4,6,7 | - | PC1,2,3,4,6,7
6.4A.1.1~7 | PC3 | PC3 | -
6.4A.2.1.1~7 | PC1~PC4 | - | PC1,2,3,4
6.4A.2.2.1~7 | PC1~PC4 | - | PC1,2,3,4
6.4A.2.3.1~7 | PC1~PC4 | - | PC1,2,3,4
6.4D.1 | PC3 | PC3 | -
6.4D.3 | PC1~PC4 | - | PC1,2,3,4
6.5.1 | PC1~PC5 | PC1,3,5 | PC2,4
6.5.2.1 | PC1~PC6 | PC1,3,5,6 | PC2,4
6.5.2.1_1 | PC1~PC6 | PC1,3,5,6 | PC2,4
6.5.2.3 | PC1~PC6 | PC1,3,5,6 | PC2,4
6.5.3.1 | PC1~PC7 | PC1,3,5 | PC2,4,6,7
6.5.3.1_1 | PC1,2,3,4,6 | PC1,3 | PC2,4,6
6.5.3.2 | PC1~PC7 | PC1,3,5 | PC2,4,6,7
6.5.3.2_1 | PC1,2,3,4,6 | PC1,3 | PC2,4,6
6.5.3.3 | PC1~PC6 | PC1,3,5 | PC2,4,6
6.5.3.3_1 | PC1~PC6 | PC1,3,5 | PC2,4,6
6.5A.1.1~7 | PC1~PC4 | - | PC1,2,3,4
6.5A.2.1.1~3 | PC1~PC5 | PC1,3,5 | PC2,4
6.5A.2.1.4~7 | PC1~PC4 | - | PC1,2,3,4
6.5A.2.2.1~3 | PC1~PC5 | PC1,3,5 | PC2,4
6.5A.2.2.4~7 | PC1~PC4 | - | PC1,2,3,4

## Slide 5
Track the status of power class information for FR2 TCs in TS 38.521-2
Table 1 Continued
TC | Involved power classes | Completed | Incomplete
6.5A.3.1.1~7 | PC1~PC4 | PC3 | PC1,2,4
6.5A.3.2.1~7 | PC1~PC4 | PC3 | PC1,2,4
6.5A.3.3.1~3 | PC1 | PC1 | -
6.5A.3.3.4~7 | PC3 | - | PC3
6.5D.1 | PC1~PC5 | PC3 | PC1,2,4,5
6.5D.2.1 | PC1~PC4 | PC1,3 | PC2,4
6.5D.2.2 | PC1~PC4 | PC3 | PC1,2,4
6.5D.3.1 | PC1~PC5 | PC1,3 | PC2,4,5
6.5D.3.2 | PC1~PC5 | PC1,3 | PC2,4,5
6.5D.3.3 | PC1~PC4 | PC3 | PC1,2,4
6.6.1 | PC3,5,6,7 | PC3 | PC5,6,7
6.6.2 | PC3 | PC3 | -
7.3.2 | PC1~PC7 | PC1,3,5,6,7 | PC2,4
7.3A.2.1~3 | PC1~PC4 | PC3 | PC1,2,4
7.3A.2.4~7 | PC1~PC4 | - | PC1~PC4
7.3A.3.1~3 | PC3 | - | PC3
7.3.4 | PC1~PC7 | PC1,3,5,7 | PC2,4,6
7.4 | PC3 | - | PC3
7.4A.1~7 | PC3 | - | PC3
7.5 | PC1,3,5,6,7 | PC1,3,5,6 | PC7
7.6.2 | PC1,3,5,6,7 | PC1,3,5,6 | PC7
7.9 | PC1,3,5,7 | PC1,3,5 | PC7

## Slide 6
How to handle TCs applicability which only apply to a non PC3 power class
Observation 3: For TCs 6.5A.3.3.1 to 6.5A.3.3.3 in TS 38.521-2, only PC1 is applicable as per description in test applicability.
Observation 4: “Branch column” should only include the information that one test cases have different features support. Thus, PC1 was removed from the branch column for these three TCs in the last meeting.
Proposal 3.1: It is proposed to update applicability conditions and give a comment in the additional information column to address PC1 informaiton.
Proposal 3.2: It is proposed to add PC1 back in the Branch column for TCs 6.5A.3.3.1 to 6.5A.3.3.3.
TS 38.521-2 i52
Changes for Proposal 3.1
Changes for Proposal 3.2

## Slide 7: Thank you !