## Slide 1: Discussion on AIML Post-deployment Testing
CMCC, ZTE
3GPP TSG-RAN5 Meeting #106
Athens, Greece, February 17 – 21, 2025 R5-250157

## Slide 2
Background
Way forward from RAN5#105
Notes: AIML conformance test framework
UE lab conformance aspects of post-deployment testing

## Slide 3
Potential Solutions for Post-deployment Testing
Solution 1: For the Post-deployment testing of the updated AI/ML model, to use the performance of the verified/certified model (“Model_1”) in the Post-deployment testing as the “minimum requirements”. If the performance of the updated model (“Model_2”) is not worse than/similar to the performance of the verified/certified model (“Model_1”) in the Post-deployment testing, the updated model (“Model_2”) can be regarded as “PASS” or “applicable models” which is ready to be activated.
Solution 2: For the Post-deployment testing of the updated AI/ML model (“Model_2”), to use the same model input/ground truth as the ones used in Pre-Deployment Testing. Basing on the same model input/ground truth, to compare the performance of the updated model (“Model_2”) in the Post-deployment testing with the performance of the verified/certified model (“Model_1”) in the Post-deployment testing.
Pre-deployment testing
Post-deployment testing
Proposal 1: RAN5 to evaluate the feasibility of the Solution 1~2 above and take them into consideration when discussing post-deployment testing.

## Slide 4
Potential Applications of Test Mode
Solution 3: Besides to be used in Pre-deployment testing, test mode also can be used in Post-deployment Testing.
Solution 4: Besides to be used in UE lab conformance testing, test mode also can be considered in AI/ML model Post-deployment Field Testing. Once AI/ML UEs are in idle/inactive modes, test mode can be triggered to test/verify/certify the AI/ML models. When UE is in test mode, the AI/ML model performance can be tested/verified/certified by UE’s being connected to the testing server, and the users’ common communication services might be impacted.
Proposal 2: RAN5 to evaluate the feasibility of the Solution 3~4 above and take them into consideration when discussing AIML conformance test framework.
The performance of Model_1 to be used as the “minimum requirements”
Model_2 to be tested/verified/certified

## Slide 5: Thank you !