## Slide 1: Test frequency calculation tool
Implemented in Python
R5-250637
3GPP TSG-RAN5 Meeting #106
Athens, February 17 – 21 2025

## Slide 2: Supported Functionality of the Tool
Python tool
User input (GUI)
( Configuration, Band, SCS, UL/DL -> Table )
3GPP Tables
(38.101, 38.213, 38.508)
3GPP parameters, hard coded in python.
(38.101, 38.213, 38.508)
3GPP Tables, coded in python.
(38.101, 38.508)
Manual insertion
Input parameters in CSV format, as a reference.
Single Freq
TDD, FDD, FR1, FR2
Intra CA Contiguous
TDD, FR1, FR2
Intra CA Noncontiguous UL, TDD, FR1
More Types
DL
DL&UL
Possibly in JSON format, outside python.
More Types
Test frequencies and Coreset#0 in CSV format.
SSB and Coreset#0 Calculation

## Slide 3: Added configuration types since Ran5#105 meeting.
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, for UL testfrequencies (FDD Bands)

## Slide 4: Added 3GPP tables in JSON format.
38.101-1, table 5.3.5-1

## Slide 5: What configuration types does the tool support at this stage? (38.508-1, Annex C)
C.3: Determination of SSB and CORESET#0
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, (FR1, FR2, FDD, TDD).
C.2.4.2.2: Determination of test frequencies for Low-, Mid- and High-Range, for NR Intra-band Contiguous CA, FR1 and FR2, for 2 carriers only.
C.2.4.3: Determination of test frequencies for NR Intra-band Non-Contiguous CA , only FR1, only 2 carriers.
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.

## Slide 6: What is not supported in 38.508-1, at this stage?
Potentially all clauses above are possible to implement.
Further studies are required.
C.2.1.2: Determination test frequencies for Mid-Low and Mid-High-Range for signalling tests.
C.2.4.2A: Determination of test frequencies for FR1 NR Intra-band Contiguous CA without UL CA for bands with uplink bandwidth less than downlink bandwidth.
C.2.5: Frequency determination for supplemental uplink.
C.2.6: Frequency determination for EN-DC configurations.
C.4: Determination of SSB and CORESET#0 for RRM testing with SSB SCS 120 kHz and 240 kHz.

## Slide 7: Proposal 1
Make this python tool a part of the standard to support calculations of test frequencies that is not added in test frequency tables due to too many bandwidth combinations.
In addition, the tool can be used to generate data as input to CRs for new bands/CA combinations. This will still require updates of the tool for specific band/CA configurations.

## Slide 8: What is next?
Move hardcoded input outside Python code (in JSON format?) to make it possible to include bands/configurations without updating python code.
Represent input 3GPP Tables in JSON format (today, they are represented python).
Represent output in JSON (today the format is in .CSV).
Represent input tables from specs (38.101, 38.213, 38.508), that today are manually read, in JSON format. This will remove need for any hardcoded band/configuration specific parameters in the tool and will then possibly make the tool support any band/CA configuration, as long as the needed input is available in RAN4 specs. (Long term)